## Slide 1: Residue Quad Tree Depth for Chroma in Intra coding
Xin Zhao, Xun Guo, Xiang Li, Shawmin Lei, Siwei Ma and Wen Gao
MediaTek Inc.
Presented by Xiang Li
7th JCT-VC Meeting in Geneva
21-30 November, 2011
Notes: <number>

## Slide 2: Overall Summary
Independent RQT depth setting is proposed for chroma in intra coding.
The default setting of RQT depth in intra coding is 0
Experimental results
  Based on HM4.0 and test conditions of JCTVC-F900
  Average BD-rate reductions of -0.0%, -1.7% and -1.7% for HE-AI -0.2%, -2.4% and -2.5% for LC-AI
Run time
  Encoding runtime is almost the same as that of HM4.0
  Decoding runtime is slightly reduced (2%~4%)
<number>

## Slide 3: Introduction
In HM 4.0, the RQT depth of luma is reused for chroma
The reuse of luma RQT depth avoids additional cost for decidng and signaling of chroma RQT structure
However, in JCTVC-D060, it is reported that RQT introduces losses for Chroma
<number>
Luma
Chroma

## Slide 4: Proposed method
Due to the different statistics between chroma and luma, we propose independent signaling of max intra RQT depth for chroma in SPS
<number>
seq_parameter_set_rbsp( ) { | Descriptor
… | …
log2_diff_max_min_transform_block_size | ue(v)
log2_min_pcm_coding_block_size_minus3 | ue(v)
max_transform_hierarchy_depth_inter | ue(v)
max_transform_hierarchy_depth_intra | ue(v)
max_transform_ depth_intra_chroma | ue(v)
chroma_pred_from_luma_enabled_flag | u(1)
loop_filter_across_slice_flag | u(1)
… | …
} | 

## Slide 5: Proposed method
Since chroma presents smoother texture, and prefers larger transform, we propose default setting of max RQT depth as 0
To avoid 32x32 transform for chroma, which is not in the current design of HEVC, we propose the default setting as
<number>
64x64 CU
32x32 CU
16x16 CU
8x8 CU
Depth 1
Depth 0

## Slide 6: Simulation Results
Anchor – HM4.0
Test condition: AI-HE, AI-LC
Thank Intel for crosschecking (JCTVC-G798)
<number>

## Slide 7: Simulation Results
Experimental results
<number>
Crosscheck | HE-AI | LC-AI
Enc Time (%) | 100% | 98%
Dec Time (%) | 97% | 98%
 | AI-HE |  |  | AI-LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -1.5% | -1.4% | -0.1% | -2.0% | -2.3%
Class B | -0.1% | -1.8% | -1.8% | -0.3% | -2.4% | -3.0%
Class C | 0.0% | -1.3% | -1.5% | -0.2% | -1.5% | -1.9%
Class D | 0.0% | -1.5% | -1.7% | -0.1% | -1.1% | -1.2%
Class E | -0.1% | -2.3% | -2.2% | -0.2% | -5.9% | -4.7%
All Avg | -0.04% | -1.67% | -1.70% | -0.20% | -2.43% | -2.53%
Enc Time (%) | 99% |  |  | 98% |  | 
Dec Time (%) | 96% |  |  | 96% |  | 

## Slide 8: Conclusions
Residue Quad Tree Depth for Chroma in Intra coding is proposed
  Signaling of max intra chroma RQT depth in SPS
  Default setting of max intra chroma RQT depth as 0
Average Chroma BD-rate reductions of
  -0.0%, -1.7% and -1.7% for HE-AI
  -0.2%, -2.4% and -2.5% for LC-AI
Compared to HM4.0, the encoding runtime is almost the same, decoding runtime is slightly reduced (2%~4%)
<number>

## Slide 9
Thank you
Notes: <number>