## Slide 1: CE11: Extended Mode-Dependent Coefficient Scanning
Xin Zhao, Xun Guo, Mei Guo, Shawmin Lei, Siwei Ma and Wen Gao
MediaTek Inc.
Presented by Xun Guo
7th JCT-VC Meeting in Geneva
21-30 Nov., 2011
Notes: <number>

## Slide 2: Overall Summary
Test on extended Mode-dependent coefficients scanning (MDCS) method in CE7 is reported
  Extend to TU sizes of 16x16 and 32x32
    M0: Modified horizontal and vertical scanning orders
    M1: Simplified version of M0
Experimental results
  Based on HM4.0 and conditions of JCTVC-F900
  M0: average BD-rate reductions of 0.2% and 0.6% for AI-HE and AI-LC
  M1: average BD-rate reductions of 0.1% and 0.5% for AI-HE and AI-LC
Run time
  Almost the same as that of HM4.0
<number>

## Slide 3: Outline
Introduction
Proposed method
Simulation results
Conclusions
<number>
Notes: <number>

## Slide 4: Scanning Orders in HM4.0
Zigzag, Horizontal, Vertical and Diagonal
  HE: Diagonal, Horizontal, Vertical
  LC: Zigzag, Horizontal, Vertical
The scanning order for each TU is determined by it’s intra prediction mode
<number>
Zigzag
Horizontal
Vertical
Diagonal

## Slide 5: MDCS Selection
Scanning pattern is selected according to a look-up-table
  HE – 0: Diagonal, 1: Horizontal, 2: Vertical
  LC – 0: Zigzag, 1: Horizontal, 2: Vertical
  For 16x16 and 32x32, zigzag is always used
<number>
Mode TU | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33
32x32 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
16x16 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
8x8 | 1 | 2 | 0 | 0 | 1 | 1 | 0 | 2 | 2 | 0 | 0 | 1 | 1 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 0 | 0
4x4 | 1 | 2 | 0 | 0 | 1 | 1 | 0 | 2 | 2 | 0 | 0 | 1 | 1 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 0 | 0

## Slide 6: Outline
Introduction
Proposed method
Simulation results
Conclusions
<number>
Notes: <number>

## Slide 7: Extend MDCS to Larger TU Sizes
A modified MDCS
  Zigzag, modified horizontal scanning order, modified vertical scanning order
  New mapping table for TUs of 16x16 and 32x32
Proposed mapping table
  0: diagonal/zigzag, 1: modified horizontal, 2: modified vertical
<number>
Mode TU | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33
16x16, 32x32 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 2 | 0 | 0 | 0
4x4, 8x8 | 1 | 2 | 0 | 0 | 1 | 1 | 0 | 2 | 2 | 0 | 0 | 1 | 1 | 0 | 0 | 2 | 2 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 2 | 2 | 2 | 2 | 0 | 0

## Slide 8: Modified Scanning Order M0
Offline derivation of modified horizontal and vertical scanning orders
  To retrieve the scanning pattern analytically, coefficient variances are calculated based on image correlation model
  Scanning pattern is obtained by sorting the variance values in descending order
<number>

## Slide 9: Proposed Scanning Orders for 16x16 TU
Horizontal scanning order
Vertical scanning order is the transposition of horizontal scanning order
<number>

## Slide 10: Proposed Scanning Order for 32x32 TU
Horizontal scanning order
Vertical scanning order is the transposition of horizontal scanning order
<number>

## Slide 11: Modified Scanning Order M1
Simplified version of M0
  Need no additional memory to store the scanning pattern
  For CABAC: support partial parallel context formation
  For CAVLC: support optimization such as SIMD
<number>

## Slide 12: Proposed Scanning Orders for 16x16 TU
Horizontal scanning order
Vertical scanning order is the transposition of horizontal scanning order
<number>

## Slide 13: Proposed Scanning Order for 32x32 TU
Horizontal scanning order
Vertical scanning order is the transposition of horizontal scanning order
<number>

## Slide 14: Outline
Introduction
Proposed method
Simulation results
Conclusions
<number>
Notes: <number>

## Slide 15: Simulation Results
Anchor – HM4.0
Test two modified scan orders
  A: modified scan order M0
  B: modified scan order M1
Two experiments: “A” and “B” for HE-AI and LC-AI
Thank Sony for crosschecking (JCTVC-G364)
<number>

## Slide 16: Simulation Results
Experimental results of A
<number>
 | HE-AI |  |  | LC-AI |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.4% | -0.4% | -0.3% | -0.9% | -1.0%
Class B | -0.2% | -0.8% | -0.8% | -0.9% | -1.7% | -1.7%
Class C | -0.1% | -0.3% | -0.3% | -0.2% | -0.6% | -0.5%
Class D | -0.1% | -0.4% | -0.4% | -0.3% | -0.6% | -0.5%
Class E | -0.4% | -1.2% | -1.0% | -1.2% | -2.3% | -2.0%
All Avg | -0.2% | -0.6% | -0.6% | -0.6% | -1.2% | -1.1%
Enc Time (%) | 99% |  |  | 100% |  | 
Dec Time (%) | 97% |  |  | 97% |  | 

## Slide 17: Simulation Results
Experimental results of B
<number>
 | HE-AI |  |  | LC-AI |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.3% | -0.3% | -0.2% | -0.7% | -0.8%
Class B | -0.2% | -0.7% | -0.7% | -0.8% | -1.6% | -1.6%
Class C | -0.1% | -0.3% | -0.3% | -0.2% | -0.6% | -0.5%
Class D | -0.1% | -0.4% | -0.3% | -0.2% | -0.5% | -0.4%
Class E | -0.4% | -0.9% | -0.8% | -0.8% | -1.8% | -1.6%
All Avg | -0.1% | -0.5% | -0.5% | -0.5% | -1.0% | -1.0%
Enc Time (%) | 100% |  |  | 100% |  | 
Dec Time (%) | 97% |  |  | 97% |  | 

## Slide 18: Conclusions
An extended MDCS method is proposed
  Modified MDCS is applied for 16x16 and 32x32
  Two modified horizontal/vertical scan orders are proposed
For M0, average BD-rate reductions of 0.2% and 0.6% for HE-AI and LC-AI respectively
For M1, average BD-rate reductions of 0.1% and 0.5% for HE-AI and LC-AI respectively
The run time is almost the same as that of HM4.0
<number>

## Slide 19
Thank you
Notes: <number>