## Slide 1: Non-CE11: Methods for Solving the Parsing Issue of MDCS
Xin Zhao, Xun Guo, Chih-Wei Hsu, Tzu-Der Chuang, Yu-Wen Huang and Shawmin Lei
MediaTek Inc.
Presented by Xun Guo
7th JCT-VC Meeting in Geneva
21-30 Nov., 2011
Notes: <number>

## Slide 2: Overall Summary
A solution to solve the parsing issue of MDCS is proposed
  Deriving the context in index of significance map using horizontal scan order
  Coding the last significant position with horizontal scan order
Experimental results
  Based on HM4.0 and conditions of JCTVC-F900
  Average BD-rate increase of 0.22% for AI-HE for both of the methods
    The overall coding gain of MDCS is about 1.5%)
Run time
  Almost the same as that of HM4.0
<number>

## Slide 3: Outline
Introduction
Problem statement
Proposed method
Simulation results
Conclusions
<number>
Notes: <number>

## Slide 4: Problem Statement
MDCS in HM4.0
  Applied on TU sizes of 4x4 and 8x8
  Diagonal, horizontal and vertical scans are used according to the intra prediction modes.
  Significance map and last coefficient position is highly dependant on scan pattern
Intra prediction modes have to be derived in parsing stage
Such parsing issue was focused and fixed by a number of contributions in Torino meeting
  Fixed the number of MPM
  Fixed the number of MVP
Parsing issue of MDCS is the only left one
Copyright © MediaTek Inc. All rights reserved.
<number>

## Slide 5: Concept of the Proposed Solution - Decoder
<number>
HM-4.0
Proposed
CABAC
parsing
Coeff. Buffer
IT/IQ
D
H
V
H
CABAC parsing
H
Coeff. Buffer
IT/IQ
D
H
V
Parsing stage
Reconstruction stage
MDCS
MDCS
Always parsing with horizontal scanning

## Slide 6: Concept of the Proposed Solution - Encoder
<number>
T/Q
H
Coeff. Buffer
CABAC
Coding
D
H
V
HM-4.0
Proposed
T/Q
Coeff. Buffer
CABAC
Coding
D
H
V
H
MDCS
MDCS
Always coding with horizontal scanning

## Slide 7: Implementation 1
Significance map
  Context index is derived according to the position (X, Y) along with scan order within a 4x4 or 8x8 TU
Last significant coefficient position
  The coordinate (x, y) in horizontal order is transmitted
Context formation keeps unchanged
Copyright © MediaTek Inc. All rights reserved.
<number>
Y = scanPos / N,
X = scanPos – (Y×N),
where N = 4 or 8

## Slide 8: Implementation 2
All scanning patterns are re-mapped into horizontal pattern, then only horizontal scan is used in coding
Encoder
  (diagonal, vertical, horizontal) => horizontal
Decoder
  Horizontal => (diagonal, vertical, horizontal)
<number>

## Slide 9: Simulation Results
Anchor – HM4.0
Tested two implementations
Two experiments: “A” and “B” for AI-HE, RA-HE and LB-HE
Thank Intel for crosschecking (JCTVC-G531)
<number>

## Slide 10: Simulation Results
Experimental results of A and B
<number>
 | Intra, HE |  |  | Random Access, HE |  | 
 | Y | U | V | Y | U | V
Class A | 0.30% | 0.12% | 0.19% | 0.12% | 0.13% | 0.14%
Class B | 0.20% | 0.00% | 0.07% | 0.11% | 0.02% | -0.07%
Class C | 0.19% | 0.19% | 0.20% | 0.15% | 0.36% | 0.36%
Class D | 0.23% | 0.36% | 0.43% | 0.16% | 0.45% | 0.22%
Class E | 0.19% | -0.08% | -0.21% |  |  | 
All Avg | 0.22% | 0.12% | 0.15% | 0.13% | 0.23% | 0.15%
Enc Time (%) | 99% |  |  | 100% |  | 
Dec Time (%) | 97% |  |  | 100% |  | 
 | Low Delay B, HE |  |  | Low Delay P, HE |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.05% | -0.17% | -0.12% | 0.08% | 0.12% | -0.14%
Class C | 0.11% | 0.10% | 0.13% | 0.07% | 0.14% | 0.25%
Class D | 0.09% | 0.18% | 0.16% | 0.05% | 0.26% | -0.09%
Class E | 0.11% | 0.12% | 0.53% | 0.03% | -0.09% | 0.03%
All Avg | 0.08% | 0.04% | 0.13% | 0.06% | 0.12% | 0.00%
Enc Time (%) | 100% |  |  | 100% |  | 
Dec Time (%) | 98% |  |  | 98% |  | 

## Slide 11: Conclusions
Methods of solving parsing issue of MDCS in CABAC
  Simple modifications residual coding of MDCS
  Pre-scan procedure
No additional overhead
Average BD-rate increase of 0.22% in AI-HE for both of the implementation
The run time is almost the same as that of HM4.0
<number>

## Slide 12
Thank you
Notes: <number>