## Slide 1: CE12 Subtest 1: Chroma Deblocking Filter
Qian Huang, Jicheng An, Xun Guo, Shawmin Lei, Andrey Norkin, Kenneth Andersson and Rickard Sjöberg
MediaTek and Ericsson.
Presented by Xun Guo
7th JCT-VC Meeting in Geneva
21-30 Nov., 2011
Notes: <number>

## Slide 2: Overall Summary
Major difference compared to JCTVC-F120
  Removing 4x4 filtering unit
Some modifications in chroma deblocking filter
  Added filtering on/off decision
    Chroma components share the filtering decision results of luma
  Also filter inter boundaries
    The boundaries with Bs > 0 could be filtered
Experimental results
  Objective quality
    Average BD-rate reductions of 0.4%, 1.5% and 1.2% for AI, RA and LD chroma components, respectively
  Subjective quality
    Similar to HM4.0
Run time
  Almost the same as that of HM4.0
<number>

## Slide 3: Outline
Introduction
Proposed method
Simulation results
Conclusions
<number>
Notes: <number>

## Slide 4: Filtering on/off Decision in HM4.0
Only apply on luma
<number>
d = |p22 - 2*p12 + p02| + |q22 - 2*q12 + q02| + |p25 - 2*p15 + p05| + |q25 - 2*q15 + q05|
d < beta (QPluma)

## Slide 5: Proposed Changes
Re-use luma filtering decision information for chroma
  For Intra slices
    Reuse the computed d of luma
    Use 2xQPluma as thresholds
  For non-Intra slices
    Directly use the filtering decision results of luma
Also filter inter boundaries
  Boundaries with Bs > 0 could be filtered, which is Bs > 2 in HM4.0
<number>
d < 2xQPluma

## Slide 6: Simulation Results
<number>
Anchor – HM4.0
Recommended test conditions in JCTVC-F900
Thank Microsoft for crosschecking (JCTVC-G411)
 | Intra |  |  | Intra_LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
All | 0.0% | -0.6% | -0.5% | 0.0% | -0.3% | -0.2%
 | 0.0% | -0.6% | -0.5% | 0.0% | -0.3% | -0.2%
EncTime[%] | 99.5% |  |  | 99.9% |  | 
DecTime[%] | 99.8% |  |  | 99.0% |  | 
 | RandomAccess |  |  | RandomAccess_LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
All | 0.0% | -1.5% | -1.4% | 0.0% | -1.7% | -1.4%
 | 0.0% | -1.5% | -1.3% | 0.0% | -1.7% | -1.4%
EncTime[%] | 99.7% |  |  | 100.0% |  | 
DecTime[%] | 100.2% |  |  | 99.0% |  | 
 | LowDelay |  |  | LowDelay_LoCo |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
All | -0.1% | -1.5% | -1.5% | -0.1% | -0.9% | -0.9%
 | -0.1% | -1.5% | -1.5% | -0.1% | -0.9% | -0.9%
EncTime[%] | 99.8% |  |  | 100.0% |  | 
DecTime[%] | 99.5% |  |  | 99.2% |  | 

## Slide 7: Conclusions
A modified chroma deblocking filter is proposed
  Filtering on/off decision is added for chroma boundaries
  Inter boundary filtering is added
Objective performance
  Average BD-rate reductions of 0.4%, 1.5% and 1.2% for AI, RA and LD chroma components, respectively
Subjective quality
  Similar to HM4.0
Decoding time is almost the same as that of HM4.0
<number>

## Slide 8
Thank you
Notes: <number>

## Slide 9: Consistency Statistics of Filtering Decision
Statistics of identical filtering decisions for luma and chroma
Copyright © MediaTek Inc. All rights reserved.
<number>