## Slide 1: JCTVC-G290: Deblocking Filter Simplifications
Geert Van der Auwera, Xianglin Wang, Marta Karczewicz
Qualcomm Inc.

## Slide 2: Summary
Deblocking filter simplifications are proposed:
  Weak filter: simplify coefficients for delta computation
  Reduction of number of strong/weak filter decisions for an edge segment is reduced from eight to two (edge is split into 2 halves of 4 lines each)

## Slide 3: Weak Filter Delta Simplification
HM4:
   = ( 9*(q0-p0) - 3*(q1-p1) + 8 )/16
Proposed:
  = ( 3*(q0-p0) - (q1-p1) + 4 )/8
Objective result:
  Gains: -0.1% to -0.3%
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.3% | 0.0% | 0.0% | -0.2% | 0.0% | 0.0%
Class B | -0.3% | 0.0% | 0.0% | -0.2% | 0.0% | 0.0%
Class C | -0.2% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
Class D | -0.2% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
Class E | -0.2% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
Overall | -0.2% | 0.0% | 0.0% | -0.2% | 0.0% | 0.0%
 | -0.2% | 0.0% | 0.0% | -0.2% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 97% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.1% | -0.1% | -0.2% | -0.1% | 0.1% | -0.1%
Class B | -0.2% | 0.0% | 0.0% | -0.1% | -0.1% | 0.1%
Class C | -0.1% | -0.1% | 0.0% | -0.1% | 0.0% | 0.1%
Class D | -0.1% | 0.1% | 0.0% | -0.1% | -0.2% | 0.0%
Class E |  |  |  |  |  | 
Overall | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
 | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
Enc Time[%] | 96% |  |  | 100% |  | 
Dec Time[%] | 97% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.2% | -0.2% | -0.3% | -0.1% | 0.0% | 0.1%
Class C | -0.1% | -0.1% | -0.1% | -0.1% | 0.2% | -0.2%
Class D | -0.2% | 0.1% | 0.2% | -0.1% | 0.1% | 0.0%
Class E | -0.3% | -0.2% | 0.8% | -0.2% | 0.3% | -0.3%
Overall | -0.2% | -0.1% | 0.1% | -0.1% | 0.1% | -0.1%
 | -0.2% | -0.1% | 0.1% | -0.1% | 0.1% | -0.1%
Enc Time[%] | 97% |  |  | 99% |  | 
Dec Time[%] | 98% |  |  | 97% |  | 

## Slide 4: Strong/Weak Decision Simplification
HM4:
  Computed for each line/column of 8-sample edge segment ( i=0…7 )
  d is computed only once per edge segment
  tC and β are threshold parameters depending on QP
Proposed:
  Use decision result of line i=2 for first 4 lines/columns of 8-sample edge segment and use decision result of line i=5 for second 4 lines/columns of 8-sample edge segment.

## Slide 5: Strong/Weak Decision Simplification
Objective result: comparable with HM4 anchor
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% |  |  | 96% |  | 
Dec Time[%] | 97% |  |  | 100% |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.2% | -0.3% | 0.1% | 0.0% | 0.1%
Class B | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.1% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
Class D | 0.1% | 0.0% | -0.1% | 0.1% | -0.1% | 0.1%
Class E |  |  |  |  |  | 
Overall | 0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
 | 0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 96% |  |  | 100% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.1% | -0.1% | -0.1% | 0.1% | 0.0% | 0.3%
Class C | 0.1% | 0.0% | -0.1% | 0.0% | 0.2% | -0.2%
Class D | 0.1% | 0.0% | -0.1% | 0.0% | 0.1% | -0.1%
Class E | 0.3% | 0.1% | 0.8% | 0.1% | -0.1% | 0.1%
Overall | 0.1% | 0.0% | 0.1% | 0.1% | 0.1% | 0.1%
 | 0.1% | 0.0% | 0.1% | 0.1% | 0.0% | 0.0%
Enc Time[%] | 97% |  |  | 95% |  | 
Dec Time[%] | 98% |  |  | 97% |  | 

## Slide 6: Conclusion
Deblocking filter simplifications:
  Simpler weak filter delta: gains from -0.1% to -0.3%
  Strong/weak decision computations reduced from 8 to 2 (edge segment is split into 2 halves of 4 lines each)
Proposed to adopt in HM5
Thanks to Panasonic for cross checking! (JCTVC-G929)