## Slide 1: JCTVC-G291: Non-CE12 Subtest 5: Transform dependent Deblocking Filter Parameter Adjustment in Slice Level
Geert Van der Auwera, Xianglin Wang, Marta Karczewicz
Qualcomm Inc.

## Slide 2: Summary
Signaling of deblocking filter control parameters in slice header to adjust tC, β parameters
  Transform block size dependent tC to control deblocking strength, because of significantly different psycho-visual importance of block sizes (4x4 up to 32x32)
    Allows subjective tuning depending on content, frame resolution, screen size, etc.
  Separate for intra and inter tC
  One parameter for adjusting β
deblocking_filter_control_present_flag in SPS

## Slide 3: Adjusting tC, β
Currently: no adjustment through signaling
  TcOffset = ( Bs > 2 ) ? DEFAULT_INTRA_TC_OFFSET(=2) : 0
  tC: Q = Clip3(0, MAX_QP+4, QP + TcOffset ) (luma and chroma deblocking)
  β: Q = Clip3(0, MAX_QP, QP ) (luma deblocking only)
Proposed: if deblocking_filter_control_present_flag = true
  slice_tc_offset_intra
  slice_tc_offset_intra_delta
  slice_tc_offset_inter
  slice_tc_offset_inter_delta
  slice_beta_offset

## Slide 4: Adjusting tC, β
Proposed:
  transform_type = NxN (= 4x4 or 8x8 or 16x16 or 32x32)
    INTRA_TC_OFFSET = slice_tc_offset_intra + tc_offset_NxN_intra_delta
    INTER_TC_OFFSET = slice_tc_offset_inter + tc_offset_NxN_inter_delta
    BETA_OFFSET = slice_beta_offset
  Tc_offset_NxN_intra_delta = slice_tc_offset_intra_delta * factor_NxN
  Tc_offset_NxN_inter_delta = slice_tc_offset_inter_delta * factor_NxN
  Constant values used in the computation (not signaled):
    Factor_4x4 = 3
    Factor_8x8 = 2
    Factor_16x16 = 1
    Factor_32x32 = 0
  TcOffset = ( Bs > 2 ) ? INTRA_TC_OFFSET : INTER_TC_OFFSET
  BetaOffset = BETA_OFFSET
  tC: Q = Clip3(0, MAX_QP+4, QP + TcOffset ) (luma and chroma)
  β: Q = Clip3(0, MAX_QP+4, QP + BetaOffset ) (luma de-blocking only)

## Slide 5: Proposed Signaling
SPS
Slice Header
  If deblocking_filter_control_present_flag = false
    LoopFilterDisable : 0
    LoopFilterBetaOffset : 0
    slice_tc_offset_intra : 0
    slice_tc_offset_inter : -2
    slice_tc_offset_intra_delta : -1
    slice_tc_offset_inter_delta : 1
  tC offsets for block sizes (32x32, 16x16, 8x8, 4x4):
    Intra: (0, -1, -2, -3)
    Inter: (-1, 0, 1, 2)
slice_header( ) {
...
if( deblocking_filter_control_present_flag ) {
disable_deblocking_filter_idc
if( disable_deblocking_filter_idc != 1 ) {
slice_beta_offset
slice_tc_offset_intra
slice_tc_offset_intra_delta
if ( slice_type != I) {
slice_tc_offset_inter
slice_tc_offset_inter_delta
}
}
}
}
seq_parameter_set_rbsp( ) {
...
chroma_pred_from_luma_enabled_flag
deblocking_filter_control_present_flag
loop_filter_across_slice_flag
sample_adaptive_offset_enabled_flag
adaptive_loop_filter_enabled_flag
pcm_loop_filter_disable_flag
...
}

## Slide 6: Objective Results
Compared with HM4.0 anchor (QP=22, 27, 32, 37)
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.3% | -0.4% | -0.3% | 0.0% | -0.4% | -0.3%
Class B | -0.3% | -0.5% | -0.4% | -0.1% | -0.4% | -0.3%
Class C | -0.2% | -0.6% | -0.5% | -0.1% | -0.4% | -0.3%
Class D | -0.2% | -0.5% | -0.5% | -0.1% | -0.3% | -0.2%
Class E | -0.2% | 0.0% | 0.0% | 0.0% | 0.2% | 0.3%
Overall | -0.3% | -0.4% | -0.4% | -0.1% | -0.3% | -0.2%
 | -0.3% | -0.4% | -0.3% | -0.1% | -0.3% | -0.2%
Enc Time[%] | 103% |  |  | 99% |  | 
Dec Time[%] | 99% |  |  | 102% |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -0.4% | -0.4% | 0.0% | -0.3% | -0.4%
Class B | -0.1% | -0.4% | -0.3% | 0.0% | -0.4% | -0.3%
Class C | 0.0% | -0.3% | -0.3% | 0.0% | -0.6% | -0.4%
Class D | 0.1% | -0.3% | -0.2% | 0.1% | -0.5% | -0.4%
Class E |  |  |  |  |  | 
Overall | -0.1% | -0.4% | -0.3% | 0.0% | -0.4% | -0.4%
 | 0.0% | -0.4% | -0.3% | 0.0% | -0.4% | -0.4%
Enc Time[%] | 100% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | -0.1%
Class C | 0.0% | -0.1% | 0.1% | 0.1% | 0.1% | -0.2%
Class D | 0.2% | 0.2% | 0.6% | 0.1% | 0.4% | 0.0%
Class E | 0.1% | 0.4% | 0.8% | 0.0% | 0.5% | 0.2%
Overall | 0.1% | 0.1% | 0.3% | 0.1% | 0.2% | 0.0%
 | 0.1% | 0.1% | 0.3% | 0.1% | 0.2% | 0.0%
Enc Time[%] | 100% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 

## Slide 7: Objective Results
Compared with HM4.0 anchor for high QP (=32, 37, 42, 47)
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.3% | -0.3% | -0.2% | 0.1% | -0.3% | -0.1%
Class B | -0.2% | -0.1% | -0.1% | 0.1% | -0.1% | 0.1%
Class C | -0.2% | -0.3% | -0.2% | -0.1% | -0.1% | 0.1%
Class D | -0.2% | -0.3% | -0.2% | -0.1% | 0.0% | 0.2%
Class E | -0.2% | 0.0% | 0.0% | 0.1% | 0.1% | 0.3%
Overall | -0.2% | -0.2% | -0.2% | 0.0% | -0.1% | 0.1%
 | -0.2% | -0.3% | -0.2% | 0.0% | -0.1% | 0.1%
Enc Time[%] | 98% |  |  | 97% |  | 
Dec Time[%] | 101% |  |  | 101% |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.1% | -0.3% | 0.0% | 0.2% | 0.2% | -0.3%
Class B | 0.0% | -0.1% | 0.0% | 0.1% | -0.2% | 0.0%
Class C | 0.2% | 0.1% | 0.1% | 0.1% | -0.2% | 0.3%
Class D | 0.7% | 0.3% | 0.5% | 0.6% | 0.0% | 0.3%
Class E |  |  |  |  |  | 
Overall | 0.2% | 0.0% | 0.1% | 0.2% | -0.1% | 0.1%
 | 0.2% | 0.0% | 0.1% | 0.2% | 0.0% | 0.1%
Enc Time[%] | 99% |  |  | 99% |  | 
Dec Time[%] | 98% |  |  | 101% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.2% | 0.7% | -0.1% | 0.1% | 0.1% | 0.0%
Class C | 0.2% | 0.1% | 0.6% | 0.3% | 0.3% | -0.3%
Class D | 1.0% | 1.9% | 1.2% | 0.7% | 0.6% | 0.4%
Class E | 0.7% | 1.3% | 1.2% | 0.4% | -0.1% | 0.4%
Overall | 0.5% | 1.0% | 0.7% | 0.4% | 0.2% | 0.1%
 | 0.5% | 0.9% | 0.5% | 0.4% | 0.2% | 0.1%
Enc Time[%] | 99% |  |  | 98% |  | 
Dec Time[%] | 101% |  |  | 99% |  | 

## Slide 8: Subjective Results
Class B “Kimono” sequence (Low delay B LC, QP=32). Roof area contains more details on the right.
HM4.0
Proposal
Frame 181

## Slide 9: Subjective Results
Class C “BQMall” sequence (Low delay B LC, QP=32). The HM4 frame contains trailing edges.
HM4.0
Proposal
Frame 220

## Slide 10: Subjective Adjustment Example
Class C “RaceHorses” coded using “All Intra LC” and QP = 37

## Slide 11: Subjective Adjustment Example
slice_tc_offset_intra_delta = -5
  tC offsets for 32x32, 16x16, 8x8, 4x4 : 0, -5, -10, -15

## Slide 12: Conclusion
Signaling of deblocking filter control parameters in slice header to adjust tC, β
deblocking_filter_control_present_flag in SPS
Transform block size dependent tC to control subjective quality of wide range of block sizes (4x4 to 32x32)
BD-rate gains, mainly for intra
Proposed to adopt in HM5
Thanks to Toshiba for cross checking!