## Slide 1: Results on Context Simplification for Coefficients Coding
JCTVC-G301
Wenpeng Ding, Jizheng Xu
Beijing University of Technology

## Slide 2: Summary
Large number of contexts used for coefficients coding.
  60->24 for both coeff_abs_level_greater1_flag and coeff_abs_level_greater2_flag.
  72 (60%) contexts are removed
Context with similar 0/1 probability can be grouped together.
Small coding performance comparied with HM4.0
  BDRate increase 0.02 for Intra, -0.03 for Random access and -0.13 for Low delay.

## Slide 3: Proposed scheme
Reduce the number of used contexts by remapping.
Mapping tables to map similar contexts to one context. Four tables for luma/chroma/inter/intra.
Original | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Proposed | 0 | 1 | 2 | 3 | 4 | 0 | 5 | 4 | 6 | 6 | 7 | 8 | 8 | 8 | 9
Original | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Proposed | 5 | 10 | 10 | 10 | 1 | 6 | 3 | 3 | 3 | 3 | 0 | 9 | 11 | 11 | 11
Context simplification on coeff_abs_level_greater1_flag for Intra Luma : 30 maps to 12

## Slide 4: Working draft modification
Derivation process of ctxIdxInc for the syntax element coeff_abs_level_greater1_flag
ctxIdxInc = ( ctxSet * 5 ) + Min( 4, greater1Ctx )
mapIdx = (slide_type>1?2:0)+(cIdx>1?1:0)
ctxIdxInc = abs_level_greater1_map[mapIdx][ctxIdxInc ] (9‑70)
Derivation process of ctxIdxInc for the syntax element coeff_abs_level_greater2_flag
ctxIdxInc = ( ctxSet * 5 ) + Min( 4, greater1Ctx )
mapIdx = (slide_type>1?2:0)+(cIdx>1?1:0)
ctxIdxInc = abs_level_greater2_map[mapIdx][ctxIdxInc ] (9‑77)

## Slide 5: Results
 | All Intra HE |  |  | All Intra LQ |  | 
 | Y | U | V | Y | U | V
Class A | 0.01% | -0.06% | 0.01% | 0.02% | 0.00% | 0.01%
Class B | 0.02% | 0.01% | 0.01% | 0.02% | 0.04% | 0.02%
Class C | 0.00% | 0.03% | 0.00% | 0.01% | 0.01% | 0.01%
Class D | 0.01% | 0.04% | -0.04% | 0.02% | 0.02% | 0.00%
Class E | 0.02% | 0.00% | 0.00% | 0.00% | -0.10% | 0.01%
Overall | 0.02% | 0.00% | 0.00% | 0.01% | 0.00% | 0.01%
 | 0.02% | 0.00% | -0.01% | 0.01% | 0.01% | 0.00%
Enc Time[%] | 91% |  |  | 101% |  | 
Dec Time[%] | 92% |  |  | 101% |  | 
 | Random Access HE |  |  | Random Access LQ |  | 
 | Y | U | V | Y | U | V
Class A | -0.02% | -0.01% | -0.03% | 0.02% | -0.09% | -0.04%
Class B | -0.06% | -0.05% | -0.15% | 0.04% | -0.08% | -0.20%
Class C | -0.04% | -0.24% | -0.22% | -0.02% | -0.08% | -0.07%
Class D | -0.02% | -0.05% | -0.33% | 0.00% | -0.02% | -0.28%
Class E |  |  |  |  |  | 
Overall | -0.04% | -0.08% | -0.18% | 0.01% | -0.07% | -0.15%
 | -0.03% | -0.09% | -0.19% | 0.01% | -0.05% | -0.15%
Enc Time[%] | 109% |  |  | 101% |  | 
Dec Time[%] | 107% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LQ |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.16% | -0.29% | -0.66% | 0.02% | 0.02% | 0.01%
Class C | -0.15% | -0.29% | -0.58% | -0.03% | -0.10% | -0.06%
Class D | -0.07% | -0.11% | -0.04% | -0.02% | -0.20% | -0.13%
Class E | -0.15% | 0.29% | 0.49% | -0.03% | -0.30% | 0.10%
Overall | -0.13% | -0.13% | -0.27% | -0.01% | -0.13% | -0.02%
 | -0.13% | -0.06% | -0.21% | -0.01% | -0.15% | -0.07%
Enc Time[%] | 141% |  |  | 101% |  | 
Dec Time[%] | 155% |  |  | 99% |  | 

## Slide 6: Cross-checking Results
Thanks TI and Huawei for cross-checking our results.
 | Intra |  |  | Random access |  |  | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.01% | -0.06% | 0.01% | -0.02% | -0.01% | -0.03% |  |  | 
Class B | 0.02% | 0.01% | 0.01% | -0.06% | -0.05% | -0.15% | -0.16% | -0.29% | -0.66%
Class C | 0.00% | 0.03% | 0.00% | -0.04% | -0.24% | -0.22% | -0.15% | -0.29% | -0.58%
Class D | 0.01% | 0.04% | -0.04% | -0.02% | -0.05% | -0.33% | -0.07% | -0.11% | -0.04%
Class E | 0.02% | 0.00% | 0.00% |  |  |  | -0.15% | 0.29% | 0.49%
All | 0.02% | 0.00% | 0.00% | -0.04% | -0.08% | -0.18% | -0.13% | -0.13% | -0.27%
Enc Time[%] | 99% |  |  | 97% |  |  | 99% |  | 
Dec Time[%] | 99% |  |  | 94% |  |  | 95% |  | 

## Slide 7: Complexity
Expected to be same as HM4.0
The running times in our results is obtained using different machines, which makes it unreliable.
Running time from cross-checkers shows that the complexity is the same as that of HM4.0

## Slide 8: Conclusion
72 Contexts (60%) are removed for
c…_greater1_flag and c…_greater2_flag
Small coding gain
Simple solution by mapping contexts.
Same or less runtime complexity as HM4.0.
Recommend to adopt.