## Slide 1: Results on Context Simplification for Coefficients Coding
JCTVC-G301
Wenpeng Ding, Jizheng Xu and Xiaoyin Che
Beijing University of Technology

## Slide 2: Summary
Large number of contexts used for coefficients coding.
  60->24 for both coeff_abs_level_greater1_flag and coeff_abs_level_greater2_flag.
Context with similar 0/1 probability can be grouped together.
Small coding performance comparied with HM4.0
  BDRate increase 0.02 for Intra, -0.03 for Random access and -0.13 for Low delay.

## Slide 3: Proposed scheme
Reduce the number of used contexts by remapping.
Mapping tables to map similar contexts to one context. Four tables for luma/chroma/inter/intra.
Original | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Proposed | 0 | 1 | 2 | 3 | 4 | 0 | 5 | 4 | 6 | 6 | 7 | 8 | 8 | 8 | 9
Original | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Proposed | 5 | 10 | 10 | 10 | 1 | 6 | 3 | 3 | 3 | 3 | 0 | 9 | 11 | 11 | 11
Context simplification on coeff_abs_level_greater1_flag for Intra Luma : 30 maps to 12

## Slide 4: Working draft modification
Derivation process of ctxIdxInc for the syntax element coeff_abs_level_greater1_flag
ctxIdxInc = ( ctxSet * 5 ) + min( 4, greater1Ctx ) (9‑70)
ctxIdxInc = abs_level_greater1_map[IsChroma] [ctxIdxInc] (9‑71)
Derivation process of ctxIdxInc for the syntax element coeff_abs_level_greater2_flag
  ctxIdxInc = ( ctxSet * 5 ) + min(4, greater2Ctx ) (9‑75)
  ctxIdxInc = abs_level_greater2_map[IsChroma] [ctxIdxInc] (9‑76)

## Slide 5: Results
 | Intra |  |  | Intra LQ |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.01 | -0.05 | -0.04 | 0.02 | 0.02 | -0.04
Class B | 0.03 | 0.01 | 0.01 | 0.02 | 0.05 | 0.02
Class C | 0.00 | 0.01 | 0.00 | 0.01 | 0.01 | 0.01
Class D | 0.01 | 0.02 | -0.05 | 0.02 | 0.03 | 0.00
Class E | 0.02 | 0.00 | 0.00 | 0.00 | -0.10 | 0.01
All | 0.02 | 0.00 | -0.01 | 0.01 | 0.01 | 0.00
 |  | Random access |  |  | Random access LQ | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -0.02 | -0.06 | 0.01 | 0.01 | -0.08 | -0.04
Class B | -0.05 | -0.07 | -0.17 | 0.03 | -0.04 | -0.18
Class C | -0.04 | -0.21 | -0.20 | -0.02 | -0.07 | -0.07
Class D | -0.02 | -0.01 | -0.41 | 0.00 | -0.02 | -0.28
Class E |  |  |  |  |  | 
All | -0.03 | -0.09 | -0.19 | 0.01 | -0.05 | -0.15
 | Low delay |  |  | Low delay LC |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A |  |  |  |  |  | 
Class B | -0.16 | -0.26 | -0.58 | -1.09 | -1.19 | 0.48
Class C | -0.14 | -0.21 | -0.44 | 0.38 | 1.06 | 1.67
Class D | -0.06 | -0.07 | -0.10 | 0.28 | 1.37 | 1.75
Class E | -0.16 | 0.49 | 0.57 | -1.18 | -1.10 | -0.39
All | -0.13 | -0.06 | -0.21 | -0.40 | 0.03 | 0.93

## Slide 6: Cross-checking Results
Thanks TI for cross-checking our results.
 | Intra |  |  | Random access |  |  | Low delay |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.01% | -0.06% | 0.01% | -0.02% | -0.01% | -0.03% |  |  | 
Class B | 0.02% | 0.01% | 0.01% | -0.06% | -0.05% | -0.15% | -0.16% | -0.29% | -0.66%
Class C | 0.00% | 0.03% | 0.00% | -0.04% | -0.24% | -0.22% | -0.15% | -0.29% | -0.58%
Class D | 0.01% | 0.04% | -0.04% | -0.02% | -0.05% | -0.33% | -0.07% | -0.11% | -0.04%
Class E | 0.02% | 0.00% | 0.00% |  |  |  | -0.15% | 0.29% | 0.49%
All | 0.02% | 0.00% | 0.00% | -0.04% | -0.08% | -0.18% | -0.13% | -0.13% | -0.27%
Enc Time[%] | 99% |  |  | 97% |  |  | 99% |  | 
Dec Time[%] | 99% |  |  | 94% |  |  | 95% |  | 

## Slide 7: Complexity
Expected to be same as HM4.0
The running times in our results is obtained using different machines, which makes it unreliable.
Running time from TI shows that the complexity is the same or less than that of HM4.0

## Slide 8: Conclusion
Contexts for are reduced by 60% for
c…_greater1_flag and c…_greater2_flag
Small coding gain
Simple solution by mapping contexts.
Same or less runtime complexity as HM4.0.
Recommend to adopt.