## Slide 1: JCTVC-G318 Tile groups
Ye-Kui Wang, Ying Chen, Muhammed Coban, Marta Karczewicz

## Slide 2: Proposal
A tile grouping mechanism
  Tiles are assigned to tile groups
  Decoding/scan order: in ascending order of tile group IDs
  Inside a tile group: tile rater scan order
tile #0, tile group #0
tile #1, tile group #1
tile #2, tile group #0
tile #3, tile group #1
tile #4, tile group #0
tile #5, tile group #1
tile #6, tile group #0
tile #7, tile group #1

## Slide 3: Why?
Improved parallel processing
Improved error resilience
Flexible region-of-interest (ROI) coding

## Slide 4: Improved parallel processing
Tiles 0, 2, 4, 6 are processed by one processing (encoding or decoding) core, and tiles 1, 3, 5, 7 are processed by another processing core.
It would thus be ideal to put coded bits for tiles 0, 2, 4, 6 continuously in decoding order, followed by tiles 1, 3, 5, 7.
tile #0, tile group #0
tile #1, tile group #1
tile #2, tile group #0
tile #3, tile group #1
tile #4, tile group #0
tile #5, tile group #1
tile #6, tile group #0
tile #7, tile group #1

## Slide 5: Improved error resilience
Better error concealment using received (and correctly decoded) neighboring blocks
tile #0, tile group #0
tile #1, tile group #1
tile #2, tile group #0
tile #3, tile group #1
tile #4, tile group #0
tile #5, tile group #1
tile #6, tile group #0
tile #7, tile group #1
tile group #0
tile group #1

## Slide 6: Flexible ROI coding
The region covered by tile group#0 is an independently decodable region, which can be the only ROI to some clients. Due to restrictions such as decoding capability and network bandwidth as well as user preferences, the clients may choose to request the transmission of only coded bits that are sufficient to decode the ROI.
In this case, it is ideal to place the coded bits of the tiles covering the ROI into one slice, and the coded bits of other tiles into a different slice.
tile group #1
tile group #0

## Slide 7: Six tile group types
0: all tiles belong to one tile group
1: each column of tiles belongs to one tile group, and the tile group identifier TileGroupId is equal to 0 for the left-most column of tiles, and increases by 1 for each column of tiles from left to right, modular NumTileGroups
2: each row of tiles belongs to one tile group, and the tile group identifier TileGroupId is equal to 0 for the top row of tiles, and increases by 1 for each row of tiles from top to bottom, modular NumTileGroups
3: one or more "foreground" tile groups and the "leftover" tile group, similar as slice group type 2 in AVC
4 or 5: explicit assignment of each tile to a tile group, coded in a compact manner, column first or row first
6: checkerboard like assignment of tiles to two tile groups, similar as slice group type 1 in AVC