## Slide 1: JCTVC-G320 CE11: Scanning Passes of Residual Data in HE
Joel Sole, Rajan Joshi, Marta Karczewicz

## Slide 2: HEVC Scanning Passes
HEVC has 5 scan passes over the residual data
Pass | Syntax element | CABAC mode | # bins | Scan Type
1 | significant_coeff_flag | Regular | 1 | Entire TU
2 | coeff_abs_level_greater1_flag | Regular | 1 | 16 coeff sets
3 | coeff_abs_level_greater2_flag | Regular | 1 | 16 coeff sets
4 | coeff_sign_flag | Bypass | 1 | 16 coeff sets
5 | coeff_abs_level_minus3 | Bypass | >= 1 | 16 coeff sets
Entire TU scan
(significance flag)
16 coeff set scan
(coeff level)
Interleaved

## Slide 3: HEVC Scanning Passes
Coding passes with regular bins are done differently (first 3 passes)
  All use regular bins with contexts depending of previous coefficients, but
  Significance is on the full TU, coefficient on sets of 16 consecutive coefficients
Coding passes with different bin type are done in the same way
Proposal: unify scanning passes
  All passes in sets of 16 coefficients
    Other set sizes are possible
  All passes on the entire transform unit
1 | significant_coeff_flag | Regular | Entire TU
2 | coeff_abs_level_greater1_flag | Regular | 16 coeff sets
3 | coeff_abs_level_greater2_flag | Regular | 16 coeff sets
2 | coeff_abs_level_greater1_flag | Regular | 16 coeff sets
3 | coeff_abs_level_greater2_flag | Regular | 16 coeff sets
4 | coeff_sign_flag | Bypass | 16 coeff sets
5 | coeff_abs_level_minus3 | Bypass | 16 coeff sets

## Slide 4: Unified Scan Passes
All scan passes the same
Two variants studied in CE11:
  Interleaved sub-set scans
    More localized data processing, parallel set processing
  Entire TU scans
    More bypass data grouping, better for speculative coding
Trade-offs on selecting the set size (from 16 to TU)
  Memory requirements, parallelization, data grouping, data access
Note that bypass scan passes (4 and 5) can be interchanged

## Slide 5: Performance and Conclusions
Common conditions, HE configuration
  BD-rate average YUV: ( 6Y + U + V ) / 8
  Cross-check: Canon (JCTVC-G412)
  Complexity and BD-rate is very similar to HM4.0
    Same bins coded in different order
    Sub-block based scans can be applied with sub-set passes
  Recommend to unify the scan passes in HEVC
BD-rate | AI – HE | RA – HE | LB – HE
Sub-sets 16 | 0.00% | 0.00% | -0.01%
Entire TU | 0.00% | 0.02% | 0.02%

## Slide 6
Thank you!

## Slide 7: BD-rate (with class F and low delay P)
5 scan passes on sub-set of 16 coefficients
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.00% | -0.05% | -0.04% | 0.00% | -0.06% | 0.11% |  |  |  |  |  | 
Class B | 0.00% | 0.01% | 0.02% | -0.01% | -0.05% | 0.01% | 0.02% | -0.03% | -0.60% | 0.01% | 0.12% | -0.17%
Class C | 0.00% | 0.03% | 0.00% | 0.03% | -0.03% | 0.14% | 0.00% | 0.02% | -0.25% | 0.02% | 0.08% | -0.15%
Class D | 0.00% | -0.03% | -0.05% | 0.03% | 0.02% | -0.36% | 0.05% | 0.15% | 0.17% | 0.05% | 0.08% | -0.11%
Class E | 0.00% | -0.02% | 0.01% |  |  |  | 0.11% | -1.23% | 0.58% | 0.02% | 0.00% | 0.08%
Class F | 0.01% | -0.02% | 0.01% | 0.00% | 0.09% | -0.11% | -0.14% | -0.04% | 0.15% | -0.01% | 0.03% | -0.06%
Overall | 0.00% | -0.01% | -0.01% | 0.01% | -0.01% | -0.04% | 0.00% | -0.16% | -0.05% | 0.01% | 0.07% | -0.09%
 | 0.00% | -0.01% | -0.02% | 0.01% | -0.01% | -0.02% | 0.00% | -0.20% | 0.02% | 0.02% | 0.06% | -0.05%
Enc T [%] | 102% |  |  | 100% |  |  | 98% |  |  | 99% |  | 
Dec T[%] | 100% |  |  | 100% |  |  | 100% |  |  | 99% |  | 

## Slide 8: BD-rate (with class F and low delay P)
5 scan passes on the entire TU
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.00% | -0.02% | 0.02% | 0.05% | -0.02% | -0.23% |  |  |  |  |  | 
Class B | 0.00% | 0.02% | -0.01% | -0.02% | 0.03% | 0.07% | 0.03% | -0.02% | -0.34% | 0.02% | 0.27% | -0.21%
Class C | 0.00% | 0.00% | -0.01% | 0.00% | 0.01% | 0.05% | 0.00% | -0.30% | -0.03% | -0.01% | 0.08% | -0.11%
Class D | 0.00% | -0.03% | 0.02% | 0.05% | 0.17% | 0.03% | 0.05% | 0.47% | -0.23% | 0.09% | 0.24% | -0.30%
Class E | 0.01% | -0.04% | 0.02% |  |  |  | 0.18% | -0.09% | -0.09% | 0.02% | -0.21% | -0.82%
Class F | -0.01% | 0.07% | 0.00% | 0.04% | 0.01% | -0.12% | -0.08% | -0.33% | 0.11% | -0.13% | -0.11% | -0.33%
Overall | 0.00% | 0.00% | 0.01% | 0.02% | 0.04% | -0.03% | 0.03% | -0.05% | -0.13% | 0.00% | 0.08% | -0.32%
 | 0.00% | 0.01% | 0.00% | 0.02% | 0.02% | -0.06% | 0.03% | -0.04% | -0.12% | 0.00% | 0.10% | -0.30%
Enc T [%] | 103% |  |  | 102% |  |  | 101% |  |  | 100% |  | 
Dec T[%] | 99% |  |  | 101% |  |  | 106% |  |  | 104% |  | 

## Slide 9: Results with sub-block scan
Unified scan passes with diagonal scan in 4×4 sub-blocks (JCTVC-G323)
  5 scan passes on blocks of 4×4
  Sub-blocks for 16×16 and 32×32
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.02% | -0.23% | 0.02% | 0.13% | 0.19% | 0.64% |  |  | 
Class B | 0.08% | 0.09% | 0.11% | 0.08% | 0.13% | 0.06% | 0.11% | 0.04% | -0.13%
Class C | 0.01% | 0.01% | 0.02% | 0.02% | -0.13% | -0.10% | 0.06% | -0.10% | -0.09%
Class D | 0.01% | 0.02% | -0.03% | 0.07% | 0.16% | -0.13% | -0.02% | 0.58% | 0.50%
Class E | 0.00% | -0.08% | -0.05% |  |  |  | 0.17% | -1.32% | 0.51%
Class F | -0.01% | -0.05% | -0.06% | 0.02% | -0.17% | -0.16% | -0.19% | -0.27% | 0.01%
Overall | 0.02% | -0.03% | 0.01% | 0.06% | 0.04% | 0.06% | 0.02% | -0.15% | 0.13%