## Slide 1: JCTVC-G322 CE6.c: Harmonization of HE residual coding with non-square block transforms
Joel Sole, Rajan Joshi, Xianglin Wang, Marta Karczewicz

## Slide 2: Non-Square Blocks Transforms
NSQT & SDIP use non-square transforms
  Inter NSQT block sizes: 32×8, 8×32, 16×4, 4×16
  Intra SDIP block sizes: 32×8, 8×32, 32×2, 2×32, 16×4, 4×16, 8×2, 2×8
Issue: entropy coder only handles square blocks
  NSQT/SDIP introduce mappings between non-square transforms and ‘square-based’ entropy coder
    Extra computational complexity
    Neighborhood relation between coefficients is ‘broken’
Harmonization: modify entropy coding in HE to handle in the same way square and non-square blocks and without intermediate mapping
  Contexts for significance map
  Scans for NSQT blocks
  Last coefficient coding

## Slide 3: NSQT & SDIP Harmonization with CABAC
Significance map coding
  Context derivation for the non-square blocks similar to square blocks
    Blocks with same sizes share (transposed) contexts
  Small blocks (<= 64 coefficients) use contexts based on position
  Blocks 32×8 and 8×32 use the method for square blocks of 16×16 and 32×32
15 | 15 | 16 | 16 | 17 | 17 | 18 | 18 | 23 | 23 | 24 | 24 | 25 | 25 | 26 | 26
15 | 15 | 16 | 16 | 17 | 17 | 18 | 18 | 23 | 23 | 24 | 24 | 25 | 25 | 26 | 26
19 | 19 | 20 | 20 | 21 | 21 | 22 | 22 | 27 | 27 | 28 | 28 | 29 | 29 | 30 | 30
19 | 19 | 20 | 20 | 21 | 21 | 22 | 22 | 27 | 27 | 28 | 28 | 29 | 29 | 30 | 30
15 | 15 | 19 | 19
15 | 15 | 19 | 19
16 | 16 | 20 | 20
16 | 16 | 20 | 20
17 | 17 | 21 | 21
17 | 17 | 21 | 21
18 | 18 | 22 | 22
18 | 18 | 22 | 22
23 | 23 | 27 | 27
23 | 23 | 27 | 27
24 | 24 | 28 | 28
24 | 24 | 28 | 28
25 | 25 | 29 | 29
25 | 25 | 29 | 29
26 | 26 | 30 | 30
26 | 26 | 30 | 30
16×4 block
4×16 block

## Slide 4: NSQT & SDIP Harmonization with CABAC
Scans
  Removal of the mapping between non-square and square
  Horizontal, vertical, and fixed diagonal scan starting at the long side
Last significant position coding
  Context depends on the length of the side of the block
  One context for the sides of length 2
0 | 2 | 5 | 9 | 13 | 17 | 21 | 25 | 29 | 33 | 37 | 41 | 45 | 49 | 53 | 57
1 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60
3 | 7 | 11 | 15 | 19 | 23 | 27 | 31 | 35 | 39 | 43 | 47 | 51 | 55 | 59 | 62
6 | 10 | 14 | 18 | 22 | 26 | 30 | 34 | 38 | 42 | 46 | 50 | 54 | 58 | 61 | 63
0 | 2 | 5 | 9
1 | 4 | 8 | 13
3 | 7 | 12 | 17
6 | 11 | 16 | 21
10 | 15 | 20 | 25
14 | 19 | 24 | 29
18 | 23 | 28 | 33
22 | 27 | 32 | 37
26 | 31 | 36 | 41
30 | 35 | 40 | 45
34 | 39 | 44 | 49
38 | 43 | 48 | 53
42 | 47 | 52 | 57
46 | 51 | 56 | 60
50 | 55 | 59 | 62
54 | 58 | 61 | 63
16×4 block
4×16 block

## Slide 5: Performance on SDIP/NSQT (I)
Common conditions, HE configuration
Compared to HM4.0 + SDIP
  Cross-check: Huawei (JCTVC-G797)
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.15% | -0.29% | -0.51% | -0.08% | -0.31% | -0.42% |  |  | 
Class B | -0.15% | -0.15% | -0.26% | -0.10% | -0.04% | -0.21% | -0.11% | -0.19% | -0.03%
Class C | 0.01% | -0.06% | -0.09% | -0.01% | -0.11% | -0.10% | -0.04% | 0.00% | -0.08%
Class D | 0.02% | 0.02% | -0.04% | 0.00% | -0.25% | -0.34% | -0.03% | -0.15% | -0.56%
Class E | -0.14% | -0.54% | -0.36% |  |  |  | -0.14% | -0.92% | -0.96%
All | -0.08% | -0.19% | -0.25% | -0.05% | -0.17% | -0.27% | -0.08% | -0.27% | -0.35%
Enc T[%] | 98% |  |  | 100% |  |  | 100% |  | 
Dec T[%] | 100% |  |  | 99% |  |  | 100% |  | 

## Slide 6: Performance on NSQT (II)
Common conditions, HE configuration
Compared to HM4.0 (no SDIP)
  Cross-check: BBC (JCTVC-G890)
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.00% | 0.00% | 0.00% | -0.02% | -0.22% | -0.28% |  |  | 
Class B | 0.00% | 0.00% | 0.00% | -0.04% | -0.01% | -0.04% | -0.07% | -0.11% | -0.17%
Class C | 0.00% | 0.00% | 0.00% | -0.02% | -0.07% | 0.01% | -0.03% | -0.09% | -0.11%
Class D | 0.00% | 0.00% | 0.00% | 0.03% | -0.02% | 0.10% | 0.00% | 0.13% | -0.20%
Class E | 0.00% | 0.00% | 0.00% |  |  |  | -0.06% | 0.38% | 0.52%
All | 0.00% | 0.00% | 0.00% | -0.01% | -0.08% | -0.05% | -0.04% | 0.05% | -0.03%
Enc T[%] | 106% |  |  | 102% |  |  | 102% |  | 
Dec T[%] | 97% |  |  | 99% |  |  | 100% |  | 

## Slide 7: Conclusions
Extension of CABAC to NSQT/SDIP
Simplification of the current design
  Removal of the additional mapping
Slight improvement in performance

## Slide 8
Thank you!

## Slide 9: BD-rate (with class F and low delay P)
Proposal vs HM4.0 + SDIP
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | -0.15% | -0.29% | -0.51% | -0.08% | -0.31% | -0.42% |  |  |  |  |  | 
Class B | -0.15% | -0.15% | -0.26% | -0.10% | -0.04% | -0.21% | -0.11% | -0.19% | -0.03% | -0.07% | 0.03% | 0.01%
Class C | 0.01% | -0.06% | -0.09% | -0.01% | -0.11% | -0.10% | -0.04% | 0.00% | -0.08% | -0.09% | 0.21% | 0.09%
Class D | 0.02% | 0.02% | -0.04% | 0.00% | -0.25% | -0.34% | -0.03% | -0.15% | -0.56% | -0.01% | -0.27% | -0.03%
Class E | -0.14% | -0.54% | -0.36% |  |  |  | -0.14% | -0.92% | -0.96% | -0.05% | -0.67% | -0.83%
Class F | 0.27% | 0.33% | 0.52% | 0.11% | 0.21% | 0.18% | 0.19% | 0.36% | 0.75% | 0.07% | 0.31% | -0.08%
Overall | -0.02% | -0.10% | -0.12% | -0.02% | -0.10% | -0.18% | -0.02% | -0.15% | -0.13% | -0.03% | -0.04% | -0.12%
 | -0.02% | -0.10% | -0.12% | -0.02% | -0.07% | -0.14% | -0.03% | -0.17% | -0.12% | -0.03% | -0.03% | -0.16%
Enc T [%] | 98% |  |  | 100% |  |  | 100% |  |  | 102% |  | 
Dec T[%] | 100% |  |  | 99% |  |  | 100% |  |  | 100% |  | 

## Slide 10: BD-rate (with class F and low delay P)
Proposal vs HM4.0 (no SDIP)
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.00% | 0.00% | 0.00% | -0.02% | -0.22% | -0.28% |  |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | -0.04% | -0.01% | -0.04% | -0.07% | -0.11% | -0.17% | -0.03% | 0.02% | 0.06%
Class C | 0.00% | 0.00% | 0.00% | -0.02% | -0.07% | 0.01% | -0.03% | -0.09% | -0.11% | -0.07% | 0.03% | -0.20%
Class D | 0.00% | 0.00% | 0.00% | 0.03% | -0.02% | 0.10% | 0.00% | 0.13% | -0.20% | -0.03% | 0.24% | -0.15%
Class E | 0.00% | 0.00% | 0.00% |  |  |  | -0.06% | 0.38% | 0.52% | -0.02% | -0.23% | 0.13%
Class F | 0.00% | 0.00% | 0.00% | -0.05% | -0.14% | -0.19% | -0.29% | -0.53% | -0.07% | -0.19% | 0.30% | -0.09%
Overall | 0.00% | 0.00% | 0.00% | -0.02% | -0.09% | -0.08% | -0.09% | -0.07% | -0.04% | -0.07% | 0.08% | -0.05%
 | 0.00% | 0.00% | 0.00% | -0.02% | -0.09% | -0.08% | -0.09% | -0.13% | -0.08% | -0.07% | 0.06% | -0.11%
Enc T [%] | 106% |  |  | 102% |  |  | 102% |  |  | 101% |  | 
Dec T[%] | 97% |  |  | 99% |  |  | 100% |  |  | 100% |  |