## Slide 1: JCTVC-G323 Non-CE11: Diagonal sub-block scan for HE residual coding
Joel Sole, Rajan Joshi, Marta Karczewicz

## Slide 2: Large Diagonal Scans
HEVC has diagonal scans for HE residual data coding
Large diagonal scans (16×16 and 32×32)
  Hardware complexity is approximately double of 4×4 sub-block scans
    According to Sony’s JCTVC-F597
  SIMD implementation is difficult
subblock
coefficients

## Slide 3: Diagonal Sub-block Scan
Propose to use sub-block based scans (for 16×16 and 32×32)
  Diagonal scan within sub-blocks
  Diagonal scan across sub-blocks
Tested 3 sub-blocks of sizes
  4×4, 8×8 and 16×16
  With and without parallel contexts

## Slide 4: Parallel Context
Context for parallelization
  Avoid dependency of current context with previous coefficient
  Modified context for
    Top-left corner coefficient of a sub-block
    Coefficient above bottom-right corner of sub-block

## Slide 5: Performance
Common conditions, HE configurations
For sub-blocks sizes 4×4, 8×8 and 16×16
  Without parallel contexts
  With parallel contexts
  Cross-check: Sony (JCTVC-G302)
BD-rate | AI – HE | RA – HE | LB – HE
4×4 | -0.02% | 0.03% | 0.03%
8×8 | 0.12% | 0.08% | 0.03%
16×16 | 0.06% | 0.06% | 0.04%
BD-rate | AI – HE | RA – HE | LB – HE
4×4 | 0.02% | 0.06% | 0.05%
8×8 | 0.13% | 0.10% | 0.03%
16×16 | 0.06% | 0.06% | 0.02%

## Slide 6: Integration with Unified Scan Passes
4×4 sub-block scan for all residual data scan passes (JCTVC-G320)
Pass | Syntax element | CABAC mode | Current Scan | Unified
1 | significant_coeff_flag | Regular | Entire TU | 4×4 block
2 | abs_level_greater1_flag | Regular | 16 coeff sets | 4×4 block
3 | abs_level_greater2_flag | Regular | 16 coeff sets | 4×4 block
4 | coeff_sign_flag | Bypass | 16 coeff sets | 4×4 block
5 | coeff_abs_level_minus3 | Bypass | 16 coeff sets | 4×4 block
16 coefficient set scan
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.02% | -0.23% | 0.02% | 0.13% | 0.19% | 0.64% |  |  | 
Class B | 0.08% | 0.09% | 0.11% | 0.08% | 0.13% | 0.06% | 0.11% | 0.04% | -0.13%
Class C | 0.01% | 0.01% | 0.02% | 0.02% | -0.13% | -0.10% | 0.06% | -0.10% | -0.09%
Class D | 0.01% | 0.02% | -0.03% | 0.07% | 0.16% | -0.13% | -0.02% | 0.58% | 0.50%
Class E | 0.00% | -0.08% | -0.05% |  |  |  | 0.17% | -1.32% | 0.51%
Overall | 0.02% | -0.03% | 0.02% | 0.08% | 0.09% | 0.11% | 0.08% | -0.11% | 0.16%
Cross-check: LGE (JCTVC-G1021)

## Slide 7: Conclusions
Proposed sub-block based scan for large blocks
  Hardware and SIMD friendly
  Same encoding/decoding times
  Parallel contexts for significance map
Recommend to adopt one of the sub-block based scans for HE residual coding

## Slide 8
Thank you!

## Slide 9: BD-rate (with class F and low delay P)
4×4 sub-block
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | -0.07% | -0.31% | -0.11% | 0.09% | 0.29% | 0.47% |  |  |  |  |  | 
Class B | 0.03% | 0.02% | 0.04% | 0.04% | -0.03% | 0.07% | 0.06% | -0.05% | -0.11% | 0.06% | 0.05% | -0.11%
Class C | -0.02% | 0.00% | 0.00% | -0.04% | -0.11% | 0.09% | 0.01% | -0.05% | 0.05% | 0.04% | 0.21% | -0.05%
Class D | -0.01% | -0.04% | -0.07% | 0.00% | 0.02% | -0.32% | 0.00% | 0.07% | -0.32% | 0.04% | -0.42% | -0.61%
Class E | -0.06% | -0.15% | -0.17% |  |  |  | 0.07% | 0.04% | 0.40% | 0.05% | -0.19% | -0.19%
Class F | -0.03% | -0.02% | -0.04% | 0.01% | 0.07% | -0.16% | -0.16% | -0.47% | 0.12% | -0.03% | 0.02% | -0.30%
Overall | -0.02% | -0.08% | -0.05% | 0.02% | 0.04% | 0.03% | -0.01% | -0.10% | 0.00% | 0.03% | -0.06% | -0.25%
 | -0.02% | -0.09% | -0.08% | 0.02% | 0.02% | 0.01% | -0.01% | -0.10% | -0.01% | 0.03% | 0.01% | -0.26%
Enc T [%] | 101% |  |  | 99% |  |  | 102% |  |  | 98% |  | 
Dec T[%] | 99% |  |  | 99% |  |  | 100% |  |  | 98% |  | 

## Slide 10: BD-rate (with class F and low delay P)
8×8 sub-block
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.28% | 0.05% | 0.28% | 0.27% | 0.24% | 0.57% |  |  |  |  |  | 
Class B | 0.11% | 0.17% | 0.19% | 0.02% | 0.11% | 0.00% | 0.02% | 0.03% | -0.03% | 0.02% | 0.11% | 0.06%
Class C | -0.01% | 0.12% | 0.03% | 0.03% | -0.07% | 0.02% | 0.00% | -0.06% | 0.02% | 0.02% | -0.14% | -0.08%
Class D | 0.02% | 0.00% | -0.04% | 0.03% | 0.11% | -0.14% | -0.02% | 0.45% | 0.11% | 0.06% | 0.36% | -0.57%
Class E | 0.21% | 0.10% | 0.17% |  |  |  | 0.14% | -1.14% | -0.18% | 0.12% | -0.83% | -0.73%
Class F | -0.01% | -0.01% | -0.03% | 0.00% | 0.04% | -0.18% | -0.13% | -0.41% | -0.07% | -0.05% | -0.13% | 0.19%
Overall | 0.10% | 0.07% | 0.10% | 0.07% | 0.09% | 0.05% | 0.00% | -0.17% | -0.02% | 0.03% | -0.08% | -0.19%
 | 0.09% | 0.07% | 0.07% | 0.07% | 0.09% | 0.07% | 0.00% | -0.20% | -0.04% | 0.03% | -0.02% | -0.26%
Enc T [%] | 100% |  |  | 100% |  |  | 100% |  |  | 99% |  | 
Dec T[%] | 96% |  |  | 96% |  |  | 96% |  |  | 95% |  | 

## Slide 11: BD-rate (with class F and low delay P)
16×16 sub-block
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.20% | -0.24% | -0.10% | 0.27% | -0.41% | -0.88% |  |  |  |  |  | 
Class B | 0.02% | 0.08% | 0.08% | 0.00% | 0.02% | 0.05% | 0.03% | 0.00% | -0.03% | 0.02% | 0.00% | -0.17%
Class C | -0.02% | 0.02% | 0.01% | -0.03% | -0.11% | -0.07% | -0.01% | -0.09% | 0.10% | -0.02% | 0.04% | 0.10%
Class D | 0.00% | 0.03% | 0.01% | 0.02% | 0.32% | 0.20% | -0.03% | -0.08% | 0.16% | 0.03% | 0.14% | -0.38%
Class E | 0.11% | 0.27% | 0.22% |  |  |  | 0.22% | -0.14% | -0.11% | 0.10% | -0.46% | -0.08%
Class F | 0.01% | 0.01% | 0.08% | -0.05% | -0.01% | -0.18% | -0.10% | -0.33% | 0.03% | -0.07% | 0.10% | 0.00%
Overall | 0.05% | 0.02% | 0.04% | 0.04% | -0.04% | -0.17% | 0.01% | -0.12% | 0.03% | 0.01% | -0.01% | -0.11%
 | 0.05% | 0.04% | 0.07% | -0.02% | -0.05% | -0.14% | 0.01% | -0.13% | 0.04% | 0.01% | -0.03% | -0.13%
Enc T [%] | 101% |  |  | 99% |  |  | 100% |  |  | 100% |  | 
Dec T[%] | 97% |  |  | 95% |  |  | 95% |  |  | 94% |  | 

## Slide 12: BD-rate (with class F and low delay P)
4×4 sub-block, parallel contexts
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | -0.01% | -0.24% | -0.01% | 0.13% | 0.14% | 0.05% |  |  |  |  |  | 
Class B | 0.08% | 0.11% | 0.11% | 0.07% | 0.00% | 0.12% | 0.06% | 0.11% | -0.32% | 0.07% | 0.20% | -0.13%
Class C | 0.01% | 0.01% | 0.03% | -0.01% | -0.02% | -0.02% | 0.06% | 0.11% | 0.01% | 0.02% | -0.08% | -0.01%
Class D | 0.00% | 0.02% | 0.02% | 0.06% | -0.04% | -0.14% | -0.03% | -0.40% | -0.23% | 0.05% | 0.17% | -0.25%
Class E | 0.00% | -0.09% | -0.06% |  |  |  | 0.13% | -0.05% | 0.61% | 0.10% | 0.00% | 0.27%
Class F | -0.01% | -0.01% | 0.05% | -0.03% | 0.07% | -0.14% | -0.01% | -0.09% | -0.10% | -0.02% | 0.05% | -0.09%
Overall | 0.01% | -0.02% | 0.03% | 0.05% | 0.03% | -0.02% | 0.04% | -0.06% | -0.05% | 0.04% | 0.08% | -0.06%
 | 0.01% | -0.03% | 0.01% | 0.04% | 0.01% | -0.02% | 0.04% | -0.06% | -0.06% | 0.05% | 0.10% | -0.07%
Enc T [%] | 101% |  |  | 101% |  |  | 101% |  |  | 99% |  | 
Dec T[%] | 97% |  |  | 93% |  |  | 94% |  |  | 95% |  | 

## Slide 13: BD-rate (with class F and low delay P)
8×8 sub-block , parallel contexts
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.30% | 0.08% | 0.27% | 0.33% | 0.66% | 0.86% |  |  |  |  |  | 
Class B | 0.12% | 0.18% | 0.23% | 0.03% | 0.16% | 0.00% | 0.04% | 0.05% | -0.26% | 0.04% | 0.22% | 0.08%
Class C | 0.00% | 0.10% | 0.02% | 0.00% | -0.01% | 0.07% | 0.01% | 0.02% | -0.22% | 0.02% | 0.29% | -0.16%
Class D | 0.02% | 0.02% | -0.02% | 0.05% | 0.09% | 0.04% | -0.04% | 0.03% | -0.19% | 0.01% | 0.44% | -0.38%
Class E | 0.22% | 0.15% | 0.21% |  |  |  | 0.10% | -1.43% | -0.28% | 0.14% | -0.41% | -1.13%
Class F | 0.00% | -0.01% | 0.03% | 0.02% | 0.11% | -0.04% | -0.11% | -0.12% | 0.12% | 0.00% | 0.06% | -0.11%
Overall | 0.11% | 0.09% | 0.13% | 0.08% | 0.20% | 0.18% | 0.00% | -0.22% | -0.16% | 0.03% | 0.15% | -0.28%
 | 0.10% | 0.09% | 0.11% | 0.09% | 0.19% | 0.17% | 0.00% | -0.20% | -0.13% | 0.04% | 0.14% | -0.33%
Enc T [%] | 102% |  |  | 100% |  |  | 100% |  |  | 101% |  | 
Dec T[%] | 105% |  |  | 105% |  |  | 104% |  |  | 105% |  | 

## Slide 14: BD-rate (with class F and low delay P)
16×16 sub-block, parallel contexts
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | 0.20% | -0.20% | -0.13% | 0.29% | -0.33% | -0.54% |  |  |  |  |  | 
Class B | 0.02% | 0.06% | 0.08% | 0.00% | 0.05% | -0.10% | 0.02% | 0.22% | -0.26% | 0.00% | 0.06% | -0.34%
Class C | -0.02% | 0.02% | 0.01% | -0.04% | 0.01% | -0.11% | 0.00% | -0.09% | -0.09% | -0.01% | 0.17% | 0.19%
Class D | 0.01% | 0.02% | -0.01% | 0.01% | 0.15% | 0.02% | -0.02% | 0.18% | -0.05% | 0.04% | 0.33% | -0.61%
Class E | 0.11% | 0.30% | 0.24% |  |  |  | 0.11% | -0.14% | -0.13% | 0.11% | -0.29% | -0.74%
Class F | 0.00% | 0.04% | 0.13% | -0.05% | -0.05% | -0.16% | -0.05% | 0.12% | 0.37% | -0.11% | 0.06% | -0.24%
Overall | 0.05% | 0.03% | 0.05% | 0.04% | -0.03% | -0.18% | 0.01% | 0.07% | -0.04% | 0.00% | 0.08% | -0.33%
 | 0.05% | 0.04% | 0.08% | -0.02% | -0.05% | -0.13% | 0.01% | 0.05% | -0.03% | 0.00% | 0.11% | -0.37%
Enc T [%] | 101% |  |  | 102% |  |  | 103% |  |  | 99% |  | 
Dec T[%] | 98% |  |  | 95% |  |  | 96% |  |  | 94% |  |