## Slide 1: JCTVC-G326 Non-CE1.b: On the exponential memory decay probability update
Joel Sole, Marta Karczewicz

## Slide 2: Motivation
Probability update process based on a exponential memory decay function
  Instead of the next state look-up tables in HEVC
  Included in JCTVC-A114 and in JCTVC-F254 (part of CE1)
  JCTVC-F254 has two variants of it
    One model case
    Multi-parameter: twice of the memory requirements and operations of the one model
Focus on improving some issues found in one model case of JCTVC-F254
  Highly skewed probabilities
    Minimum probability of ~0.00003 (as opposed to ~0.019 in HEVC)
  Asymmetry of the estimator
    Symbol 0 and 1 updates are not equivalent
  Large LPS range table size
    Currently 512×64×9 bits = 288 Kb

## Slide 3: Technical Description
Changes to address the 3 issues
1) Introduction of an offset in the estimator to avoid highly skewed probabilities
  Set offset = 256
2) Removal of asymmetry by balancing the asymptotic probability values for symbol 0 and 1
With above changes, the exponential probability update functions become:
  If symbol = 0: iP0 -= ( ( iP0 - offset ) >> alfa )
  If symbol = 1: iP0 += ( ( ( 32767 - offset ) - iP0 ) >> alfa )
The initialization function is modified to avoid the highly skewed probabilities in the initial values:
  iP0 = 32768 - min( max( 1 + offset, c ), 32767 - offset )

## Slide 4: Technical Description
3) Reduction of LPS range table size from 512×64×9 bits to 64×4×4 bits
Quantize range in 64 intervals
Use 4 bit-shift operations to determine the range given the probability iP0
  qrange = (m_uiRange - 256) >> 2
  uiLPS = ( (iP0<< LPSshifts[qrange][0]) + (iP0<< LPSshifts[qrange][1]) + (iP0<< LPSShifts[qrange][2]) - (iP0<< LPSShifts[qrange][3])) >> 15
Multiplication of range*probability is cast to 4 bit-shifts
  LPSShifts table contains the shifts applied for each quantized range value
  Each of the shifts values can be expressed in 4 bits
  Shifts can be computed in parallel
LPS table size is reduced by a factor of 288
  Half the size of the current HEVC table

## Slide 5: Results
Common conditions, HE configuration
  Cross-check: RIM (JCTVC-G974)
BD-rate | All Intra HE |  |  | Random access HE |  |  | Low delay B HE |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.58% | -0.56% | -0.58% | -0.71% | -0.18% | 0.33% |  |  | 
Class B | -0.49% | -0.82% | -0.81% | -0.57% | -0.70% | -0.76% | -0.49% | -0.69% | -1.15%
Class C | -0.47% | -0.94% | -1.01% | -0.52% | -0.80% | -0.79% | -0.49% | -0.90% | -1.03%
Class D | -0.49% | -1.53% | -1.61% | -0.63% | -1.18% | -1.38% | -0.72% | -0.95% | -1.33%
Class E | -0.46% | -1.17% | -1.19% |  |  |  | -0.52% | -1.62% | -1.69%
All | -0.50% | -0.99% | -1.02% | -0.61% | -0.71% | -0.66% | -0.55% | -0.98% | -1.26%
Enc T[%] | 103% |  |  | 99% |  |  | 103% |  | 
Dec T[%] | 98% |  |  | 100% |  |  | 98% |  | 

## Slide 6: Conclusions
Clean-up of JCTVC-F254
  One model case
  Removal of the 288Kb table
BD-rate gains
BD-rate | AI – HE | RA – HE | LB – HE | LP – HE
Avg YUV | -0.63% | -0.63% | -0.69% | -0.62%

## Slide 7
Thank you!

## Slide 8: BD-rate (with class F and low delay P)
Common conditions, HE configuration
 | All Intra HE |  |  | Random Access HE |  |  | Low delay B HE |  |  | Low delay P HE |  | 
 | Y | U | V | Y | U | V | Y | U | V | Y | U | V
Class A | -0.58% | -0.56% | -0.58% | -0.71% | -0.18% | 0.33% |  |  |  |  |  | 
Class B | -0.49% | -0.82% | -0.81% | -0.57% | -0.70% | -0.76% | -0.49% | -0.69% | -1.15% | -0.49% | -0.39% | -0.62%
Class C | -0.47% | -0.94% | -1.01% | -0.52% | -0.80% | -0.79% | -0.49% | -0.90% | -1.03% | -0.46% | -0.58% | -0.77%
Class D | -0.49% | -1.53% | -1.61% | -0.63% | -1.18% | -1.38% | -0.72% | -0.95% | -1.33% | -0.55% | -0.77% | -0.96%
Class E | -0.46% | -1.17% | -1.19% |  |  |  | -0.52% | -1.62% | -1.69% | -0.62% | -1.88% | -1.94%
Class F | -0.33% | -0.43% | -0.30% | -0.40% | -0.33% | -0.45% | -0.43% | -0.71% | -0.01% | -0.32% | -0.19% | -0.17%
Overall | -0.47% | -0.89% | -0.90% | -0.57% | -0.64% | -0.62% | -0.53% | -0.93% | -1.01% | -0.48% | -0.69% | -0.83%
 | -0.47% | -0.89% | -0.89% | -0.55% | -0.63% | -0.60% | -0.52% | -0.91% | -0.96% | -0.48% | -0.62% | -0.82%
Enc T [%] | 103% |  |  | 99% |  |  | 103% |  |  | 98% |  | 
Dec T[%] | 98% |  |  | 100% |  |  | 98% |  |  | 101% |  |