## Slide 1: JCTVC-G328: Bit depth of output pictures
Ying Chen, Ye-Kui Wang, Xianglin Wang, In Suk Chong, and Marta Karczewicz

## Slide 2: Introduction
In the current HEVC WD, only the bit depth of decoded pictures is signaled, and the bit depth of output pictures is the same as the bit depth of the decoded pictures
If the desired output bit depth is lower than the bit depth of decoded pictures, further memory optimization can be achieved by signaling the target output bit depth, since not every decoded picture has to be stored in the buffer with a higher bit depth all the time
  For example, if the input source pictures are of 8-bit precision, and the decoded pictures are of 10-bit precision, while the ideal output bit precision may well be 8-bit precision
    In this case, if half of pictures are coded as non-reference pictures, storing the non-reference pictures in the DPB with 8-bit precision can save 10% DPB memory
    More DPB memory saving can be achieved if reference pictures marked as “unused for reference” are also stored with 8-bit precision

## Slide 3: Proposal – syntax
In addition to the bit depth of decoded pictures, the output bit depth is also signaled (through the delta between the two bit depth values)
The output bit depth shall be equal to or lower than the bit depth of the decoded pictures

## Slide 4: Proposal – process
If a decoded picture is a reference picture and is marked as “used for reference”, it is stored in the DPB with luma bit depth equal to BitDepthY and chorma bit depth equal to BitDepthC
Otherwise (the decoded picture is a non-reference picture or is marked as “unused for reference”), it is stored in the DPB with luma bit depth equal to BitDepthOutY and chorma bit depth equal to BitDepthOutC
When output a picture, the picture it is output with luma bit depth equal to BitDepthOutY and chorma bit depth equal to BitDepthOutC
  In case BitDepthOutY is less than BitDepthY, the luma value of a sample is right-shifted to be of BitDepthOutY bits. In case BitDepthOutC is less than BitDepthC, the chroma value of a sample is right-shifted to be of BitDepthOutC bits