## Slide 1: JCTVC-G334 On sequence parameter set and picture parameter set
Ye-Kui Wang, Ying Chen, Yunfei Zheng, Wei-Jung Chien

## Slide 2: This is a discussion document
Discusses some SPS and PPS syntax elements, including their
  Syntax element coding
  Value ranges
  Semantics

## Slide 3: pcm_bit_depth_luma_minus1 pcm_bit_depth_chroma_minus1
Currently coded using u(4)
Shall be smaller than BitDepthY and BitDepthC, respectively
Discussion: Should them be coded as deltas, using ue(v)?
Value ranges are currently missing
Discussion: Should PCMBitDepthY and PCMBitDepthC be both in the range of 8 to 14, same as BitDepthY and BitDepthC?

## Slide 4: log2_min_coding_block_size_minus3, log2_diff_max_min_coding_block_size
Define SCU size (Log2MinCUSize) and LCU size (Log2MaxCUSize)
Value ranges currently missing
Discussions
  Can SCU size be smaller than 16x16, e.g., equal to 8x8?
  Can SCU size be larger than 32x32?
  Would SCU and LCU sizes be level dependent?
  Can LCU size be as small as 8x8?
  Can LCU size be as big as 128x128?

## Slide 5: Value ranges of other SPS syntax elements
Discussion: What are the value ranges of the following syntax elements?
  log2_min_transform_block_size_minus2
  max_transform_hierarchy_depth_intra
  max_transform_hierarchy_depth_inter

## Slide 6: PPS flag to disable temporal MV predictor
Agreed at the previous meeting
Semantics and corresponding decoding process text unclear
Discussion
  The semantics (and other WD text using the flag) should not just apply for a particular picture referring to the PPS, but also for the following pictures in decoding order, which may or may not refer to this PPS, not to use any earlier pictures in decoding order for temporal MV prediction.
    In other words, if the flag is set to disable temporal MV prediction for picture A, then any picture C following picture A in decoding order shall not perform temporal MV prediction from any picture B before picture A in decoding order.
  Alternatively, this flag is defined as an SPS flag, then the above by default applies
    We think that this is better, because otherwise the parsing problem would be there anyway, and only disabling temporal MV predictor for some pictures can hardly solve the problem