## Slide 1: JCTVC-G336: Unified NAL unit header design for HEVC and its extensions
Ying Chen, Ye-Kui Wang, and Marta Karczewicz

## Slide 2: Introduction
H.264/AVC and its extensions
  Non-scalable bitstream has an 1-byte (8-bit) NAL unit header
  SVC: 3-byte NAL unit header extension
  MVC: 3-byte NAL unit header extension
Drawbacks of such a design
  In each AVC extension, a different prefix NAL unit has to be used to carry information that is in the SVC\MVC NAL unit header, for the base layer
  In various situations, a scalable bitstream doesn’t have any variation in one or more of the scalability or view dimensions, thus redundant bits are always sent for each VCL NAL unit:
    The syntax element related to that dimension still has to be signaled with a fixed maximum possible length
      For example, quality_id has to use 4 bits even the bitstream just uses only 2-layer spatial scalability.
    SVC and MVC might be jointly supported in one HEVC amendment, wherein a NAL unit header might cost 6 bytes

## Slide 3: Proposal
Motivation
  High level syntax hooks in the “base” HEVC design for its potential extensions
  Efficient NAL unit header design in a unified fashion
Proposal
  In the NAL unit header, a set of syntax elements are signaled, including e.g., different scalable identifiers or view identifier
    Each may have a variable length in different coded video sequence and the length can be zero.

## Slide 4: Proposal
A NAL unit header map to specify the layout of NAL unit header fields
  Each scalability or view dimension corresponding to a syntax element in the NAL unit header has its length specified
    such as spatial scalability, temporal scalability, quality scalability or view
  Compact representation in the NAL unit header
    Not the value, but the index can be signaled if
      Only M possible values for a syntax element,
      Specific values can take N bits, and
      The length, i.e., 1 << Ceil(log2(M+1)), can be much smaller than N
    For example, instead of signaling a 10-bit view_id, only a 2-bit view_idx is signaled in the NAL unit header, if
      A selected set of views have four instances of view_id values 45, 50, 55, 60
    A view index to ID table is signaled

## Slide 5: Examples (1/2)
A scalable bitstream with QVGA to VGA spatial scalability while each dependency layer has 3 temporal layers. 3 bits
  priority_id: not present
  temporal_id: 2 bits
  dependency_id: 1 bit
  quality_id: not present
  view_idx: not present
A stereoscopic bitstream with multiple (2) spatial layers for each view, each of which has up to 3 temporal layers. 4 bits
  priority_id: not present
  temparal_id: 2 bits
  dependency_id: 1 bit
  quality_id: not present
  view_idx: 1 bit

## Slide 6: Examples (2/2)
A multiview bitstream contains 8 views, each has two quality layers, hierarchical B prediction structure with a GOP Size 16 (thus 4 temporal layers). 7 bits
  priority_id: not present
  temparal_id: 3 bits
  dependency_id: not present
  quality_id: 1 bit
  view_idx: 3 bits

## Slide 7: Syntax
Summary
  NAL unit header map Parameter Set (NPS)
    Signaling how many bits are used to signal each syntax element
    Including also the view index to ID table
    It is extensible for more syntax elements
  The ID of a NPS is included in the SPS
  Fixed length NAL unit header for a coded video sequence
    NPS and SPS always have 1-byte NAL unit header