## Slide 1: Chroma intra prediction based on residual luma samples
K. Kawamura, T. Yoshino, H. Kato, S. Naito
KDDI Corp. (KDDI R&D Laboratories Inc.)
<number>

## Slide 2: Overview
New intra prediction mode for chroma
  Based on residual luma samples and linear model
    Similar to chroma_from_luma
  BD-bitrate -0.1%, -4.1%, -4.7%, -0.7% (AI/HE)
  BD-bitrate -0.1%, -3.5%, -4.0%, -0.6% (AI/LC)
  Additional run-time is 1.6% / 1.4% (HE/LC)
    Decreased from 6.1%(AI/HE) and 7.6%(AI/LC) on HM3.0.
Cross-checked by NTT (JCTVC-G069) and Intel (JCTVC-G911)
<number>

## Slide 3: Introduction
LM mode (chroma intra prediction) in HM4.0
  uses reconstructed luma samples
  Parameters  and  are derived from adjacent blocks
Prediction performance by LM mode might be degraded especially for object boundary regions
  Correlation between luma and chroma is varying
<number>
Notes: <number>

## Slide 4: Motivation & Solution
Motivation
  Reduce two redundancy simultaneously
    Adjacent pixels’ correlation and inter-channel correlation
  Improve inter-channel prediction performance
Proposed solution: RM mode
  Inter-channel residual prediction between luma and chroma as an additional mode
  Chroma is predicted twice.
<number>

## Slide 5: Proposed method (RM mode)
Luma intra prediction in HM4.0 (no change)
Chroma intra prediction with three steps
  Chroma intra prediction with mode 0 (derived from luma) in HM4.0
  Chroma intra residual prediction with  derived on the encoder side
  Residual samples from above two steps are transformed, quantized, and coded.
<number>

## Slide 6: Comparison between LM and RM
Prediction target
  LM: Base-band samples
  RM: Intra residual samples
Parameters in the model
  LM: Not coded and derived from adjacent blocks
  RM:  is derived at the encoder side and coded. Syntax is then changed.
Above two modes are complementary.
<number>

## Slide 7: Experimental Results 1
Implemented on HM4.0
Summary of the results for all intra
<number>
YUV BD-bitrate is derived from bit-rate and weighted PSNR [JCTVC-F386].

## Slide 8: Experimental Results 2
<number>

## Slide 9: Related contributions
JCTVC-G173 Cross-channel intra chroma residual prediction (Intel)
  Approach is similar but target is different.
  Coding gain is mostly additive JCTVC-G1009 A joint contribution on the coding tools of residual prediction for intra chroma prediction (Intel and KDDI).
<number>

## Slide 10: Conclusion
New intra prediction mode for chroma
  BD-bitrate -0.1%, -4.1%, -4.7%, -0.7% (AI/HE)
  BD-bitrate -0.1%, -3.5%, -4.0%, -0.6% (AI/LC)
  Additional run-time is negligible.
  Additive relation with other chroma tools
We propose to adopt the RM mode into the “CE6: Intra Coding Improvements.”
<number>
Notes:   Further significant gain will be obtained for 4:4:4 contents .
<number>