## Slide 1: Modification of angular intra prediction
Shohei Matsuo, Seishi Takamura and Hirohisa Jozawa
NTT Cyber Space Laboratories
NTT Corporation, Japan
JCTVC-G350

## Slide 2: Summary
Modification for angular intra prediction
  >2-tap interpolation is applied to generate reference pixels
Simulation results
  For AI:
    Overall average (HE): 0.4% (Y), 0.5% (U), 0.5% (V)
    Overall average (LC): 0.5% (Y), 0.6% (U), 0.6% (V)
    Max (BasketballDrill): 1.9% (Y), 1.8% (U), 2.2% (V)
    EncTime: 100.8% (HE), 101.7% (LC)
    Dectime: 100.3% (HE), 100.7% (LC)
  Works OK with inter, too
  Cross-checked by KDDI (JCTVC-G348)

## Slide 3: Basic idea
Angular intra prediction
  Conventional (HM4.0): 2-tap interpolation is applied
  Proposal: >2-tap interpolation is applied to small blocks
Block to be predicted
A1,0
P1,0
P0,0
Decoded block
A0,0
A-1,0
A-1,1
A2,0

## Slide 4: Encoding/decoding algorithm
Block size mxm?
>2-tap
interpolation
2-tap interpolation
(HM4.0)
Yes
No
Generation of reference pixels

## Slide 5: Simulation results
Conditions
  Interpolation filter: 4-tap DCT-IF with s=0.07 (s defined in D344)
  Block size threshold: m=16
Results

## Slide 6: Simulation results (inter)
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.1% | -0.2% | 0.0% | -0.1% | 0.1%
Class B | -0.2% | -0.3% | -0.4% | -0.2% | -0.5% | -0.5%
Class C | -0.2% | -0.4% | -0.3% | -0.4% | -0.7% | -0.5%
Class D | -0.1% | -0.4% | -0.4% | -0.3% | -0.5% | -0.3%
Overall | -0.1% | -0.3% | -0.3% | -0.2% | -0.4% | -0.3%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
Class B | 0.0% | -0.1% | -0.5% | -0.1% | 0.0% | 0.1%
Class C | -0.1% | -0.3% | -0.3% | -0.2% | -0.2% | -0.5%
Class D | -0.1% | -0.2% | 0.5% | -0.1% | -0.1% | -0.5%
Class E | 0.0% | -0.9% | -0.2% | -0.2% | 0.1% | -0.4%
Overall | -0.1% | -0.3% | -0.1% | -0.1% | 0.0% | -0.3%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class B | 0.0% | -0.1% | -0.2% | -0.1% | -0.1% | -0.2%
Class C | -0.1% | -0.3% | -0.4% | -0.2% | -0.2% | 0.0%
Class D | -0.1% | -0.1% | -0.2% | -0.1% | -0.5% | -0.6%
Class E | 0.0% | -0.2% | -1.2% | -0.1% | -0.8% | -0.7%
Overall | -0.1% | -0.2% | -0.4% | -0.1% | -0.3% | -0.4%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 

## Slide 7: Conclusion
Modified angular prediction
  Conventional 2-tap filter for larger blocks
  4-tap filter for smaller blocks
Considerable gain with negligible complexity
  For intra,
    Overall average (HE): 0.4% (Y), 0.5% (U), 0.5% (V)
    Overall average (LC): 0.5% (Y), 0.6% (U), 0.6% (V)
    Max (BasketballDrill): 1.9% (Y), 1.8% (U), 2.2% (V)
    EncTime: 100.8% (HE), 101.7% (LC)
    DecTime: 100.3% (HE), 100.7% (LC)
  Works OK with inter, too
Suggestion: Proposal should be incorporated into HEVC
Cross-checked by
KDDI (JCTVC-G348)

## Slide 8
Thank you, questions?

## Slide 9: Interpolation filter
Interpolation filters are derived by using the following equations.
  s denotes a smoothing parameter (D344)
  When s=0, the DCT-IF employed in HM4.0 is applied

## Slide 10: Generation of reference pixels
Conventional
  equation (8-44) described in Sec.8.3.3.1.6 of WD (F803_d5)
Proposed

## Slide 11: Intra prediction angle definition

## Slide 12: Additional results

## Slide 13: Examples of smoothed coefficients
// 0.25-pel, sigma=0
{-1, 4, -10, 57, 19, -7, 3, -1};
// 0.25-pel, sigma=0.01
{-1, 4, -9, 55, 18, -6, 3, 0};
// 0.25-pel, sigma=0.02
{-1, 3, -8, 54, 19, -6, 3, 0};
// 0.25-pel, sigma=0.03
{-1, 3, -7, 54, 19, -6, 2, 0};
// 0.25-pel, sigma=0.04
{-1, 3, -6, 52, 19, -5, 2, 0};
// 0.25-pel, sigma=0.05
{0, 3, -6, 51, 19, -5, 2, 0};
// 0.25-pel, sigma=0.06
{0, 3, -5, 49, 19, -4, 2, 0};
// 0.25-pel, sigma=0.07
{0, 2, -4, 49, 19, -4, 2, 0};
// 0.25-pel, sigma=0.08
{0, 2, -3, 48, 19, -4, 2, 0};
// 0.25-pel, sigma=0.09
{0, 2, -2, 46, 19, -3, 2, 0};
// 0.25-pel, sigma=0.1
{0, 2, -2, 46, 20, -3, 1, 0};
// 0.5-pel, sigma=0
{-1, 5, -11, 39, 39, -11, 5, -1};
// 0.5-pel, sigma=0.01
{-1, 5, -11, 39, 39, -11, 5, -1};
// 0.5-pel, sigma=0.02
{-1, 4, -10, 39, 39, -10, 4, -1};
// 0.5-pel, sigma=0.03
{-1, 4, -9, 38, 38, -9, 4, -1};
// 0.5-pel, sigma=0.04
{-1, 4, -9, 38, 38, -9, 4, -1};
// 0.5-pel, sigma=0.05
{-1, 4, -8, 37, 37, -8, 4, -1};
// 0.5-pel, sigma=0.06
{-1, 3, -7, 37, 37, -7, 3, -1};
// 0.5-pel, sigma=0.07
{-1, 3, -7, 37, 37, -7, 3, -1};
// 0.5-pel, sigma=0.08
{-1, 3, -6, 36, 36, -6, 3, -1};
// 0.5-pel, sigma=0.09
{0, 3, -5, 34, 34, -5, 3, 0};
// 0.5-pel, sigma=0.1
{0, 2, -5, 35, 35, -5, 2, 0};