## Slide 1: Parameterization of Default Quantization Matrices
Ehsan Maani, Munsi Haque, Ali Tabatabai
Proposal
JCTVC-G352
Nov 15 2011

## Slide 2: Outline
Default quantization matrices
Parameterization
  Storage of parameters vs. matrices
Conclusions
<number>
JCTVC-G351

## Slide 3: Default Quantization Matrices
Quantization matrices allow unequal quantization across different frequencies
  Each DCT coefficient can be quantized differently
In case, a quantization matrix is not provided, the default will be used by encoder/decoder
Default quantization matrices are stored in the memory at the decoder (and perhaps the encoder)
<number>
JCTVC-G352

## Slide 4: Parameterization of default matrices
Proposal:
  Instead of storing default quantization matrices, store parameters that can efficiently represent those matrices
Extensive subjective quality evaluations are needed to find a set of quantization matrices for HEVC
  Then, the proposed parameterization can result in matrices close to those with no visual quality impact but far more efficient for compact storage
<number>
JCTVC-G352

## Slide 5: Parameterization of default matrices
<number>
JCTVC-G352
4-parameter symmetric quadratic model (a, b, c, d):
denotes the quantization scale value at location (i,j)
where is the size of the transform
represents the scaling factor for bit accuracy of the model
Least Squares Fitting is used to derive parameters from known metrices

## Slide 6: Parameterization of AVC’s matrices
<number>
JCTVC-G352
AVC Intra | Parametric | Error
6 13 20 28 13 20 28 32 20 28 32 37 28 32 37 42 | 6 13 21 27 13 20 27 33 21 27 32 37 27 33 37 42 | 0 0 -1 1 0 0 1 -1 -1 1 0 0 1 -1 0 0
AVC Inter | Parametric | Error
10 14 20 24 14 20 24 27 20 24 27 30 24 27 30 34 | 10 15 20 24 15 19 24 27 20 24 27 31 24 27 31 33 | 0 -1 0 0 -1 1 0 0 0 0 0 -1 0 0 -1 1
AVC Intra | Parametric | Error
6 10 13 16 18 23 25 27 10 13 16 18 23 25 27 29 13 16 18 23 25 27 29 31 16 18 23 25 27 29 31 33 18 23 25 27 29 31 33 36 23 25 27 29 31 33 36 38 25 27 29 31 33 36 38 40 27 29 31 33 36 38 40 42 | 7 10 13 16 19 22 24 27 10 13 16 19 22 24 27 29 13 16 19 22 24 27 29 32 16 19 22 24 27 29 32 34 19 22 24 27 29 32 34 36 22 24 27 29 32 34 36 38 24 27 29 32 34 36 38 40 27 29 32 34 36 38 40 41 | -1 0 0 0 -1 1 1 0 0 0 0 -1 1 1 0 0 0 0 -1 1 1 0 0 -1 0 -1 1 1 0 0 -1 -1 -1 1 1 0 0 -1 -1 0 1 1 0 0 -1 -1 0 0 1 0 0 -1 -1 0 0 0 0 0 -1 -1 0 0 0 1
AVC Inter | Parametric | Error
9 13 15 17 19 21 22 24 13 15 17 19 21 22 24 25 15 17 19 21 22 24 25 27 17 19 21 22 24 25 27 28 19 21 22 24 25 27 28 30 21 22 24 25 27 28 30 32 22 24 25 27 28 30 32 33 24 25 27 28 30 32 33 35 | 11 13 15 17 19 20 22 24 13 15 17 19 20 22 24 25 15 17 19 20 22 24 25 27 17 19 20 22 24 26 27 29 19 20 22 24 26 27 29 30 20 22 24 26 27 29 30 32 22 24 25 27 29 30 32 33 24 25 27 29 30 32 33 34 | -2 0 0 0 0 1 0 0 0 0 0 0 1 0 0 0 0 0 0 1 0 0 0 0 0 0 1 0 0 -1 0 -1 0 1 0 0 -1 0 -1 0 1 0 0 -1 0 -1 0 0 0 0 0 0 -1 0 0 0 0 0 0 -1 0 0 0 1
4x4
8x8

## Slide 7: Parameterization and extension of AVC’s matrices
After parameterization, scaling can be done to generate matrices for 16x16 and 32x32 from 8x8
The results, using AVC’s matrices:
As seen in the previous page error is minimal and will have negligible impact on visual quality
<number>
JCTVC-G352
Transform Size | Slice Type | Parameters (a, b, c, d)
4x4 | Intra | -256, -901, 8264, 5652
8x8 | Intra | -56, -127, 3364, 6898
16x16 | Intra | -14, -32, 1682, 6898
32x32 | Intra | -4, -8, 841, 6898
4x4 | Inter | -192, -563, 5440, 9907
8x8 | Inter | -28, -50, 2070, 11260
16x16 | Inter | -7, -13, 1035, 11260
32x32 | Inter | -2, -3, 517, 11260

## Slide 8: Storage of default matrices
Default quantization matrices in HEVC (only square matrices)
  Total number of elements:
Parameterization can reduce this number to 8x4x3=96.
  Still, each matrix is represented separately and independently, and can easily be changed in the future
<number>
JCTVC-G352
Y/U/V
Inter/Intra

## Slide 9: Conclusions
Explicit representation of quantization matrices in HEVC requires large memory
The difference between parameterized and original matrices are small for most existing quantization matrices (especially AVC)
  The difference is too small to have any visible impact on visual quality
Each matrix is independently represented and therefore can be easily changed in the future if needed w/o changing the calculation logic
  This is not the case if some of the matrices are derived from others
<number>
JCTVC-G352

## Slide 10
Notes: <number>