## Slide 1: G358: New Modes for Chroma Intra Prediction
Xingyu Zhang, Oscar C. Au,
Jingjing Dai, Feng Zou, Chao Pang, Xing Wen

## Slide 2: JCTVC-G358
Outline
1. Overview
2. Proposed Modes LML and LMA
3. Implementation & Advantages
    Scheme 1 (8 modes)
    Scheme 2 (6 modes)
    Scheme 3 (4 modes)

## Slide 3
Chroma Intra Prediction Mode | Codeword | IntraPredMode |  |  |  | 
 |  | 0 | 1 | 2 | 3 | X ( 0 <= X < 35 )
DM | 0 | 0 | 1 | 2 | 3 | X
LM | 10 | LM | LM | LM | LM | LM
Planar | 110 | 7 | 0 | 0 | 0 | 0
Vertical | 1110 | 1 | 7 | 1 | 1 | 1
Horizontal | 11110 | 2 | 2 | 7 | 2 | 2
DC | 11111 | 3 | 3 | 3 | 7 | 3
JCTVC-G358
Overview
6 modes are used in chroma intra prediction:
DM, LM, Planar, Vertical, Horizontal, and DC.
When one of the last four modes is the same with DM, Ver+8 will replace it. (5 tables)

## Slide 4: JCTVC-G358
LM mode: Using a linear model to predict Chroma from Luma.
Parameters alpha and beta are very important for prediction correctness.
Fig. 1 2N neighboring samples are used for parameters derivation in LM mode (L shape template)
Overview

## Slide 5: JCTVC-G358
Analysis
However, hints of B can be found in the left lower portion of the neighborhood.
A
B
In the example, no training samples in the L-shape neighborhood can give any hint of object B.
Thus, object B cannot be well predicted by LM mode.

## Slide 6: JCTVC-G358
Proposed Modes: LML and LMA
Fig. 2 In total, 2N neighboring samples are used for parameters derivation in LML mode
Fig. 3 In total, 2N neighboring samples are used for parameters derivation in LMA mode
(Essentially same as LM except training samples taken at different locations)

## Slide 7: JCTVC-G358
Mode | Codeword
DM | 0
LM | 100
LML | 1010
LMA | 1011
Planar | 110
Vert | 1110
Hori | 11110
DC | 11111
Implementation
Scheme 1 (8 modes)
Mode | Codeword
DM | 0
LM | 10
LML | 110
LMA | 1110
Verti | 11110
DC | 11111
Scheme 2 (4+2 modes)
Mode | Codeword
DM | 0
LM | 10
LML | 110
LMA | 111
Scheme 3 (4 modes)
No new syntax in all 3 schemes

## Slide 8: JCTVC-G358
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -8.8% | -9.6% | -0.1% | -9.3% | -10.1%
Class B | -0.1% | -2.6% | -2.1% | -0.1% | -2.7% | -2.2%
Class C | -0.2% | -2.2% | -2.7% | -0.1% | -2.1% | -2.7%
Class D | -0.1% | -1.7% | -1.7% | -0.1% | -2.0% | -2.1%
Class E | -0.1% | -1.1% | -1.3% | 0.0% | -1.8% | -1.8%
Class F | -0.3% | -2.4% | -3.0% | -0.2% | -2.1% | -2.5%
Overall (Without Class F ) | -0.1% | -3.4% | -3.5% | -0.1% | -3.6% | -3.8%
Overall (With Class F ) | -0.2% | -3.2% | -3.4% | -0.1% | -3.4% | -3.6%
Enc Time[%] | 106% |  |  | 105% |  | 
Dec Time[%] | 100% |  |  | 98% |  | 
Implementation
Scheme 1 (8 modes)
Mode | Codeword
DM | 0
LM | 100
LML | 1010
LMA | 1011
Planar | 110
Vert | 1110
Hori | 11110
DC | 11111

## Slide 9: JCTVC-G358
DM | LM | LML | LMA | Planar | VER | HOR | DC | VER+8 (not DM)
33.8% | 15.1% | 13.0% | 12.5% | 8.3% | 5% | 4.7% | 4.8% | 2.8%
Stats of Chroma Mode selection
Chart: 
| DM | LM | LML | LMA | Planar | Vertical | Hori | DC | Ver+8
Mode Selection percentage (%) | 33.8 | 15.1 | 13 | 12.5 | 8.3 | 5 | 4.7 | 4.8 | 2.8
74.4%

## Slide 10: JCTVC-G358
Test | Intra-HE |  |  |  |  | Intra-LC |  |  |  | 
 | Y BD-Rate (%) | U BD-Rate (%) | V BD-Rate (%) | Enc Time (%) | Dec Time (%) | Y BD-Rate (%) | U BD-Rate (%) | V BD-Rate (%) | Enc Time (%) | Dec Time (%)
1(P+D) | -0.1% | -3.3% | -3.4% | 101 | 99 | -0.1% | -4.2% | -4.2% | 99 | 98
2(P+H) | -0.1% | -3.2% | -3.4% | 100 | 98 | -0.2% | -4.1% | -4.1% | 97 | 97
3(P+V) | -0.1% | -3.2% | -3.4% | 101 | 101 | -0.2% | -4.1% | -4.1% | 97 | 99
4(H+D) | -0.1% | -3.4% | -3.5% | 99 | 99 | -0.1% | -4.1% | -4.0% | 96 | 99
5(H+V) | -0.1% | -3.4% | -3.5% | 100 | 101 | -0.1% | -4.0% | -3.9% | 96 | 98
6(V+D) | -0.1% | -3.4% | -3.6% | 100 | 100 | -0.1% | -4.1% | -4.1% | 96 | 98
Simulation results of different combinations when 6 modes are kept (Without Class F)
(P=Planar, D=DC, H=Horizontal, V=Vertical)
Implementation
Scheme 2: 4+2 modes: DM, LM, LML, LMA + two more modes (vertical and DC)

## Slide 11: JCTVC-G358
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -9.0% | -9.7% | -0.2% | -10.9% | -11.0%
Class B | -0.1% | -2.4% | -1.9% | -0.1% | -2.9% | -2.1%
Class C | 0.0% | -1.9% | -2.3% | -0.1% | -1.8% | -2.2%
Class D | 0.0% | -1.5% | -1.6% | 0.1% | -1.5% | -1.4%
Class E | -0.1% | -1.5% | -1.5% | 0.0% | -2.3% | -2.0%
Class F | -0.2% | -2.4% | -2.8% | -0.2% | -2.1% | -2.6%
Overall (Without Class F ) | -0.1% | -3.3% | -3.4% | -0.1% | -3.9% | -3.7%
Overall (With Class F ) | -0.1% | -3.1% | -3.3% | -0.1% | -3.6% | -3.5%
Enc Time[%] | 94% |  |  | 92% |  | 
Dec Time[%] | 97% |  |  | 99% |  | 
Implementation
Scheme 3 (4 modes)
Mode | Codeword
DM | 0
LM | 10
LML | 110
LMA | 111

## Slide 12: JCTVC-G358
Propose to adopt one of 3 schemes in HM
Good RD performance
Simplification of chroma mode derivation table. (HM4.0 - 5 tables; Scheme1 – 5 tables,
Scheme 2 – 3 tables, Scheme3 - 1 table )
Complexity of LMA and LML similar to that of LM
No new syntax
Test | Intra-HE |  |  |  |  | Intra-LC |  |  |  | 
 | Y BD-Rate (%) | U BD-Rate (%) | V BD-Rate (%) | Enc Time (%) | Dec Time (%) | Y BD-Rate (%) | U BD-Rate (%) | V BD-Rate (%) | Enc Time (%) | Dec Time (%)
Scheme 1 | -0.1% | -3.4% | -3.5% | 106 | 100 | -0.1% | -3.6% | -3.8% | 105 | 98
Scheme 2 | -0.1% | -3.4% | -3.6% | 100 | 100 | -0.1% | -4.1% | -4.1% | 96 | 98
Scheme 3 | -0.1% | -3.3% | -3.4% | 94 | 97 | -0.1% | -3.9% | -3.7% | 92 | 99

## Slide 13: Thank you

## Slide 14: JCTVC-G358 Appendix
Scheme 3 combined with G173
Only DM mode uses cross-channel prediction proposed by G173, details are reported in G1024.
Without Class F | All Intra HE |  |  | All Intra LC |  | 
Overall | Y | U | V | Y | U | V
G173 | -0.3% | -1.0% | -2.9% | -0.3% | -0.6% | -3.5%
G358 (scheme 3) | -0.1% | -3.3% | -3.4% | -0.1% | -3.9% | -3.7%
G173+G358 | -0.4% | -3.9% | -5.7% | -0.3% | -4.1% | -6.3%
With Class F | All Intra HE |  |  | All Intra LC |  | 
Overall | Y | U | V | Y | U | V
G173 | -0.4% | -1.1% | -2.7% | -0.3% | -0.7% | -3.3%
G358 (scheme 3) | -0.1% | -3.1% | -3.3% | -0.1% | -3.6% | -3.5%
G173+G358 | -0.5% | -3.7% | -5.5% | -0.4% | -3.9% | -6.0%