## Slide 1: JCTVC-G360 CE5: Redundancy removal for Run-mode in CAVLC
Jun Xu, Ali Tabatabai
SONY

## Slide 2: Outline
Introduction
Proposed solutions & results
Conclusion

## Slide 3: Introduction
CAVLC for transform coefficients in HM4.0
  Last non-zero position
  Run-mode
  Level-mode
Current HM4.0 technology
  Run-mode employs various VLC tables
  Index 0 VLC table is unary-like
  The maximal code number can be derived based on “maxrun”.
    Redundancy for unary codes in run-mode for “maxrun”.
codenumber | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Bit length | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 9 | 9

## Slide 4: Proposals
Solutions
  Use truncated unary code to replace index 0 VLC table
Implementations
  Identify where index 0 VLC table is used
    const UInt g_auiVlcTable8x8Inter[29] = {8,0,0,5,5,5,5,5,5,5,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,3};
    const UInt g_auiVlcTable8x8Intra[29] = {8,0,0,5,5,5,5,5,5,5,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,6,3};
    const UInt g_auiVlcTable16x16Intra[29] = {8,0,0,0,0,5,5,5,5,5,5,5,5,5,5,5,5,5,1,1,1,1,1,1,1,1,1,1,2};
    const UInt g_auiVlcTable16x16Inter[29] = {8,0,1,1,1,1,2,2,2,2,2,2,2,6,6,6,6,6,6,3,3,3,3,3,3,3,3,3,3};
  Replace with truncated unary codes
    Void TEncCavlc::xWriteUnaryMaxSymbol( UInt uiSymbol, UInt uiMaxSymbol )
    Void TDecCavlc::xReadUnaryMaxSymbol( UInt& ruiSymbol, UInt uiMaxSymbol )
    uiMaxSymbol is derived by maxrun

## Slide 5: Results
Cross-check by Samsung, JCTVC-G786
 | All Intra LC |  | 
 | Y | U | V
Class A | -0.1% | 0.0% | 0.0%
Class B | -0.1% | -0.1% | -0.1%
Class C | -0.1% | -0.1% | -0.1%
Class D | -0.1% | -0.1% | -0.1%
Class E | -0.1% | -0.1% | -0.1%
Overall | -0.1% | -0.1% | -0.1%
 | -0.1% | -0.1% | -0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 99% |  | 
 | Random Access LC |  | 
 | Y | U | V
Class A | -0.1% | 0.0% | 0.2%
Class B | -0.1% | -0.1% | 0.0%
Class C | -0.1% | -0.2% | -0.1%
Class D | -0.1% | -0.2% | 0.3%
Class E |  |  | 
Overall | -0.1% | -0.1% | 0.1%
 | -0.1% | -0.1% | 0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
 | Low delay B LC |  | 
 | Y | U | V
Class A |  |  | 
Class B | -0.1% | 0.1% | 0.3%
Class C | -0.1% | 0.0% | -0.3%
Class D | -0.1% | 0.1% | -0.2%
Class E | -0.1% | 0.0% | 0.0%
Overall | -0.1% | 0.0% | 0.0%
 | -0.1% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 99% |  | 

## Slide 6: Conclusion
Presented solutions to remove redundancy of run-mode coding
0.1% BD-rate savings observed, no complexity.
Propose to adopt in HM5.0