## Slide 1: JCTVC-G362 Non-CE4: Efficient binarization of delta_QP in CABAC with signaling of Max and Min QP
Jun Xu, Kenji Kondo, Kazushi Sato, Ali Tabatabai
SONY

## Slide 2: Outline
Introduction
Proposed solutions & results
Conclusion

## Slide 3: Introduction
JCTVC-F174/JCTVC-G462 proposed to signal Max and Min QP of a slice in the slice header. It was further studied in CE4 1.2.a.
  Based on [minQP, maxQP] and predicted QP (refQP), the possible range of delta_QP can be determined.
  Adaptive code index mapping table for mapping delta_QP to codeword index is designed.
  Truncated unary code with maximum value for binarization of the codeword index in CABAC

## Slide 4: Proposals
Solutions
  Use maxQP, minQP and refQP to remove redundancy in sign bits by sending absolute values first.
Algorithm
  If delta_QP==0,
  send flag 0.
  Else
  Send flag 1.
  AbsDelta_QPMinus1 = |delta_QP|-1.
  MaxAbsDelta_QPMinus1 = max(maxQP-refQP-1, refQP-minQP-1)
  Binarize AbsDelta_QPMinus1 with truncated unary code with max= MaxAbsDelta_QPMinus1
  If refQP + AbsDelta_QPMinus1+1<= maxQP && refQP - AbsDelta_QPMinus1-1>=minQP
  Send sign of delta_QP
Example
  maxQP=32
  minQP=24
  refQP=30
Index | dQP value | QP | JCTVC-F174 | Proposed
0 | 0 | 30 | 0 | 0
1 | 1 | 31 | 10 | 100
2 | -1 | 29 | 110 | 101
3 | 2 | 32 | 1110 | 1100
4 | -2 | 28 | 11110 | 1101
5 | -3 | 27 | 11110 | 1110
6 | -4 | 26 | 1111110 | 11110
7 | -5 | 25 | 11111110 | 111110
8 | -6 | 24 | 11111111 | 111111

## Slide 5: Results
Cross-checked by Nokia, JCTVC-G956
Anchor is JCTVC-F174/JCTVC-G462
 | All Intra HE |  |  | 
 | Y | U | V | dQP incr.
Class A | -0.1% | -0.1% | -0.1% | -2.2%
Class B | -0.1% | -0.1% | -0.1% | -1.9%
Class C | -0.1% | -0.1% | -0.1% | -1.8%
Class D | -0.1% | -0.1% | -0.1% | -2.2%
Class E | -0.1% | -0.1% | -0.1% | -1.8%
Overall | -0.1% | -0.1% | -0.1% | -2.0%
 | -0.1% | -0.1% | -0.1% | 
Enc Time[%] | #NUM! |  |  | 
Dec Time[%] | #NUM! |  |  | 
 | Random Access HE |  |  | 
 | Y | U | V | dQP incr.
Class A | -0.1% | -0.1% | -0.1% | -2.6%
Class B | -0.1% | -0.1% | -0.1% | -2.3%
Class C | -0.1% | -0.1% | -0.1% | -2.6%
Class D | -0.1% | -0.1% | -0.1% | -3.2%
Class E |  |  |  | 
Overall | -0.1% | -0.1% | -0.1% | -2.7%
 | -0.1% | -0.1% | -0.1% | 
Enc Time[%] | #NUM! |  |  | 
Dec Time[%] | #NUM! |  |  | 
 | Low delay B HE |  |  | 
 | Y | U | V | dQP incr.
Class A |  |  |  | 
Class B | -0.1% | -0.1% | -0.1% | -2.6%
Class C | -0.1% | -0.1% | -0.1% | -2.8%
Class D | -0.1% | -0.1% | -0.1% | -3.6%
Class E | -0.1% | -0.1% | -0.1% | -2.5%
Overall | -0.1% | -0.1% | -0.1% | -2.9%
 | -0.1% | -0.1% | -0.1% | 
Enc Time[%] | #NUM! |  |  | 
Dec Time[%] | #NUM! |  |  | 

## Slide 6: Results
Anchor is CE4 anchor
 | All Intra HE |  |  | 
 | Y | U | V | dQP incr.
Class A | -0.1% | -0.1% | -0.1% | -3.1%
Class B | -0.1% | -0.1% | -0.1% | -2.4%
Class C | -0.1% | -0.1% | -0.1% | -2.7%
Class D | -0.1% | -0.1% | -0.1% | -4.1%
Class E | -0.2% | -0.2% | -0.1% | -3.2%
Overall | -0.1% | -0.1% | -0.1% | -3.1%
 | -0.1% | -0.1% | -0.1% | 
Enc Time[%] | 99% |  |  | 
Dec Time[%] | 100% |  |  | 
 | Random Access HE |  |  | 
 | Y | U | V | dQP incr.
Class A | -0.1% | 0.0% | -0.4% | -3.7%
Class B | -0.1% | -0.1% | 0.0% | -3.0%
Class C | -0.1% | -0.1% | -0.2% | -3.8%
Class D | 0.1% | 0.2% | 0.0% | -5.2%
Class E |  |  |  | 
Overall | 0.0% | 0.0% | -0.1% | -3.9%
 | 0.0% | 0.0% | -0.1% | 
Enc Time[%] | 100% |  |  | 
Dec Time[%] | 100% |  |  | 
 | Low delay B HE |  |  | 
 | Y | U | V | dQP incr.
Class A |  |  |  | 
Class B | -0.1% | 0.1% | -0.4% | -3.4%
Class C | -0.2% | -0.3% | 0.0% | -4.2%
Class D | 0.0% | -0.3% | 0.3% | -5.6%
Class E | 0.0% | 1.1% | -0.5% | -5.5%
Overall | -0.1% | 0.1% | -0.1% | -4.6%
 | -0.1% | 0.1% | 0.0% | 
Enc Time[%] | 100% |  |  | 
Dec Time[%] | 101% |  |  | 

## Slide 7: Conclusion
Presented solutions to remove redundancy of delta_QP binarization in CABAC with maxQP and minQP
0.1% BD-rate savings observed and >2% dQP bits savings over JCTVC-F174/JCTVC-G462, 3%~4% dQP bits savings over CE4 anchor, no complexity
Propose to adopt in HM5.0