## Slide 1
1
Cheung Auyeung
Sony Electronics Inc.
November 16, 2011
Binarisation of last position for higher throughput
JCTVC-G370
Notes: 1

## Slide 2: Binarisation of Last Position
With CABAC, HM4 binarise the last position coordinates (x,y) of transform coefficients with unary and fixed binary codes.
  Fixed binary codes are encoded in bypass mode.
Proposed binarisation to improve throughput:
x-prefix unary
x-suffix fixed binary
y-prefix unary
y-suffix fixed binary
x-prefix unary
x-suffix fixed binary
y-prefix unary
y-suffix fixed binary
Encode together in bypass mode with CABAC.
Decisions to skip syntax elements can be easily pipelined.

## Slide 3: Simulations
Algorithms were integrated into HM4.0.
Simulations were performed in Microsoft HPC clusters
  All intra simulations are performed on AMD Opteron Processor 6136 @ 2.4GHz.
  All RA simulations are performed on Intel Xeon X5690 @ 3.47GHz.
  All LD simulations are performed on Intel Xeon X5680 @ 3.33GHz.
Crosschecks are provided by Panasonic in JCTVC-G900
  Thank you very much.

## Slide 4: BD-Rate Results and Summary
The proposed binarisation improves throughput with no changes in BD-Rate.
Propose to be adopted to HM5.
 | All Intra HE |  | 
 | Y | U | V
Class A | 0.0% | 0.0% | 0.0%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 101% |  | 
Random Access HE |  | 
Y | U | V
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
100% |  | 
99% |  | 
Low delay B HE |  | 
Y | U | V
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
100% |  | 
100% |  |