## Slide 1
1
Cheung Auyeung
Teruhiko Suzuki
Sony Electronics Inc.
November 16, 2011
Reordering of Sign and Level Minus 3 coding with CABAC
Notes: 1

## Slide 2: Summary
HM4 encode the coeff_abs_level_minus3 after coeff_sign_flag.
Propose to encode the coeff_sign_flag after coeff_abs_level_minus3 to reduce
  sum of internal and interface buffer size
  latency.
0.00% BDR for all test cases.

## Slide 3: F130
TI proposed to send bypass coding part at the same place
But HM4 encode sign bits before GR-EG
HM3
F130

## Slide 4: F130/HM4.0
1
2
3
4
5
6
7
8
9
10
Order to finalize coeff
Process the coefficients in data driven order to finalize the value of the coefficients.
Need to convert data driven order to scan order to interface with external logics:
  Concern on throughput
  full bit(～16bit) x 2block register is necessary for high throughput
Pros
  Doesn’t need to store coeff_abs_level_minus3 which
  has longer code length
  block buffer: flag 3bit x 1block is necessary
Bitstream
order

## Slide 5: Concern on F130/HM4.0
1
2
3
4
5
6
7
8
9
10
Order to finalize coeff
  coeff_abs_level_minus3 is variable length
Implementations for reordering without using full bit buffer but with lower throughput:
  CABAC decoding maybe stopped to wait for re-order I/F
Most probable reordering implementation for higher throughput
  Implement full bit(～16bit) block buffer with 2bank
  Performance problem can be solved.
Notes: Rice Golomb (k=3) prefix/remで4bit
EG0 1-2:3bit, 3-6:5bit, 16383-32766:29bit

## Slide 6: Proposal
1
2
3
4
5
6
7
8
9
10
Order to finalize coeff
Coeff finalized order＝scan order
Process coefficients after coeff_sign_flag is decoded
  No scheduling is necessary
  No latency: buffer is empty after decoding 1block
full bit(～16bit) x 1block is necessary

## Slide 7: Simulations and Results
Algorithms were integrated into HM4.0.
Simulations were performed in Microsoft HPC clusters:
  All intra simulations were performed on AMD Opteron 6136 processor cluster @ 2.4GHz.
  Random Access simulations were performed on Intel Xeon X5690 processor cluster @ 3.47GHz.
  Low Delay simulations were performed on Intel Xeon X5680 processor cluster @ 3.33GHz.
Cross-checked by Samsung in JCTVC-G744
  Thank you very much.
BDR results
 | All Intra HE |  | 
 | Y | U | V
Class A | 0.00% | 0.00% | 0.00%
Class B | 0.00% | 0.00% | 0.00%
Class C | 0.00% | 0.00% | 0.00%
Class D | 0.00% | 0.00% | 0.00%
Class E | 0.00% | 0.00% | 0.00%
Overall | 0.00% | 0.00% | 0.00%
 | 0.00% | 0.00% | 0.00%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Random Access HE |  | 
Y | U | V
0.00% | 0.00% | 0.00%
0.00% | 0.00% | 0.00%
0.00% | 0.00% | 0.00%
0.00% | 0.00% | 0.00%
0.00% | 0.00% | 0.00%
0.00% | 0.00% | 0.00%
100% |  | 
100% |  | 
Low delay B HE |  | 
Y | U | V
0.00% | 0.00% | 0.00%
0.00% | 0.00% | 0.00%
0.00% | 0.00% | 0.00%
0.00% | 0.00% | 0.00%
0.00% | 0.00% | 0.00%
0.00% | 0.00% | 0.00%
100% |  | 
101% |  | 

## Slide 8: Conclusion
To improve throughput, encoding the coeff_sign_flag after coeff_abs_level_minus3 requires less total memory and has lower latency.
Propose to encode the coeff_sign_flag after coeff_abs_level_minus3 in HM5.