## Slide 1
1
Cheung Auyeung
Sony Electronics Inc.
November 18, 2011
Performance of Secondary Boundary DC intra prediction
JCTVC-G373
Notes: 1

## Slide 2: Summary
When the secondary boundary non-DC intra predictions JCTVC-F122 and JCTVC-F358Planar are available in HM4, the secondary boundary DC intra prediction could be removed to lower complexity for the following cost in BD-Rate :
  0.04% for I_HE
  0.03% for I_LC
BDR without Class A:
  0.02% for I_HE
  0.00% for I_LC

## Slide 3: Background
Secondary boundary DC intra prediction from JCTVC-E069 was adopted to HM3 with BD-Rate of
  -0.2% on AI_HE
  -0.4% on AI_LC
A simplified version from JCTVC-F252 was adopted to HM4 with BD-Rate of
  -0.04% on AI_HE
  -0.02% on AI_LC.
In CE6d, other secondary boundary non-DC intra prediction was studied, e.g.
  JCTVC-F122 on “Direction based angular intra prediction”.
  JCTVC-F358 Planar on” Mode dependent filtering for intra predicted sample”.
What is the performance of secondary boundary DC intra prediction when other secondary boundary non-DC intra predictions are available?

## Slide 4: Simulations
Algorithms were integrated into HM4.0.
Simulations were performed in a PC cluster:
  All intra simulations were performed on AMD Opteron 6136 processor cluster @ 2.4GHz.
Cross-checked by MediaTek in JCTVC-G861. All results matched.
  Thank you very much.

## Slide 5: Results
BDR results of HM4.0+F122+F358 with/without secondary boundary DC intra prediction. Anchor is with secondary boundary DC intra prediction.
BDR results without Class A:
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.15% | 0.22% | 0.24% | 0.13% | 0.32% | 0.37%
Class B | 0.05% | 0.15% | 0.10% | -0.03% | 0.18% | 0.20%
Class C | 0.00% | 0.10% | 0.11% | 0.02% | 0.10% | 0.13%
Class D | -0.01% | 0.05% | 0.12% | 0.01% | 0.06% | 0.08%
Class E | 0.02% | -0.01% | 0.13% | 0.02% | 0.06% | 0.05%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Overall | 0.04% | 0.11% | 0.14% | 0.03% | 0.15% | 0.18%
 | 0.05% | 0.11% | 0.14% | 0.03% | 0.15% | 0.18%
Enc Time[%] | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 101% |  | 
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Class B | 0.05% | 0.15% | 0.10% | -0.03% | 0.18% | 0.20%
Class C | 0.00% | 0.10% | 0.11% | 0.02% | 0.10% | 0.13%
Class D | -0.01% | 0.05% | 0.12% | 0.01% | 0.06% | 0.08%
Class E | 0.02% | -0.01% | 0.13% | 0.02% | 0.06% | 0.05%
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Overall | 0.02% | 0.08% | 0.11% | 0.00% | 0.11% | 0.13%
 | 0.02% | 0.09% | 0.11% | 0.01% | 0.10% | 0.13%
Enc Time[%] | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | 99% |  |  | 101% |  | 

## Slide 6: Conclusion
Secondary boundary DC intra prediction was less effective when other secondary boundary intra prediction tools are available.
  Results showed that secondary boundary DC intra prediction could be removed to lower complexity for less than 0.05% increases in BDR-rate.
  Class A test sequences have more increases in BDR than the other classes.
Removal of secondary boundary DC intra prediction could be an profile issue.