## Slide 1: MC boundary filter JCTVC-G390
Kenji Kondo and Teruhiko Suzuki
Sony

## Slide 2: Summary
Memory bandwidth is important issue for MC because
  Cost of DDR memory increases.
  Power consumption increases.
Proposal “MC boundary filter” can reduce memory bandwidth both worst and average case.
Explanation of MC boundary filter to reduce bandwidth
Experiment
  Check coding efficiency
    To simplify encoder, we checked the case of no use this boundary filter in motion search.
  Check visual quality
Conclusion

## Slide 3: The idea to reduce bandwidth
For block boundary, reference pixel becomes unnecessary with proposal.
Input reference pixel
Interpolated pixel
Reduced pixel
Current HM : DCT-IF 8 tap
Proposal
Block boundary
Filter coefficient is zero.
Filter coefficient is zero.

## Slide 4: Filter coefficients
For test case A (and B)
  1st pixel from boundary
    { 0 , 0 , -5 , 54 , 21 , -9 , 5 , -3 , 1 } for quarter pel 0
    { 0 , 0 , -6 , 36 , 44 , -15 , 8 , -4 , 1 } for half pel
    { 0 , 0 , -3 , 16 , 59 , -12 , 6 , -3 , 1 } for quarter pel 1
  2nd pixel from boundary
    { 0 , 2 , -9 , 56 , 20 , -8 , 4 , -1 , 0 } for quarter pel 0
    { 0 , 3 , -10 , 39 , 41 , -13 , 6 , -2 , 0 } for half pel
    { 0 , 2 , -6 , 18 , 58 , -11 , 4 , -1 , 0 } for quarter pel 1
For test case C
  1st pixel from boundary
    { 0 , 2 , -9 , 56 , 20 , -8 , 4 , -2 , 1 } for quarter pel 0
    { 0 , 3 , -10 , 39 , 42 , -14 , 7 , -4 , 1 } for half pel
    { 0 , 2 , -6 , 18 , 58 , -11 , 5 , -3 , 1 } for quarter pel 1
For otherwise
  DCTIF 8 tap is used.

## Slide 5: Experiment
We checked the impact for coding efficiency and visual quality.
Four test cases
  A: 2 lines of boundary are modified to boundary filter.
  B: basically same as A.
    but proposal filter is not used in ME.
    The ME means both motion search and mode decision for each CU.
  C: 1 line of boundary is modified to boundary filter.
  C+ restriction: case-C and 8x4, 4x8 for bi-prediction are restricted.
For visual quality
  Encoding condition
    RA_HE, LDP_HE, LDP_LC without SAO
    QP : 22 and 37
    Sequence: Nebuta, BQTerrace, BQMall, and PartyScene
  Environment for viewing
    EIZO monitor and High performance PC are used.
  Results
    The difference could not be found.

## Slide 6: Anchor
Low Delay P without SAO, QP37

## Slide 7: Proposal case-A
Low Delay P without SAO, QP37

## Slide 8: Results
 | A | B (no use in ME) | C | C + Restriction
Avg. BD[%] | 0.23% | 0.27% | 0.03% | 0.30%
Bandwidth (Worst) | -44% | -44% | -38% | -58%
Bandwidth (Typical) | -17% | -17% | -12% | -13%
Operations (Worst) | -28% | -28% | -21% | -33%
Operations (Typical) | -9% | -9% | -5% | -5%
Visual quality | Same as anchor | Same as anchor | Same as anchor | Same as anchor

## Slide 9: Conclusion
MC boundary filter can reduce complexity both bandwidth and computation for both worst and typical case.
  For theoretically worst,
    The bandwidth can be reduced -44% and -56% for case-A and C with restriction.
    The operations can be reduced -28% and -33% for case-A and C with restriction.
  For average on common test condition,
    The bandwidth can be reduced -17% and -13% for case A and C with restriction.
    The operations can be reduced -9% and -5% for case A and C with restriction.
In ME, we can use only DCTIF filter with negligible coding loss (~0.04%).
Visual quality is the same as anchor.

## Slide 10: Backup

## Slide 11: In actual case for 4x4 block
Memory locality
  With boundary filter, this means to use 4 tap for memory access.
Bandwidth decreases
  The memory b/w can be reduced for worst and average.
Computation decreases
  To interpolate yellow is not need.
For all PU size
  It can reduce Complexity.
MV
Extend pixel
Interpolated pixel
Unnecessary pixel by using boundary filter