## Slide 1: Report on a restriction for small block JCTVC-G392
K. Kondo and T. Suzuki
Sony

## Slide 2: Summary
Memory bandwidth is important because of cost of DDR memory.
Study a restriction to reduce worst complexity.
Experiment
  Check coding efficiency
  Check visual quality
Conclusion

## Slide 3: Memory bandwidth for each PU
Uni-prediction 64x64 integer pel
Bi-prediction 4x8 2d filtering
(e.g. ‘j’ center position)
The bandwidth is widely change by block size and prediction mode.
The range is very wide.
Uni-prediction 4x8 2d filtering
(pred. dir., size h, size v, interpolating)

## Slide 4: Restriction for small block
The restriction for small block is simple idea to reduce worst complexity.
The restriction is non normative change.
  Encoder does not choose the inter mode for small block and bi-prediction.
  For merge mode, encoder does not choose the merge index in candidates for small block and bi-prediction.
We tested several restrictions, and an impact of coding efficiency was checked.
  3 test cases were prepared in shown next page.
Also visual quality is checked.

## Slide 5: Test case
 |  | Case-A | Case-B | Case-C | Case-C + G390
Pred. mode | PU size | Non normative change | Non normative change | Non normative change | Normative change in G390
uni | 8x4 | Restricted | Restricted |  | 
uni | 4x8 | Restricted | Restricted |  | 
bi | 8x4 | Restricted | Restricted | Restricted | Restricted
bi | 4x8 | Restricted | Restricted | Restricted | Restricted
bi | 8x8 | Restricted |  |  | 
Worst bandwidth |  | -52% | -36% | -36% | -58%
To reduce worst bandwidth over 50%, also bi-prediction 8x8 and uni-prediction 8x4, 4x8 have to be restricted.

## Slide 6: Results
 | A | B | C | C + G390
Avg. BD[%] | 2.20% | 1.42% | 0.28% | 0.30%
Bandwidth (Worst) | -52% | -36% | -36% | -58%
Bandwidth (Typical) | -6% | -3% | -1% | -13%
Operations (Worst) | -22% | -22% | -22% | -33%
Operations (Typical) | -1% | 0% | 0% | -5%
Visual quality | Slight degradation is found. | Same with anchor | Same with anchor | Same with anchor
The case-A and B restriction can significantly reduce worst complexity, but it brings large BD% loss.

## Slide 7
Case-A | RA_HE | RA_LC | LDB_HE | LDB_LC | LDP_HE | LDP_LC | Average
Class A | 1.0% | 1.0% |  |  |  |  | 1.0%
Class B | 1.5% | 1.4% | 1.9% | 1.8% | 1.0% | 0.8% | 1.4%
Class C | 2.4% | 2.4% | 3.4% | 3.2% | 2.1% | 1.7% | 2.5%
Class D | 3.5% | 3.5% | 4.6% | 4.6% | 3.7% | 3.3% | 3.9%
Class E |  |  | 1.5% | 1.3% | 0.7% | 0.5% | 1.0%
Case-B | RA_HE | RA_LC | LDB_HE | LDB_LC | LDP_HE | LDP_LC | Average
Class A | 0.5% | 0.5% |  |  |  |  | 0.5%
Class B | 0.6% | 0.5% | 0.7% | 0.6% | 1.0% | 0.8% | 0.7%
Class C | 1.4% | 1.2% | 1.8% | 1.5% | 2.1% | 1.7% | 1.6%
Class D | 2.3% | 2.1% | 2.9% | 2.7% | 3.7% | 3.3% | 2.8%
Class E |  |  | 0.6% | 0.4% | 0.7% | 0.5% | 0.6%
Case-C | RA_HE | RA_LC | LDB_HE | LDB_LC | LDP_HE | LDP_LC | Average
Class A | 0.2% | 0.2% |  |  |  |  | 0.2%
Class B | 0.2% | 0.2% | 0.3% | 0.3% | 0.0% | 0.0% | 0.2%
Class C | 0.4% | 0.4% | 0.6% | 0.5% | 0.0% | 0.0% | 0.3%
Class D | 0.6% | 0.7% | 0.9% | 0.8% | 0.0% | 0.0% | 0.5%
Class E |  |  | 0.4% | 0.2% | 0.0% | 0.0% | 0.2%
C+G390 | RA_HE | RA_LC | LDB_HE | LDB_LC | LDP_HE | LDP_LC | Average
Class A | 0.2% | 0.2% |  |  |  |  | 0.2%
Class B | 0.2% | 0.2% | 0.3% | 0.2% | 0.0% | 0.1% | 0.2%
Class C | 0.4% | 0.4% | 0.6% | 0.5% | 0.0% | 0.1% | 0.3%
Class D | 0.6% | 0.6% | 0.8% | 0.6% | 0.1% | 0.0% | 0.4%
Class E |  |  | 0.6% | 0.2% | 0.2% | 0.2% | 0.3%
Case-A
Case-B
Case-C
Case-C +G390

## Slide 8: Coding efficiency for image size
Test case
For large image such as class A, B, and E, the BD% loss is smaller than class C and D.

## Slide 9: Conclusion
To reduce worst complexity, restrictions without normative change were studied.
Theoretically worst analysis was carried out.
  The bandwidth is widely change by block size and prediction mode.
    The range is very wide.
  To reduce worst bandwidth over 50% without normative change, also bi-prediction 8x8 have to be restricted
The case-A restriction can significantly reduce worst complexity, but it brings large BD% loss.
For large image as class A, B, and E, the BD% loss is smaller than class C and D.
Recommend to design level,
  to discuss max bandwidth for each level.
  to design relevant restriction for each level