## Slide 1: High-level Syntax: Marking process for non-TMVP pictures
Bin Li, Jizheng Xu, Houqiang Li
University of Science and Technology of China Microsoft Corp.

## Slide 2: Problem
MVP and merge candidates may be incorrect when packet loss exists
It was agreed adding a flag to disable TMVP at PPS level
  Inserting non-TMVP pictures at temporal level 0 can stop the error propagation of incorrect motion vector for the default coding structure
  But it is not always guaranteed correct motion vector for arbitrary coding structure (flexible referencing structure may be used)

## Slide 3: Analysis
The motion information of the non-TMVP pictures is reliable
The motion information of the other pictures may be incorrect due to packet loss

## Slide 4: Solution
Move the no_TMVP_flag from PPS to APS, as for the purpose to stop error propagation of incorrect motion vector, some pictures will use TMVP while others will not
Mark all the unreliable motion information “unused for temporal motion vector prediction” to guarantee that errors can be stopped

## Slide 5: Marking process
Solution 1
  Marking process takes place before the beginning of the decoding process of a picture with a larger POC. (similar to CDR)
  If the current POC is greater than the last_non_TMVP_POC and the temporal_id is 0, all the pictures in DPB except the picture with the POC equals to last_non_TMVP_POC are marked as “unused for temporal motion vector prediction”. last_non_TMVP_POC is reset to the largest POC number.
  If the current picture is non-TMVP picture with temporal_id 0, last_non_TMVP_POC is set to equal to the current POC.

## Slide 6: Marking process (Cont.)
Solution 2
  Marking process takes place before decoding a picture
  If current picture is non-TMVP picture and temporal_id is 0, all the pictures in DPB is marked as “unused for temporal motion vector prediction”.

## Slide 7: Comparison of two solutions
Two solutions provide identical coding results under HM-4.0 coding structure, if one non-TMVP picture is used every 8 pictures
Solution 1 guarantees correct motion vectors for the pictures after non-TMVP picture in both decoding and display order
Solution 2 guarantees correct motion vectors for the pictures after no-TMVP picture in decoding order

## Slide 8: Comparison (Cont.)
If more flexible referencing structure is used (i.e. collocated_from_l0_flag is different in HM-4.0, it also seems that in HM-4.0 collocated_from_l0_flag has the opposite meaning)
  Solution 1 has less impact on performance
  Solution 2 is simpler

## Slide 9: More about the bug
WRITE_FLAG( pcSlice->getColDir(), "collocated_from_l0_flag" );
TComPic *pColPic = getSlice()->getRefPic( RefPicList(getSlice()->isInterB() ? getSlice()->getColDir() : 0), 0);
When pcSlice->getColDir() == 1, collocated block is from list 1 instead of list 0.
Fix at both encoder and decoder side WRITE_FLAG( pcSlice->getColDir() ? 0 : 1, "collocated_from_l0_flag" );

## Slide 10
Thank you!