## Slide 1: RDO with weighted distortion in HEVC
Bin Li, Gary J. Sullivan, Jizheng Xu
University of Science and Technology of China Microsoft Corp.

## Slide 2: Purpose
Investigate the performance change when using different weights for different components in RDO
PSNRAVGYUV = (6*PSNRAVGY+PSNRAVGU+PSNRAVGV)/8

## Slide 3: RDO decision
HM-3.0
HM-4.0
  ω was introduced in JCTVC-F386
Our target
  Enlarge the weight of chroma
  Applied when different color components are considerer together (such as mode decision)

## Slide 4
 | All Intra HE |  |  |  | All Intra LC |  |  | 
 | Y | U | V | Avg. | Y | U | V | Avg.
Class A | 0.2% | -2.4% | -2.4% | -0.1% | 0.3% | -2.1% | -2.3% | 0.0%
Class B | 0.3% | -2.6% | -2.7% | -0.2% | 0.2% | -2.2% | -2.1% | -0.2%
Class C | 0.3% | -1.9% | -2.0% | -0.1% | 0.2% | -1.7% | -1.7% | -0.1%
Class D | 0.2% | -1.6% | -1.7% | -0.1% | 0.2% | -1.3% | -1.4% | -0.1%
Class E | 0.3% | -2.7% | -2.7% | -0.3% | 0.2% | -2.0% | -2.0% | -0.2%
Overall | 0.3% | -2.3% | -2.3% | -0.1% | 0.2% | -1.9% | -1.9% | -0.1%
EncT | 100% |  |  |  | 99% |  |  | 
DecT | 99% |  |  |  | 99% |  |  | 

## Slide 5
 | Random Access HE |  |  |  | Random Access LC |  |  | 
 | Y | U | V | Avg. | Y | U | V | Avg.
Class A | 0.9% | -9.4% | -9.3% | -0.4% | 1.3% | -9.4% | -9.1% | 0.1%
Class B | 1.0% | -8.7% | -8.3% | -0.7% | 1.0% | -7.8% | -7.4% | -0.5%
Class C | 0.9% | -6.9% | -6.9% | -0.5% | 0.9% | -6.1% | -6.2% | -0.3%
Class D | 0.8% | -6.4% | -7.1% | -0.5% | 0.8% | -6.4% | -6.5% | -0.5%
Class E |  |  |  |  |  |  |  | 
Overall | 0.9% | -7.9% | -7.9% | -0.6% | 1.0% | -7.4% | -7.3% | -0.3%
EncT | 101% |  |  |  | 101% |  |  | 
DecT | 100% |  |  |  | 99% |  |  | 

## Slide 6
 | Low delay B HE |  |  |  | Low delay B LC |  |  | 
 | Y | U | V | Avg. | Y | U | V | Avg.
Class A |  |  |  |  |  |  |  | 
Class B | 1.6% | -12.5% | -12.2% | -0.8% | 1.7% | -10.7% | -10.1% | -0.3%
Class C | 1.6% | -9.6% | -9.9% | -0.5% | 1.6% | -8.2% | -8.8% | -0.2%
Class D | 1.4% | -9.7% | -10.2% | -0.5% | 1.3% | -8.5% | -8.9% | -0.4%
Class E | 0.5% | -11.7% | -11.6% | -1.6% | 0.7% | -11.3% | -10.7% | -1.2%
Overall | 1.4% | -10.9% | -11.0% | -0.8% | 1.4% | -9.6% | -9.6% | -0.5%
EncT | 100% |  |  |  | 100% |  |  | 
DecT | 99% |  |  |  | 98% |  |  | 

## Slide 7: Decreasing chroma QP
By (second_)chroma_qp_index_offset in PPS (although this syntax element is reported to be missing currently from the draft and HM software)
QP_chroma_new = Clip3( 0, QP_chroma_old − X, 51 )
  X = 1, 2, 3 are tested
The increasing of time is mainly caused by the increasing of bit rate

## Slide 8: AI_HE
 | Chroma QP − 1 |  |  |  | Chroma QP − 2 |  |  |  | Chroma QP − 3 |  |  | 
 | Y | U | V | Avg. | Y | U | V | Avg. | Y | U | V | Avg.
A | 1.6% | -11.2% | -11.3% | -0.4% | 3.5% | -20.7% | -20.9% | -0.5% | 5.8% | -29.9% | -30.1% | -0.6%
B | 2.0% | -13.2% | -13.7% | -0.9% | 4.4% | -24.4% | -25.1% | -1.4% | 7.4% | -34.7% | -35.2% | -1.7%
C | 1.9% | -11.2% | -11.2% | -0.6% | 4.1% | -20.7% | -20.7% | -1.0% | 6.7% | -30.0% | -29.9% | -1.3%
D | 1.7% | -10.9% | -10.9% | -0.5% | 3.7% | -20.2% | -20.3% | -0.9% | 6.0% | -29.2% | -29.4% | -1.2%
E | 1.1% | -12.3% | -12.2% | -1.4% | 2.3% | -22.6% | -22.5% | -2.5% | 3.8% | -31.5% | -31.4% | -3.4%
All | 1.7% | -11.8% | -11.9% | -0.7% | 3.7% | -21.8% | -22.0% | -1.2% | 6.1% | -31.2% | -31.4% | -1.6%
EncT | 100% |  |  |  | 101% |  |  |  | 102% |  |  | 
DecT | 100% |  |  |  | 101% |  |  |  | 103% |  |  | 

## Slide 9: AI_LC
 | Chroma QP − 1 |  |  |  | Chroma QP − 2 |  |  |  | Chroma QP − 3 |  |  | 
 | Y | U | V | Avg. | Y | U | V | Avg. | Y | U | V | Avg.
A | 1.6% | -10.8% | -11.0% | -0.2% | 3.4% | -20.2% | -20.5% | -0.1% | 5.7% | -29.4% | -29.7% | 0.0%
B | 2.0% | -12.9% | -13.3% | -0.6% | 4.3% | -23.7% | -24.3% | -1.0% | 7.2% | -33.7% | -34.3% | -1.1%
C | 1.9% | -11.0% | -11.1% | -0.5% | 4.1% | -20.5% | -20.5% | -0.7% | 6.6% | -29.7% | -29.6% | -1.0%
D | 1.8% | -10.9% | -11.0% | -0.4% | 3.7% | -20.4% | -20.6% | -0.7% | 6.0% | -29.6% | -29.7% | -1.0%
E | 1.0% | -11.9% | -12.0% | -1.1% | 2.3% | -22.3% | -22.0% | -1.9% | 3.7% | -30.7% | -30.7% | -2.5%
All | 1.7% | -11.6% | -11.7% | -0.5% | 3.7% | -21.5% | -21.7% | -0.8% | 6.0% | -30.8% | -31.0% | -1.1%
EncT | 101% |  |  |  | 101% |  |  |  | 102% |  |  | 
DecT | 100% |  |  |  | 102% |  |  |  | 103% |  |  | 

## Slide 10: RA_HE
 | Chroma QP − 1 |  |  |  | Chroma QP − 2 |  |  |  | Chroma QP − 3 |  |  | 
 | Y | U | V | Avg. | Y | U | V | Avg. | Y | U | V | Avg.
A | 1.2% | -18.8% | -19.0% | -1.4% | 2.7% | -33.3% | -33.2% | -2.5% | 4.7% | -45.0% | -45.1% | -3.3%
B | 1.6% | -18.1% | -18.2% | -2.1% | 3.7% | -32.0% | -32.4% | -3.8% | 6.2% | -43.4% | -44.0% | -5.1%
C | 1.7% | -14.4% | -14.3% | -1.4% | 3.6% | -26.3% | -26.1% | -2.6% | 5.8% | -36.7% | -36.5% | -3.6%
D | 1.4% | -14.8% | -15.0% | -1.6% | 3.0% | -26.8% | -26.9% | -3.0% | 4.9% | -37.5% | -37.4% | -4.2%
E |  |  |  |  |  |  |  |  |  |  |  | 
All | 1.5% | -16.6% | -16.7% | -1.7% | 3.3% | -29.8% | -29.8% | -3.0% | 5.4% | -40.8% | -41.0% | -4.1%
EncT | 100% |  |  |  | 101% |  |  |  | 101% |  |  | 
DecT | 101% |  |  |  | 102% |  |  |  | 102% |  |  | 

## Slide 11: RA_LC
 | Chroma QP − 1 |  |  |  | Chroma QP − 2 |  |  |  | Chroma QP − 3 |  |  | 
 | Y | U | V | Avg. | Y | U | V | Avg. | Y | U | V | Avg.
A | 1.2% | -17.7% | -18.0% | -1.1% | 2.7% | -31.8% | -32.4% | -2.0% | 4.7% | -43.6% | -44.5% | -2.5%
B | 1.6% | -16.9% | -17.0% | -1.7% | 3.8% | -30.6% | -30.9% | -3.0% | 6.3% | -41.6% | -42.3% | -4.0%
C | 1.6% | -13.9% | -13.8% | -1.2% | 3.6% | -25.7% | -25.5% | -2.2% | 5.9% | -35.8% | -35.7% | -2.9%
D | 1.4% | -14.5% | -14.2% | -1.4% | 3.0% | -27.0% | -26.7% | -2.7% | 5.0% | -37.4% | -37.0% | -3.7%
E |  |  |  |  |  |  |  |  |  |  |  | 
All | 1.5% | -15.8% | -15.9% | -1.4% | 3.3% | -28.9% | -29.0% | -2.5% | 5.5% | -39.7% | -40.0% | -3.3%
EncT | 100% |  |  |  | 101% |  |  |  | 101% |  |  | 
DecT | 101% |  |  |  | 102% |  |  |  | 103% |  |  | 

## Slide 12: LB_HE
 | Chroma QP − 1 |  |  |  | Chroma QP − 2 |  |  |  | Chroma QP − 3 |  |  | 
 | Y | U | V | Avg. | Y | U | V | Avg. | Y | U | V | Avg.
A |  |  |  |  |  |  |  |  |  |  |  | 
B | 1.5% | -19.7% | -19.8% | -2.3% | 3.4% | -34.5% | -34.5% | -4.2% | 6.0% | -45.9% | -46.1% | -5.6%
C | 1.6% | -15.7% | -16.1% | -1.8% | 3.4% | -28.6% | -28.5% | -3.2% | 5.7% | -39.0% | -39.2% | -4.3%
D | 1.3% | -16.0% | -16.4% | -1.8% | 2.8% | -29.7% | -29.7% | -3.5% | 4.6% | -40.4% | -40.5% | -4.8%
E | 0.6% | -17.9% | -18.3% | -2.8% | 1.2% | -33.1% | -31.9% | -5.3% | 2.0% | -44.9% | -44.3% | -7.7%
All | 1.3% | -17.5% | -17.7% | -2.1% | 2.9% | -31.6% | -31.3% | -4.0% | 4.8% | -42.6% | -42.6% | -5.5%
EncT | 100% |  |  |  | 101% |  |  |  | 101% |  |  | 
DecT | 102% |  |  |  | 102% |  |  |  | 103% |  |  | 

## Slide 13: LB_LC
 | Chroma QP − 1 |  |  |  | Chroma QP − 2 |  |  |  | Chroma QP − 3 |  |  | 
 | Y | U | V | Avg. | Y | U | V | Avg. | Y | U | V | Avg.
A |  |  |  |  |  |  |  |  |  |  |  | 
B | 1.5% | -17.7% | -17.7% | -1.8% | 3.6% | -32.2% | -32.4% | -3.3% | 6.2% | -43.3% | -43.6% | -4.3%
C | 1.6% | -14.5% | -14.9% | -1.4% | 3.7% | -27.3% | -27.6% | -2.5% | 6.0% | -37.5% | -37.7% | -3.4%
D | 1.4% | -14.9% | -15.2% | -1.5% | 3.0% | -28.8% | -29.2% | -3.0% | 4.9% | -39.4% | -39.4% | -4.1%
E | 0.4% | -17.7% | -17.1% | -2.5% | 1.2% | -31.6% | -30.9% | -4.5% | 2.1% | -43.8% | -43.5% | -6.4%
All | 1.3% | -16.2% | -16.3% | -1.8% | 3.0% | -30.0% | -30.1% | -3.3% | 5.0% | -41.0% | -41.1% | -4.4%
EncT | 100% |  |  |  | 101% |  |  |  | 101% |  |  | 
DecT | 102% |  |  |  | 103% |  |  |  | 104% |  |  | 

## Slide 14: Conclusion
Changing the weight of distortion of the different color components can bring some measured BD-Rate gain if the combined PSNR is used
If the QP of chroma is decreased, more gain can be obtained if the combined PSNR is used
Verify the effectiveness of chroma_qp_index_offset and second_chroma_qp_index_offset

## Slide 15
Thank you!