## Slide 1
JCTVC-G413
Modified probability update and table removal for multi-parameter CABAC update (F254/G764)
7th JCT-VC meeting, Nov 2011.

## Slide 2: F254/G764 studied in CE1
Issue: large 512x64x9-bit (288Kb) Look-up table present in F254/G764.
  LUT purpose is to determine 9-bit uiLPS for given uiProb and m_uiRange.
    9-bit uiProb derived from 15-bit iP0, iP1.
We propose that the LUT can be removed entirely by performing the following steps:
  Replace LUT with a 6-bit (taken from m_uiRange) by 9-bit (taken from uiProb) multiplier.
    We assert that this small bit-width is OK for hardware implementation.
  Introduce clamping operation in probability update and multiplier output.

## Slide 3: F254/G764 studied in CE1
The LUT contains clamping at the upper and lower ends of each column:
  Upper clamping dependent on m_uiRange.
  Lower clamping independent on m_uiRange.
To reduce critical path delay of arithmetic decode operation, implement ‘upper clamping’ by restricting the range of the probability update operation instead.
The previous updateLPS function is defined as:
  iP0 -= iP0 >> ALPHA0, iP1 -= iP1 >> ALPHA1
The proposed updateLPS function is defined as:
  iP0 = max(iP0 – iP0 >> ALPHA0, 2<<6), iP1 = max(iP1 – iP1 >> ALPHA1, 2<<6)

## Slide 4: Results relative to F254/G764 multisource
 | All Intra HE |  | 
 | Y | U | V
Class A | 0.0% | -0.1% | -0.2%
Class B | 0.0% | -0.1% | 0.0%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0%
Class E | 0.0% | -0.2% | -0.2%
Class F | 0.0% | 0.0% | 0.0%
Overall (A-F) | 0.0% | -0.1% | -0.1%
 | 0.0% | -0.1% | -0.1%
Overall (A-E) | 0.0% | -0.1% | -0.1%
 | 0.0% | -0.1% | -0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
 | Random Access HE |  | 
 | Y | U | V
Class A | 0.0% | 0.0% | 0.0%
Class B | 0.0% | -0.1% | -0.1%
Class C | 0.0% | 0.0% | -0.1%
Class D | 0.0% | 0.1% | -0.3%
Class E |  |  | 
Class F | 0.0% | -0.1% | 0.1%
Overall (A-F) | 0.0% | 0.0% | -0.1%
 | 0.0% | 0.0% | -0.1%
Overall (A-E) | 0.0% | 0.0% | -0.1%
 | 0.0% | 0.0% | -0.2%
Enc Time[%] | 101% |  | 
Dec Time[%] | 100% |  | 
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | -0.1% | -0.1%
Class C | 0.0% | -0.1% | 0.2%
Class D | 0.0% | -0.1% | -0.5%
Class E | -0.1% | -0.5% | -0.9%
Class F | 0.0% | -0.3% | 0.0%
Overall (A-F) | 0.0% | -0.2% | -0.2%
 | 0.0% | -0.2% | -0.1%
Overall (A-E) | 0.0% | -0.2% | -0.3%
 | 0.0% | -0.2% | -0.2%
Enc Time[%] | 100% |  | 
Dec Time[%] | 99% |  | 
 | Low delay P HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | -0.1% | -0.5%
Class C | 0.0% | -0.2% | 0.0%
Class D | 0.0% | -0.6% | 0.4%
Class E | 0.0% | -1.0% | -1.1%
Class F | 0.0% | -0.3% | -0.4%
Overall (A-F) | 0.0% | -0.4% | -0.3%
 | 0.0% | -0.4% | -0.2%
Overall (A-E) | 0.0% | -0.4% | -0.2%
 | 0.0% | -0.5% | -0.2%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 

## Slide 5: Results relative to HM-4.0
 | All Intra HE |  | 
 | Y | U | V
Class A | -1.0% | -0.8% | -0.9%
Class B | -0.9% | -1.2% | -1.2%
Class C | -0.9% | -1.2% | -1.3%
Class D | -0.9% | -1.7% | -1.7%
Class E | -0.9% | -2.0% | -1.9%
Class F | -0.6% | -0.9% | -0.8%
Overall (A-F) | -0.9% | -1.3% | -1.3%
 | -0.9% | -1.3% | -1.3%
Overall (A-E) | -0.9% | -1.4% | -1.4%
 | -0.9% | -1.3% | -1.4%
Enc Time[%] | 104% |  | 
Dec Time[%] | 100% |  | 
 | Random Access HE |  | 
 | Y | U | V
Class A | -1.1% | -0.3% | -0.2%
Class B | -0.9% | -0.8% | -0.8%
Class C | -0.9% | -0.9% | -1.0%
Class D | -0.8% | -1.0% | -1.6%
Class E |  |  | 
Class F | -0.5% | -0.5% | -0.5%
Overall (A-F) | -0.9% | -0.7% | -0.8%
 | -0.8% | -0.7% | -0.9%
Overall (A-E) | -0.9% | -0.8% | -0.9%
 | -0.9% | -0.8% | -0.9%
Enc Time[%] | 102% |  | 
Dec Time[%] | 100% |  | 
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | -0.8% | -0.9% | -1.2%
Class C | -0.7% | -0.8% | -0.9%
Class D | -0.8% | -1.2% | -1.5%
Class E | -1.0% | -2.5% | -1.3%
Class F | -0.5% | -0.9% | -0.1%
Overall (A-F) | -0.8% | -1.2% | -1.0%
 | -0.8% | -1.1% | -0.9%
Overall (A-E) | -0.8% | -1.3% | -1.2%
 | -0.8% | -1.2% | -1.1%
Enc Time[%] | 101% |  | 
Dec Time[%] | 100% |  | 
 | Low delay P HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | -0.8% | -0.7% | -0.6%
Class C | -0.8% | -0.6% | -0.7%
Class D | -0.7% | -0.9% | -0.2%
Class E | -1.0% | -2.4% | -2.0%
Class F | -0.4% | -0.3% | -0.3%
Overall (A-F) | -0.7% | -0.9% | -0.7%
 | -0.7% | -0.8% | -0.7%
Overall (A-E) | -0.8% | -1.0% | -0.8%
 | -0.8% | -1.0% | -0.8%
Enc Time[%] | 102% |  | 
Dec Time[%] | 102% |  |