## Slide 1: Reduction of the number of pixels used in ALF
Kazuyuki Miyazawa, Kazuo Sugimoto,
Akira Minezawa, Shun-ichi Sekiguchi,
and Tokumichi Murakami
Mitsubishi Electric Corporation
JCTVC-G446

## Slide 2: Summary
Proposed method
  Reduce the computational cost of Adaptive Loop Filter (ALF) by skipping ALF for the pixels where the impact of ALF likely to be insignificant.
  Calculate a score for each pixel, and skip ALF for the pixels whose scores are less than a threshold.
  The threshold is determined for each frame in the encoding process, and is transmitted to a decoder.
Results
  Enc time: 2% ~ 9% reduction (ALF-only: 24% ~ 27%)
  Dec time: 1% ~ 2% reduction (ALF-only: 5% ~ 11%)
  BD-rate: 0.1% ~ 0.2% loss

## Slide 3: Motivation
Performance degradation when the filters are not applied to one of five categories
Distributions of the percentage of each category (for Class B, all intra)
Can reduce the computation time of ALF without performance loss by not applying filters to the pixels in low activity categories.
In RA mode, Laplacian acitivity-based classification is not performed.
In some sequences, most of the pixels are classified as low activity categories.

## Slide 4: Proposed Method
Calculate a score predicting the effectiveness of ALF for each pixel, and skip ALF for the pixels whose scores are less than a threshold.
The threshold is determined for each frame based on the percentage of the number of ALF-skipped pixels, and is transmitted to a decoder.
Clustering
Filter
design
Filter
apply
CU-level
ON/OFF
Score
calculation
Thresholding
ENC
DEC
Clustering
Filter
apply
Score
calculation
Thresholding
Threshold

## Slide 5: Score Calculation
Variance-like score is calculated for each 4 x 4 block.
All 16 pixels in the 4 x 4 block have the same score.
m: Average of 4 pixels
Original frame
Score distribution
4x4 luma block

## Slide 6: Threshold Decision (Enc-Only)
The threshold is determined for each frame based on the percentage of the number of ALF-skipped pixels.
Cumulative histogram of the scores can be used.
The threshold is coded and transmitted to a decoder, for example, in PPS.
Score
Cumulative frequency
100%
Percentage of the number of ALF-skipped pixels
Threshold
Can be set as an encoder parameter, which controls the trade-off between the coding efficiency and complexity.

## Slide 7: Simulation Results (1/2)
The percentage of ALF-skipped pixels is set to 40%.
2% ~ 9% enc time reduction, and 1% ~ 2% dec time reduction with 0.1% ~ 0.2% BD-rate loss
Crosscheck-report: JCTVC-G920 (by Toshiba)
 | All Intra |  |  | Random Access |  |  | Low Delay B |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.1% | 0.0% | 0.1% | 0.2% | -0.3% | -0.2% |  |  | 
Class B | 0.1% | 0.0% | 0.1% | 0.2% | -0.2% | -0.2% | 0.3% | -0.1% | 0.1%
Class C | 0.1% | 0.1% | 0.1% | 0.1% | -0.2% | -0.2% | 0.2% | 0.2% | 0.1%
Class D | 0.0% | 0.1% | 0.0% | 0.1% | 0.0% | -0.2% | 0.1% | -0.4% | -0.3%
Class E | 0.1% | 0.2% | 0.2% |  |  |  | 0.2% | -0.3% | 1.0%
Overall | 0.1% | 0.1% | 0.1% | 0.2% | -0.2% | -0.2% | 0.2% | -0.1% | 0.2%
Enc Time | 91% |  |  | 97% |  |  | 98% |  | 
Dec Time | 99% |  |  | 98% |  |  | 98% |  | 

## Slide 8: Simulation Results (2/2)
24% ~ 27% reduction in encoding, and 5% ~ 11% reduction in decoding.
The time reduction ratio can be controlled by changing the percentage of ALF-skipped pixels.
 | All Intra | Random Access | Low Delay B
ALF Time in Enc | 76% | 73% | 75%
ALF Time in Dec | 95% | 90% | 89%
Computation time of ALF in the proposed method compared to that in HM4

## Slide 9: Conclusion
Proposed method
  Calculate a score for each pixel and skip ALF for the pixels whose scores are less than a threshold.
  Adaptively determine the threshold for each frame based on the percentage of ALF-skipped pixels, and transmit the threshold to a decoder.
Results
  Enc time: 2% ~ 9% reduction (ALF-only: 24% ~ 27%)
  Dec time: 1% ~ 2% reduction (ALF-only: 5% ~ 11%)
Recommendation
  Adopt the proposed method to CE for further study.