## Slide 1: Hybrid Horizontal/Vertical with Diagonal Mode Dependent Coefficient Scan
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.
JCTVC-G491

## Slide 2: Introduction
This contribution presents two additional Mode Dependent Coefficient Scan-orders (MDCS) for larger block sizes, dependent on the intra prediction direction.
  These Hybrid scan orders are a combination of a Horizontal/Vertical scan with a Diagonal scan, and can be implemented without a look-up table.
An additional technique (‘Speculation-Friendly’) that is claimed to reduce the burden on speculation when adding a scan order to larger blocks is also described.

## Slide 3: MDCS in HM4.0
Current MDCS Luma mapping for 4x4/8x8:
  (and chroma mapping for 4x4 chroma blocks)
Large Luma blocks (16x16/32x32) / Chroma (8x8/16x16) use Up-Right scan
  See contribution document for possible WD4/HM4 inconsistency.

## Slide 4: Hybrid Scan Orders

## Slide 5: Hybrid Scan Orders
Proposed Mappings for Large Luma blocks (16x16/32x32) or Chroma (8x8/16x16) :
Small blocks use original HM4.0 mapping

## Slide 6: ‘Speculation-Friendly’ Scanning
A system that decodes multiple coefficients at a time requires ‘speculation’ due to the interaction between adjacent context data.
This algorithm aims to increase the temporal distance between spatially adjacent context data.

## Slide 7: ‘Speculation-Friendly’ Scanning
Stage 1: Find EOB (first significant coefficient in reverse scan order) using Hybrid scan. Area of block with no significant coefficients is ‘invalid’ and has been greyed out
Stage 2: Once EOB is known, Diagonal scan over 'valid' region (in reverse order as per HM4.0)

## Slide 8: ‘Speculation-Friendly’ Scanning
Hybrid Scan order
Speculation-friendly scan
Minimum temporal distance (in reverse scan order) between neighbouring coefficients: 1 coefficient
Minimum temporal distance (in reverse scan order) between neighbouring coefficients: 4 coefficients
vs.

## Slide 9: Results
Simulations were performed for Intra HE and LC configurations.
  Note that the Speculation-friendly scan is only applicable to CABAC (HE).
We would like to thank MediaTek for offering to cross-check the results (JCTVC-G943).

## Slide 10: Conclusion
Two ‘Hybrid’ MDCS orders have been presented
  They are used for large blocks for a range of intra directions.
  They give Luma BD-rate changes (A-E) of:
    -0.15% for HE
    -0.39% for LC
  No increase in processing time
A ‘Speculation-Friendly’ HE algorithm has been presented
  Aims to increase temporal distance between spatially neighbouring values to reduce CABAC decoding complexity.
  Combined with the Hybrid MDCS gives Luma BD-rate changes of
    -0.13% for HE
    No increase in processing time