## Slide 1: Maximum VLC Limits in CABAC Escape Coding
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.
JCTVC-G492

## Slide 2: Introduction
This proposal has identified discrepancies in and between the HM4.0 source code and WD4 regarding Golomb Rice codes.
For completeness, two different sets of tables are analyzed.

## Slide 3: HM4.0
In HM4.0 source code there are two tables:
      const UInt g_auiGoRicePrefixLen[4] = {8, 10, 11, 8};
      const UInt g_auiGoRiceRange[4] = {7, 20, 42, 70};
    Indexing the elements of the tables is controlled by ‘uiGoRiceParam’
  The array g_auiGoRicePrefixLen is used to limit the length of the Golomb Rice prefix, and therefore limit the maximum value that is encoded using a simple Golomb Rice code.
  The array g_auiGoRiceRange describes the maximum value that is encoded using a simple Golomb Rice code.
    Larger values are sent with additional Exponential Golomb codes.
In WD4, only the g_auiGoRiceRange table is described
      This implies maximum prefix lengths of {7, 10, 10, 8};
        Derived as (g_auiGoRiceRange>>uiGoRiceParam)

## Slide 4: Proposal 1 (HM4.0)
Analysis of the Golomb Rice limits indicates that these would be best represented using:
    const UInt g_auiGoRicePrefixLen[4] = {8, 10, 11, 8};
    const UInt g_auiGoRiceRange[4] = {7, 20, 46, 70};
or alternatively:
    const UInt g_auiGoRicePrefixLen[4] = {8, 10, 10, 8};
    const UInt g_auiGoRiceRange[4] = {7, 20, 42, 70};
We propose that the latter set is used in the software as these give a very slight BD-rate improvement (0.0%, -0.02%, +0.01%).

## Slide 5: Proposal 2 (WD4)
In WD4, only the g_auiGoRiceRange table is described.
    This implies maximum prefix lengths of {7, 10, 10, 8}
        Defined as cMax = cTRMax >> cRiceParam
However, in WD4:
  “When the prefix bit string is not equal to the bin string that consists of ( cTRMax + 1 >> cRiceParam ) + cRiceParam ones, the bin string consists of a prefix bin string and a suffix bin string. The suffix bin string is derived using the EG0 binarization as specified in subclause 9.3.2.4”
  When cTRMax=7, cRiceParam=0
    8 ones would be needed to indicate the condition in the text.
    cMax=7
      i.e. The maximum number of ones that can be produced is 7!
  We propose either:
    changing the definition of cMax.
      cMax = (cTRMax+1) >> cRiceParam
    or, it may be better to define cTRMax in terms of cMax in order to remove the possibilities of wasted code-space if the values were to ever be changed.
  In addition, no mention of what is encoded using EG0 is made in WD4.
    i.e. suffix is EG0 encoding of value less (cTRMax+1)

## Slide 6: Results

## Slide 7: Conclusion
In HM4.0 code, the tables describing the Golomb Rice limits, namely:
    const UInt g_auiGoRicePrefixLen[4] = {8, 10, 11, 8};
    const UInt g_auiGoRiceRange[4] = {7, 20, 42, 70};
have redundancy in the code space when uiGoRiceParam=2.
Two alternative sets for Golomb Rice limits have been evaluated:
    const UInt g_auiGoRicePrefixLen[4] = {8, 10, 11, 8};
    const UInt g_auiGoRiceRange[4] = {7, 20, 46, 70};
  or alternatively:
    const UInt g_auiGoRicePrefixLen[4] = {8, 10, 10, 8};  Proposed
    const UInt g_auiGoRiceRange[4] = {7, 20, 42, 70};
  They remove the redundancy from the code-space, and the latter is the likely intended operation of WD4.
There are inconsistencies and missing information regarding CABAC VLC codes in WD4.

## Slide 9: Theory (1)
Golomb Rice code is of the form:
    value = (prefixLength << suffixLength) + suffix
      where suffixLength=uiGoRiceParam
  The maximum value encoded by a single Golomb Rice code has been limited in HM4.0:
    prefixLength has a maximum (maxPrefixLength) given in the table ‘g_auiGoRicePrefixLen’
    The value of uiGoRiceParam is used to index the array.
  The maximum value that can be represented is therefore:
    maxVal = (maxPrefixLength << uiGoRiceParam) + ((1 << uiGoRiceParam) - 1)
    = ((maxPrefixLength + 1) << uiGoRiceParam) – 1
  However, the value ‘maxVal’ is actually reserved to indicate an overflow into an escape-escape value.
    The values of g_auiGoRiceRange are the maximum allowed non-escape-escape value, and should be “maxVal-1”

## Slide 10: Theory (2)
  Given ‘g_auiGoRicePrefixLen[4] = {8, 10, 11, 8}’, this gives
  g_auiGoRiceRange[] = {7, 20, 46, 70};
  Given ‘g_auiGoRicePrefixLen[4] = {8, 10, 10, 8}’, this gives
  g_auiGoRiceRange[] = {7, 20, 42, 70};
The current set of tables:
    const UInt g_auiGoRicePrefixLen[4] = {8, 10, 11, 8};
    const UInt g_auiGoRiceRange[4] = {7, 20, 42, 70};
  would therefore use escape-escape coding for values 43, 44, 45 and 46 for uiGoRiceParam=2.
  However, these values can be expressed without requiring escape-escape coding using the current scheme if the range was changed from 42 to 46, or with less cost if the length was reduced from 11 to 10.