## Slide 1: CABAC Stream Termination
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.
JCTVC-G493

## Slide 2: Introduction
Two methods to terminate the CABAC stream are presented.
  Proposal 1: Termination takes only 1.5 bits.
  Proposal 2: Termination takes only 1 bit.
  This compares again HM4.0 that takes 8.5 bits to terminate the stream.
Applications for the methods are discussed.
Simulations have been run to confirm the cost in bits.

## Slide 3: In HM4.0
Stream termination occurs prior to IPCM data and at the end of a slice.
The processing is as follows:
  If not terminating:
    Reduce m_uiRange by 2. Renormalize if required.
  Else (terminating):
    Increase m_uiLow by (m_uiRange-2). Set m_uiRange=2. Renormalize, producing 7 bits. Output the next bit of m_uiLow. Output a 1 – this acts both as the 9th bit and as the rbsp_stop_one_bit.
9 bits are written if the bit-stream is terminated.
  This means a loss of 8.5 bits on average per termination.
This system is wasteful if the probability of termination >> 0.54%.
  ( )

## Slide 4: Proposal
This proposal considers two methods to terminate the stream.
  These can be used in combination with either a fixed or context-variable-based probability system indicating whether termination is about to occur.
As with any arithmetic coding system, the final value a CABAC encoder generates can be any value within the limits of:
  [low to high) where high=low+range
Therefore, pick a value such that the LSBs are irrelevant for a successful decode.
  The encoder then would not need to output the LSBs.
  The decoder would instead read the first few bits of the subsequent part of the data stream following the termination point without affecting the decode.

## Slide 5: Proposal 1
Method:
    In the encoder, to terminate:
      m_uiLow=(m_uiLow+128)&~127 Force 2 renormalizations Flush buffered data and reset encoder.
    In the decoder, once termination has been determined:
      Rewind the stream by 7-bits. Reset decoder.
  Cost:
    2 renormalizations per termination.
      i.e. an average of 1.5 bits per termination.

## Slide 6: Proposal 2
Method:
  In the decoder, track m_uiLow.
  In encoder and decoder, to terminate:
    test256=(m_uiLow+255)&~255 If (test256+255 < m_uiLow+m_uiRange) m_uiRange=255 (to force one renormalisation) m_uiLow=test256 revBits=8 Else m_uiLow=(m_uiLow+128)&~127 m_uiRange=127 (to force two renormalisations) revBits=7
    In encoder, renormalize, and reset.
    In decoder, rewind the stream by revBits bits – this is the start of the next data.
  Cost:
    1.5 renormalizations per termination.
      i.e. an average of 1 bit per termination.

## Slide 7: Applications
Example applications for this could be:
  Replacement for TRM mechanism for row-per-slice modes.
    Because P(termination) might be >> 0.54%
  Replacement for TRM mechanism for the last LCU of the slice.
    Because P(termination)=1.
  Replacement for TRM mechanism for IPCM data.
    Because P(termination) might be >> 0.54%
  Termination of stream if outstanding bits become too numerous.
    See JCTVC-G494 “CABAC Packet-based Stream” for an example.
The theory has been demonstrated with a system that terminates after each LCU in an all-intra configuration.
  The CABAC CV-based data is sent as per HM4.0.
  The escape and sign bits are sent as raw data following the LCU.
  Simulations confirm the losses of 1.5 bits and 1 bit for the two systems.

## Slide 8: Conclusion
Two algorithms to terminate the CABAC bit stream have been presented.
  Simulations have shown that they have a loss of 1.5 bits and 1 bit per termination.
  The current HM4.0 method of termination costs 8.5 bits.
Some applications for the algorithms have been listed.

## Slide 10: Theory (1)
For the encoder, the data written to the stream (or buffer) concatenated with “m_uiLow” is a n-bit value indicating the lower range that the final output can be.
  For simplicity, call this “low”.
“range” is a value from 256 to 510, and “high = low + uiRange” indicates the maximum (exclusive) value that the final output value can be.
At the end of the stream, any value between “low” and “high” can be selected, without affecting the decode.
We want the stream to be terminated and any bits that were not needed to decode the stream can be “pushed-back” into the stream (and used for subsequent streams of CABAC or raw data).
We are looking to output a value “v” where “v+startBitsOfNextStream” will not affect decoding of the current stream, and “startBitsOfNextStream” are not encoded using the current stream.
We assume that we are not tracking “low” in the decoder (this can give further savings)
  (See later)

## Slide 11: Theory (2)
Case 1:
low=0x45648 = 0b0100,0101,0110,0100,1000
range=0x123 = 0b 0001,0010,0011
high=0x4576b = 0b0100,0101,0111,0110,1011
We can pick any value between “low” and “high”.
  We want as many consecutive LSBs as possible to not be required to decode the stream.
  We therefore want to find the value between “low” and “high” that has the most ‘0’s at the LSBs.
  In this case,
  longestZeros = 0b0100,0101,0111,0000,0000
We now look at the ranges from “low” -> “longestZeros”, and “longestZeros” -> “high”
  If output value was:
  0b0100,0101,0110,1xxx,xxxx
  then decode would not be affected, and the bottom 7-bits could be from the start of the next stream.
  If output value was between
  0b0100,0101,0111,00xx,xxxx
  then decode would not be affected, and the bottom 6-bits could be from the start of the next stream.
  We can choose either possibility, and would want to pick the first.

## Slide 12: Theory (3)
Case 2:
low=0x456a8 = 0b0100,0101,0110,1010,1000
range=0x123 = 0b 0001,0010,0011
high=0x457cb = 0b0100,0101,0111,1100,1011
We can pick any value between “low” and “high”.
  We want as many consecutive LSBs as possible to not be required to decode the stream.
  We therefore want to find the value between “low” and “high” that has the most ‘0’s at the LSBs.
  In this case,
  longestZeros = 0b0100,0101,0111,0000,0000
We now look at the ranges from “low” -> “longestZeros”, and “longestZeros” -> “high”
  If output value was:
  0b0100,0101,0110,11xx,xxxx
  then decode would not be affected, and the bottom 6-bits could be from the start of the next stream.
  If output value was between
  0b0100,0101,0111,0xxx,xxxx
  then decode would not be affected, and the bottom 7-bits could be from the start of the next stream.
  We can choose either possibility, and would want to pick the second.

## Slide 13: Theory (4)
Because “range >= 256”, there will always be a scenario where 7-bits can be pulled in from the next section of the stream without affecting our decode.
The simplest way to therefore consider this is that we are choosing “v” such that:
  “v>=m_low” and “v[bits 6:0] = 0” and “v+127<low+range”
  i.e. “v=(low+127)&~127”
Or:
  “v>low” and “v[bits[6:0] = 0” and “v+127<low+range”
  i.e. “v=(low+128)&~127” (which uses a smaller adder)
The bottom 7 bits are therefore irrelevant to decoding the current stream.
So, in summary,
  In the encoder, to terminate:
    m_uiLow=(m_uiLow+128)&~127 Renormalize (twice) Flush buffered data and reset.
  In the decoder:
    Rewind the stream by 7-bits.

## Slide 14: Theory (5): complexity vs. efficiency
If the decoder tracks “m_uiLow”, then the loss will be reduced.
  e.g. if “low = 0” and “range=510”, then we could choose “v” so that:
    “v>=low and v[bits 7:0] = 0” i.e. “v=(low+255)&~255”
    The value “v” is chosen, and then checked to see that it is 256 lower than “high”
      If it is not, then the system reverts back to the 7-bit equation
  However, tracking “m_uiLow” in the decoder is slightly more expensive.
    Using decoding time as an indicator of complexity, shows a cost of ~0.1%.
  In summary,
    In the decoder, track “m_uiLow”
    In encoder and decoder do:
      test256=(m_uiLow+255)&~255 If (test256+255 < m_uiLow+m_uiRange) m_uiRange=255 (to force one renormalization) m_uiLow=test256 revBits=8 Else m_uiLow=(m_uiLow+128)&~127 m_uiRange=127 (to force two renormalizations) revBits=7 Renormalize.
      CABAC Stream is then terminated. Rewind the stream by revBits bits – this is the start of the next data.