## Slide 1: CABAC Packet-based Stream
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.
JCTVC-G494

## Slide 2: Introduction
In the current HEVC system (HM4.0),
  Bypass-encoded data are coded as CABAC data with fixed probability of 50%.
  This requires an iterative process in order to decode symbols with multiple bypass bits.
If bypass data were available raw, multiple bits could be read at once.
  Further, if the bypass data were available at a predetermined location in the stream, they could be interpreted in parallel with CABAC data.
This proposal outlines a method of splitting the CABAC stream into packets of CABAC and bypass data.
  This allows bypass data to be placed in the stream in raw form and read in parallel with CABAC data.
  This is used in the proposal JCTVC-G504 “CABAC with Combined Context Variables”.

## Slide 3: Packet Structure
CABAC data are written to the stream in fixed-size “CABAC packets” of 16 bits.
Each CABAC packet is followed by a “Bypass packet” of variable size.
  Bypass data are placed after the CABAC packet that allows the associated CABAC data to be fully decoded and renormalized.
The last CABAC packet in the stream may be shorter than 16 bits.
  If it has associated bypass data, it is padded out to 16 bits.

## Slide 4: Decoding a Packet-based Stream
A decoder can be implemented as a shift register.
  CABAC data are read from the front of the register. Bypass data are read from a “bypass index”.
  The decoder also speculatively reads bypass data from (bypass index + 16).
After each renormalization,
  CABAC data are read into m_uiValue, shifting all other bits as well as the bypass index.
  Bypass data (if any are needed) are read, shifting all bits further down the register.
At the end of each CABAC packet,
  The bypass index is incremented by 16.
  The bypass packet will now be empty, so CABAC data can be safely read past the end of the packet.

## Slide 5: Decoding a Packet-based Stream
A decoder can be implemented as a shift register.
  CABAC data are read from the front of the register. Bypass data are read from a “bypass index”.
  The decoder also speculatively reads bypass data from (bypass index + 16).
After each renormalization,
  CABAC data are read into m_uiValue, shifting all other bits as well as the bypass index.
  Bypass data (if any are needed) are read, shifting all bits further down the register.
At the end of each CABAC packet,
  The bypass index is incremented by 16.
  The bypass packet will now be empty, so CABAC data can be safely read past the end of the packet.

## Slide 6: Decoding a Packet-based Stream
A decoder can be implemented as a shift register.
  CABAC data are read from the front of the register. Bypass data are read from a “bypass index”.
  The decoder also speculatively reads bypass data from (bypass index + 16).
After each renormalization,
  CABAC data are read into m_uiValue, shifting all other bits as well as the bypass index.
  Bypass data (if any are needed) are read, shifting all bits further down the register.
At the end of each CABAC packet,
  The bypass index is incremented by 16.
  The bypass packet will now be empty, so CABAC data can be safely read past the end of the packet.

## Slide 7: Decoding a Packet-based Stream
A decoder can be implemented as a shift register.
  CABAC data are read from the front of the register. Bypass data are read from a “bypass index”.
  The decoder also speculatively reads bypass data from (bypass index + 16).
After each renormalization,
  CABAC data are read into m_uiValue, shifting all other bits as well as the bypass index.
  Bypass data (if any are needed) are read, shifting all bits further down the register.
At the end of each CABAC packet,
  The bypass index is incremented by 16.
  The bypass packet will now be empty, so CABAC data can be safely read past the end of the packet.

## Slide 8: Results

## Slide 9: Conclusion
A method has been presented that arranges the CABAC and bypass data into packets.
  This allows the bypass data to be inserted directly into the stream and decoded in parallel with the CABAC data.
  This method has been shown to incur a minimal BD-rate cost.
    Average {Y, U, V} BD-rate changes are {+0.01%, +0.01%, +0.01%}.
  It has also been shown to require only a small increase in software complexity.
    Average {encoding, decoding} time changes are {+0.3%, -0.2%}.
A method that limits outstanding bits has also been proposed.
  This allows the encoder to use only a small “previous bypass pointer” list.
  This method also incurs a minimal cost.
    Average {Y, U, V} BD-rate changes are {+0.01%, +0.02%, +0.02%}.
    Average {encoding, decoding} time changes are {+0.6%, +0.1%}.
We would like to thank Qualcomm for cross-checking our results.
This system is used in proposal JCTVC-G504 “CABAC with Combined Context Variables”.

## Slide 11: Encoding a Packet-based Stream
The encoder uses a buffer that can be written to in multiple places.
  On initialisation, the CABAC write pointer is set to 0 and the bypass write pointer is set to 16.
  The encoder keeps a count of how many CABAC bits the decoder has read after each renormalization.
    The count is initialised to 9 (the size of the decoder’s initial read) and incremented after each renormalization by the number of renormalized bits.
  Each time the encoder detects that the decoder has read 16 CABAC bits:
    The value of the bypass write pointer is noted as bypass_pointer_previous.
    The bypass pointer is incremented by 16.
  When the encoder finishes writing a CABAC packet:
    The CABAC write pointer is set to bypass_pointer_previous.

## Slide 12: Encoding a Packet-based Stream
This encoding process is complicated by the presence of outstanding bits.
  The encoder cannot complete CABAC packets until outstanding bits are resolved.
    Therefore it must maintain a list of pointers to where bypass packets finished.
    Without a limit on outstanding bits, this list could be endless.
A method to limit outstanding bits has been applied.
  The decoder must track m_uiLow as it would appear in the encoder.
  The method is applied after each renormalization.
    If at least 15 bits have collected in a buffer, the entire content of the buffer is considered to form a “group”.
      The group minimum size of 15 bits reduces the software overhead when using a 32-bit m_uiLow buffer.
    The group is checked:
      If the group is all ones and there is no carry, it is added to the outstanding group ‘buffer’.
      Otherwise, any previous buffered groups are flushed and then the current group is buffered.
    When a limit of outstanding groups is reached, the stream is terminated according to the method proposed in JCTVC-G493 “CABAC Stream Termination”.