## Slide 1: CABAC with Arithmetic Context Variables (ACV)
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.
JCTVC-G501

## Slide 2: Introduction
The proposal replaces the look-up tables used in CABAC with arithmetic operations:
  Tables used to update the current Context Variable (CV) state:
    UChar m_aucNextStateMPS [64]
    UChar m_aucNextStateLPS [64]
  Table used to update LPS-range:
    UChar sm_aucLPSTable [128][4]
Our intention is to reduce CABAC complexity / size.
The resulting CVs become actual probabilities.
  These are also used in contribution JCTVC-G504.

## Slide 3: Method 1: Multiplier-based
Change Context Variables (CVs):
  From a 7-bit state to 8-bit state (state0).
  They represent the probability (x256) of a ‘0’.
Replace state update tables (m_aucNextState*PS) with function:
  Function update(state0,value): Let xorVal =(value==1?255:0) Let prob_v =(state0 XOR xorVal) Let increment=Max(1, 13-(((prob_v<<3)-(prob_v))>>7)) Return Min(251, prob_v+increment) XOR xorVal
Replace range-LPS-table (sm_aucLPSTable) with multiplier:
  Let zeroRange = (m_uiRange * CV.state0)>>8
The use of a multiplier on m_uiRange is, however, not ideal:
  It is likely to impact throughput, especially if multiple decodes need to be performed per clock cycle.

## Slide 4: Method 2: Adder-based
Replace the multiplier in ‘Method 1’ with 4+1 adders:
  Approximate the multiplication process:
  If state0≥128 lps=1, lpFraction=256-state0 else lps=0, lpFraction=state0 candidateLPSRanges[4]={ (lpFraction × 9)>>3, (lpFraction ×11)>>3, (lpFraction ×13)>>3, (lpFraction ×15)>>3} lpsRange= candidateLPSRanges[m_uiRange bits 7,6]
LPS/MPS system is again used.
  MPS takes the lower end of the range.
Replaces multiplier on m_uiRange with a multiplexer.
  Method 2 has a similar structure to HM4.0.

## Slide 5: Results
We would like to thank Samsung for cross-checking our results (JCTVC-G934)

## Slide 6: Conclusion
An alternative Context Variable is proposed:
  Number of bits is increased from 7 to 8.
  Replaces look-up tables with arithmetic.
Two systems are described, both using the same 3-adder update system:
  Method 1 (multiplier-based):
    Utilizes a multiplier on the CABAC range.
    An average {Y, U, V} BD-rate change of {0.0%, -1.1%, -1.1%}.
    Processing times are (within error) the same as HM4.0.
  Method 2 (adder-based):
    Utilizes 5 adders (calculation independent on CABAC range) and a multiplexer.
    It is believed that this system is capable of higher throughput than Method 1.
    An average {Y, U, V} BD-rate change of {0.0%, -0.9%, -1.0%}.
    Increase in encoder processing time of 1%.
Method 2 Arithmetic Context Variables (ACV) are used in JCTVC-G504 “CABAC with Combined Context Variables”.

## Slide 8: Adder-based Range Calculation:
In HM4.0, bits {7, 6} of current m_uiRange are used to select the LPS range (out of 4 candidates).
Similarly, the multiplier of ‘Method 1’ can be approximated into four equally sized bands of m_uiRange:
  When m_uiRange is between:
    256 (0b100000000) & 319 (0b100111111), average is 288 (0b100100000)
    320 (0b101000000) & 383 (0b101111111), average is 352 (0b101100000)
    384 (0b110000000) & 447 (0b110111111), average is 416 (0b110100000)
    448 (0b111000000) & 511 (0b111111111), average is 480 (0b111100000)
  i.e. Given a range of m_uiRange values, approximate m_uiRange to the average value and do a fixed multiply.
    e.g. if m_uiRange=370, do (stateLPS*352)>>8 = (stateLPS*11)>>3
  Without knowing m_uiRange in advance, calculate all 4 possible outcomes.
  Select the correct value once m_uiRange is known, using bits {7,6}.
  LPS / MPS system is required, otherwise symbol range may exceed m_uiRange.