## Slide 1: CABAC with Combined Context Variables (CCV)
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.
JCTVC-G504

## Slide 2: Introduction
The aim of this proposal is to encode coefficient data in a Transform Unit (TU) in a single pass, with a constant processing time per coefficient.
  HM4.0:
    Uses up to 3 Context Variables (CVs) to encode a coefficient.
    Requires multiple passes of the data.
    The processing time per coefficient is variable.
      and the decoder may require additional buffering on the output to regulate the decode rate.
The CVs in this proposal are the Arithmetic CVs (ACV) of JCTVC-G501, where the ACVs directly represent the probability of a ‘0’.
The 3 CVs are combined into a 4-symbol alphabet, which is used to encode a coefficient into the CABAC stream with 1 quaternary arithmetic operation.
The escape and sign data are encoded/decoded in parallel with the CABAC data using the CABAC Packet-based Stream proposal (JCTVC-G494).
Problems surrounding speculation are discussed, leading to a proposed system with only 2 levels of speculation.

## Slide 3: Symbol Space
In HM4.0+ACV (JCTVC-G501), up to 3 (8-bit) ACVs per coefficient are used.
  Their meanings are:
    P(m=0), P(m=1 | m>0), P(m=2 | m>1)
    Where ‘m’ is the magnitude of the current coefficient.
  Therefore, combining the conditional probabilities:
    P(m=0) = P(m=0) P(m=1) = (1-P(m=0)) × (P(m=1 | m>0) P(m=2) = (1-P(m=0)-P(m=1)) × P(m=2 | m>2) P(m>2) = (1-P(m=0)-P(m=1)-P(m=2))
  Assuming a 10-bit fractional space (for an 11-bit m_uiRange system),
    F0=(ACV0)<<2 F1=(1024-F0) ×(ACV1) >> 8 F2=(1024-F0-F1) ×(ACV2) >> 8 F3=(1024-F0-F1-F2) Note: All symbols are prevented from being allocated 0 space.

## Slide 4: m_uiRange Calculation
The cumulative fractions in the fractional space could be multiplied with m_uiRange to generate the 4 cumulative symbol ranges.
  However, as discussed in JCTVC-G501, it is better for throughput to use an adder-based MPS/LPS system with only a multiplexer on m_uiRange.
Use the concept of a “first most probable symbol” (FMPS).
  i.e. the first symbol of ‘0’, ‘1’, ‘2’ or ‘>2’ that has at least 25% of the fractional space.
  This symbol is given the remainder of the range space after all other symbols have been allocated.
m_uiRange, m_uiLow & m_uiValue accuracy is increased.
  Combining ACVs into one operation loses accuracy, and it is better if more precision is used.
  No tables are used, and therefore the increase in complexity is small.

## Slide 5: Example decoder implementation
When multiple coefficients are decoded in one cycle, preparation stages are parallelized, but the decoding stages are sequential.

## Slide 6: Speculation
Speculation is required when decoding the worst-case scenario:
  The combination / preparation of ACVs may be dependent on values that have yet to be decoded.
    Therefore, all possible combinations must be prepared, increasing logic.
To reduce the unknown combinations:
  Update ACVs after each group of 16 coefficients.
  When decoding 4:2:0, and future 4:2:2 and 4:4:4 systems, decode 2, 3 and 4 coefficients in parallel (respectively).
    This gives sufficient time to flush the pipeline every 16 coefficients.
    This gives additional time to add gaps in the decoding, thereby removing the problem of speculation on ACV0.
  Remove speculation on ACV1 and ACV2 for large TUs (16x16;32x32).
    Use the same neighbourhood as ACV0 for “c1”, “c2” calculation.
  Reduce speculation to ‘x2’ for ACV1 and ACV2 for smaller TUs.
    Use a 3 neighbourhood and a reduced number of combinations for “c1”, “c2”.

## Slide 7: Results
We would like to thank Samsung for cross-checking our results (JCTVC-G934)

## Slide 8: Conclusion
The Combined Context Variable (CCV) system in combination with ACV (JCTVC-G501) and CABAC Packet-based bit-stream (JCTVC-G494):
  Potentially decodes multiple coefficients per clock at a constant rate.
  A single pass of the data for encoder and decoder.
  Can be designed to decode the worst-case of data even for 4:4:4 system.
    No buffering would be required on the output to regulate rate.
  Uses arithmetic, and not look-up tables for updates to ACVs.
  Speculation can be reduced to ‘x2’ for small blocks; none for larger blocks.
  Requires (illustrative pixel-rate sustained worst case):
    4:2:0 2x2x2 = 8 multipliers [10x8 bit] ; 2x(2x7+24)= 76 adders [~10bit] 4:2:2 3x2x2 = 12 multipliers [10x8 bit] ; 3x(2x7+24)= 114 adders [~10bit] 4:4:4 4x2x2 = 16 multipliers [10x8 bit] ; 4x(2x7+24)= 152 adders [~10bit]
  No significant change in overall coding efficiency or decoder run-time.
Diagonal wavefront processing of LCUs could be applied after CCV entropy decoder to allow subsequent parallel modules to decode blocks.

## Slide 10: Illustration of 4:4:4 ACV0 speculation