## Slide 1
Youngo Park
Chanyul Kim
Il-Koo Kim
Kwang Pyo Choi
JeongHoon Park
(Samsung)
AHG21: Combined signaling for reference picture set (JCTVC-G526)
Notes: <number>

## Slide 2: Current AHG21
If encoder wants to ADD just one reference pictures based on predefined reference picture set (RPS) in picture parameter set (PPS), the only way is to RESEND the whole RPS in slice header
The range of “delta_poc_lt_minus1[i]” is limited up to 216 (65536)
  We can not keep over (216 + 1) long distance reference picture
<number>

## Slide 3: Current AHG21 Syntax
<number>

## Slide 4: Proposed Syntax
<number>

## Slide 5: Proposal
The functionality for adding one or two reference pictures in slice header
  Encode “delta_poc_combined_ref_pic[i]” as SE(V) to represent positive and negative difference
  POC of reference picture will be calculated as “Current POC + delta_poc_combined_ref_pic[i]”
<number>

## Slide 6: Proposal
The functionality for supporting long distance reference picture
  When “delta_poc_combined_ref_pic[i]” is equal to 0, it means that this is special case for long distance reference picture representation
  In this case, read (delta_poc_combined_ref_pic_len_minus16 + 16) bits more
  Then, the read value could be difference POC value for long distance pictures
  If the read value is 0, then read again as the same amount of bits more to extend the delta POC value
<number>

## Slide 7: Proposal
The functionality for supporting long distance reference picture
<number>
Exception
Note: Upper example supposes that the bit length for exception case is 8 bits for simple explanation
It is though that minimum bit length for exception case will be better to be 16 bits

## Slide 8: Conclusion
It is recommended discussing combined signaling in AHG21
It is recommend that the limitation for long-distance picture should be removed
  POC difference should be supported up to Maximum POC value
It is highly recommended that SIMPLE reference picture buffer management and COMPACT syntax is required
  It is asserted that one of motivation in JCTVC-F493 was for decoder simplification
<number>

## Slide 9: Comments on Long-term Reference Picture
In AVC, shot-term and long-term reference picture were differently processed in DPB and decoding process
It is recommended to UNIFY the decoding process for reference pictures for implementation SIMPLICITY while KEEPING the functionality that is referring to long-distance reference picture
  Marked as “long-term reference picture” in DPB via MMCO command
    MMCO command is not valid in AHG21 any more
  MV Scaling
    Consideration for long distance reference picture in MV scaling has no effect
    JCTVC-G551 [Restriction on motion vector scaling for Merge and AMVP]
      0.0%(RAHE) 0.0%(RALC) -0.1%(LDHE) 0.0%(LDLC) -0.1%(LPHE) -0.1%(LPLC)
  Weighted Prediction
    WP is not ready for HM but simple restriction may solve the problem
  Reference picture list initialization
    Reference picture reordering can be sufficient
<number>