## Slide 1: JCTVC-G541: Non-CE9 Simplified scaling calculation method for temporal/spatial MVP of AMVP/Merge
<number>

## Slide 2
<number>
The scaling calculation is conducted to create motion vector predictor for 3 different mode in HM4.0
  Temporal MVP for AMVP, Spatial MVP for AMVP, Temporal MVP for Merge
The scaling is expensive not only in terms of cycles but also in terms of area (JCTVC-F068)
In this proposal, a simplified scaling is applied for each 3 mode, and evaluated the impact to coding efficiency.
Introduction
Legend
DistScaleFactor
mvCol
128
>>
8
clipMv
mvLXCol
FlipFlops
Combinational Block
clip3
32
>>
6
tx
tb
Tx table
128:1
refIdxCol
ListCol
3 cycles / 1 MVscale
3.5Kgates per 1 MV component
1Kgates
GS70, 266MHz
Td
calc
This figure is included in JCTVC-F068

## Slide 3
<number>
diffCur = PicOrderCnt(currPic) - RefPicOrderCnt(currPic, refIdxLX, LX)) diffCol = PicOrderCnt(colPic) – RefPicOrderCnt(colPic, refIdxCol, ListCol))
Simplified Scaling for temporal/spatial MVP
The proposed scaling method is constructed of comparator and bit shift operations
The scaling factor is quantized to a power of 2 based on the two distance diffCur and diffCol
The amount of bit shift is decided according to below figure.
-1
+1
-2
+2
+1
-1
-2
+2
Amount of left shift for scaled MVP
Log2(diffCur/diffCol)
abs(diffCur) >= abs(diffCol)<<2
abs(diffCur) >= abs(diffCol)<<1
abs(diffCur) <<2 <= abs(diffCol)
abs(diffCur) <<1 <= abs(diffCol)
currPic
colPic
refIdxCol
refIdxLX
diffCol
diffCur

## Slide 4
<number>
Flowchart and sample architecture diagram on proposal
1 cycle / 1MV scale
Sample architecture diagram of simplified scaling
Flowchart of simplified scaling
HM4.0:
Multiplier 24 = 2multi / 1MV scale * 2(hor,ver) * 2(L0,L1) * 3pattern(temporal/spatial for AMVP/Merge)
Apply simplified scaling to temporal MVP for AMVP:
Multiplier 16 = 2multi / 1MV scale * 2(hor,ver) * 2(L0,L1) * 2pattern
 about 30% reduction of multiplier

## Slide 5
<number>
Simulation Result (temporal MVP with simplified scaling for AMVP)
Anchor: HM4.0
The proposed method was implemented to HM4.0 software
Apply the simplified scaling to temporal MVP for AMVP
  About 30% reduction of multiplier

## Slide 6
<number>
Simulation Result (spatial MVP with simplified scaling for AMVP)
Anchor: HM4.0
The proposed method was implemented to HM4.0 software
Apply the simplified scaling to spatial MVP for AMVP
    About 30% reduction of multiplier

## Slide 7
<number>
Simulation Result (temporal MVP with simplified scaling for Merge)
Anchor: HM4.0
The proposed method was implemented to HM4.0 software
Apply the simplified scaling to temporal MVP for Merge
    About 30% reduction of multiplier

## Slide 8
<number>
Simplified scaling method, which is constructed of comparator and bit shift, was proposed for spatial/temporal MVP of AMVP/Merge
In the case of applying it to temporal MVP in AMVP, the proposed method can reduce the number of multiplier significantly while keeping BD rate loss in the range of 0.0%-0.1%
We suggest to consider the future adoption of the proposed method based on the study in a CE
Conclusion