## Slide 1: JCTVC-G542: Non-CE9/Non-CE13 Simplification on AMVP/Merge
<number>

## Slide 2
<number>
This proposal includes the following three simplifications on AMVP/Merge
  On avoiding merging candidate decision [simplification1]
    Same proposal as JCTVC-G681
  On AMVP spatial scaling candidate [simplification2]
  On zero motion vector merging candidate [simplification3]
Introduction

## Slide 3
<number>
PU2
PU0
PU1
PU1
PU0
PU1
In creating merging candidate list for PU1 of rectangular PartMode,
1. the motion parameters of the neighboring PU_N is checked whether it’s identical to that of PU0
2. if it’s true, that neighboring PU_N is not added into merging candidate list
avoid
avoid
PU0
avoid
avoid
PU3
PU2
avoid
PU0
PU1
PU3
avoid
On avoiding merging candidate decision [simplification1]
HM4.0
PU0
PU1
PU0
PU0
PU1
avoid
PU0
PU3
PU2
avoid
Decide the avoided neighboring PU by using only PartMode of the current PU
1. For the case of PU1 of PART_2NxN, PART_2NxnU, PART_2NxnD, neighboring PU_B1 is not added into merging candidate list
2. For the case of PU1 of PART_Nx2N, PART_nLx2N and PART_nRx2N, neighboring PU_A1 is not added into merging candidate list
Reduce the complexity on checking motion parameters
simplification1
merging candidate
target PU
avoid
merging candidate
target PU
A0
A1
B0
B1
B2
A0
A1
B0
B1
B2

## Slide 4
<number>
Simulation Result of simplification1
Anchor: HM4.0
The proposed method was implemented to HM4.0 software
Negligible loss was observed

## Slide 5
In creating AMVP candidate list, to use scaling calculation for upper positions is allowed only if left positions were not available or the scaling calculation was not used
If a parallel derivation of the spatial candidates is assumed, this dependency would produce some waiting time to derive the spatial candidate of upper position
HM4.0
Only if all PUs in left position are not available or all PredMode are MODE_INTRA
 The parameter isScaledFlagLX is set to 0 and the scaling calculation is allowed to use for upper position
Remove dependency for a parallel derivation of spatial candidates
simplification2
On AMVP spatial scaling candidate [simplification2]

## Slide 6
<number>
Anchor: HM4.0
The proposed method was implemented to HM4.0 software
No loss was observed
Simulation Result of simplification2

## Slide 7
On zero motion vector merging candidate [simplification3]
In adding zero motion vector merging candidate, it’s checked whether that new candidate has already been included in the mergeCandList
 Checking process would cause some complexity issues
HM4.0
Remove checking process from the derivation process of zero vector merging candidate
Remove the parameter zeroCnt, which indicates the maximum number of the duplicate checking
All available zeroCand are added to the mergeCandList in order not to produce empty space in it
Reduce the number of duplicate checking process
simplification3
Remove duplicate checking process
Remove zeroCnt

## Slide 8
<number>
Anchor: HM4.0
The proposed method was implemented to HM4.0 software
No loss was observed
Simulation Result of simplification3

## Slide 9
<number>
Anchor: HM4.0
The proposed method was implemented to HM4.0 software
No loss was observed
Simulation Result of combination on simplification1,2,3

## Slide 10
<number>
Three simplification on AMVP/Merge are proposed
It show almost no loss for all test conditions with reducing complexity on HM4.0
We suggest the proposed method be adopted in the HM/WD of HEVC
Conclusion

## Slide 11
Anchor: side activity on simplification of 2nd pruning process
JCTVC-G397 reports that removing all 2nd duplication checking process on merging candidate list only brings about 0.1% loss
The proposed simplification3 method was combined to JCTVC-G397
Negligible loss was observed
Additional Simulation Result of combination JCTVC-G397 + simplification3