## Slide 1: Syntax refinements for ALF and SAO
Semih Esenlik
Matthias Narroschke
Thomas Wedi
Panasonic Corporation
7th JCT-VC meeting, Geneva 21.-30. December 2011

## Slide 2: Outline
Two modifications in the slice header are proposed:
  Part 1: Introduce adaptive_loop_filter_flag and sample_adaptive_offset_flag in slice header.
  Part 2: Change the coding method for alf_cu_control_flag.

## Slide 3: Part 1
Introduction of adaptive_loop_filter_flag and sample_adaptive_offset_flag in slice header

## Slide 4
Part 1: APS structure
aps_rbsp( ) { | Descriptor
aps_id | ue(v)
aps_sample_adaptive_offset_flag | u(1)
aps_adaptive_loop_filter_flag | u(1)
if( aps_sample_adaptive_offset_flag ¦¦ aps_adaptive_loop_filter_flag ) { | 
aps_cabac_use_flag | u(1)
if( aps_cabac_use_flag ) { | 
aps_cabac_init_idc | ue(v)
aps_cabac_init_qp_minus26 | se(v)
} | 
} | 
if(aps_sample_adaptive_offset_flag ) { | 
sao_data_byte_count | u(12)
byte_align() | 
sao_param() | ae(v)
if(aps_adaptive_loop_filter_flag) | 
byte_align() | 
} | 
if(aps_adaptive_loop_filter_flag) { | 
alf_data_byte_count | u(8)
byte_align () | 
alf_param() | ae(v)
} | 
rbsp_trailing_bits( ) | 
} | 

## Slide 5
Part 1: Problem Statement
slice_header( ) { | Descriptor
lightweight_slice_flag | u(1)
if( !lightweight_slice_flag ) { | 
slice_type | ue(v)
pic_parameter_set_id | ue(v)
if( sample_adaptive_offset_enabled_flag ¦¦ adaptive_loop_filter_enabled_flag ) | 
aps_id | 
frame_num | u(v)
…….. | …
} | 
if( entropy_coding_mode_flag && slice_type != I) | 
cabac_init_idc | ue(v)
first_slice_in_pic_flag | u(1)
... | 
... | 
if( adaptive_loop_filter_enabled_flag && aps_adaptive_loop_filter_flag ) { | 
byte_align() | 
alf_cu_control_param( ) | ae(v)
byte_align() | 
} | 
} | 
Signalled in APS
Parsing dependency between slice header and APS.

## Slide 6
Part 1: Solution
slice_header( ) { | Descriptor
lightweight_slice_flag | u(1)
if( !lightweight_slice_flag ) { | 
slice_type | ue(v)
pic_parameter_set_id | ue(v)
if( sample_adaptive_offset_enabled_flag ¦¦ adaptive_loop_filter_enabled_flag ) | 
if(adaptive_loop_filter_enabled_flag ) | 
adaptive_loop_filter_flag | u(1)
if(sample_adaptive_offset_enabled_flag ) | 
sample_adaptive_offset_flag | u(1)
if(sample_adaptive_offset_flag ¦¦ adaptive_loop_filter_flag) | 
aps_id | 
frame_num | u(v)
…….. | …
} | 
if( entropy_coding_mode_flag && slice_type != I) | 
cabac_init_idc | ue(v)
first_slice_in_pic_flag | u(1)
... | 
... | 
if( adaptive_loop_filter_enabled_flag && adaptive_loop_filter_flag) { | 
byte_align() | 
alf_cu_control_param( ) | ae(v)
byte_align() | 
} | 
} | 
Introduce ALF flag in slice header
Introduce SAO flag in slice header
Parsing dependency is resolved
APS syntax structure is not changed

## Slide 7: Benefits
Parsing robustness and parallel parsing
Parsing robustness
Parsing dependency of slice header on APS is eliminated. A loss in APS only hinders SAO and ALF operations and not cause catastrophic parsing errors.
Parallel parsing
The parsing of slice data need not be delayed till the APS is parsed.

## Slide 8: Benefits
APS
aps_adaptive_loop_filter_flag
aps_sample_adaptive_offset_flag
Slice Header 1
adaptive_loop_filter_flag
sample_adaptive_offset_flag
Slice Header 2
adaptive_loop_filter_flag
sample_adaptive_offset_flag
Slice Header 3
adaptive_loop_filter_flag
sample_adaptive_offset_flag
adaptive_loop_filter_flag can overwrite aps_adaptive_loop_filter_flag
sample_adaptive_offset_flag can overwrite aps_sample_adaptive_offset_flag
Especially beneficial sub-optimal filter design is used in encoder.
Slice level local adaptation for SAO and ALF
Slices of a frame

## Slide 9: Benefits
Reuse of filter coefficients
APS 1
ALF parameters
SAO parameters
Frame 1
adaptive_loop_filter_flag = 1
sample_adaptive_offset_flag = 1
Frame 2
adaptive_loop_filter_flag = 1
sample_adaptive_offset_flag = 0
Example: Using ALF parameters in APS reduces MSE in Frame 2 whereas SAO parameters increase MSE.

## Slide 10: Benefits
Reduction in APS NAL unit transmission
If both sample_adaptive_offset_flag and adaptive_loop_filter_flag are off, then no aps_id and APS NAL unit need to be transmitted.
Reduction in clock cycles
The state of ALF and SAO are now signalled in slice header. If SAO and ALF are both off, there is no need for fetching and parsing an APS.
Reduction of decoding latency
If SAO and ALF are known to be off for a slice, the decoded frame can be outputted without waiting for the corresponding APS.

## Slide 11: Simulation results for Part 1
HM4.0-dev-misc R1423.
1500Byte slices.

## Slide 12: Part 2
Changing the coding method of alf_cu_control_flag

## Slide 13
Problem Statement
slice_header( ) { | Descriptor
lightweight_slice_flag | u(1)
if( !lightweight_slice_flag ) { | 
slice_type | ue(v)
pic_parameter_set_id | ue(v)
if( sample_adaptive_offset_enabled_flag ¦¦ adaptive_loop_filter_enabled_flag ) | 
if(adaptive_loop_filter_enabled_flag ) | 
adaptive_loop_filter_flag | u(1)
if(sample_adaptive_offset_enabled_flag ) | 
sample_adaptive_offset_flag | u(1)
if(sample_adaptive_offset_flag ¦¦ adaptive_loop_filter_flag) | 
aps_id | 
frame_num | u(v)
…….. | …
} | 
if( entropy_coding_mode_flag && slice_type != I) | 
cabac_init_idc | ue(v)
first_slice_in_pic_flag | u(1)
... | 
... | 
if( adaptive_loop_filter_enabled_flag && adaptive_loop_filter_flag) { | 
byte_align() | 
alf_cu_control_param( ) | ae(v)
byte_align() | 
} | 
} | 
alf_cu_control_flag
is signalled inside alf_cu_control_param()

## Slide 14: Problem statement
alf_cu_control_flag is used to signal if CU-based ALF adaptation is used or not. However it is signalled inside alf_cu_control_param() structure.
If CU-based ALF adaptation is off, alf_cu_control_param( ) consists of a single bit. However CABAC termination bits and byte alignment padding bits need to be appended at the end, increasing the bitrate.

## Slide 15
Solution
slice_header( ) { | Descriptor
lightweight_slice_flag | u(1)
if( !lightweight_slice_flag ) { | 
slice_type | ue(v)
pic_parameter_set_id | ue(v)
if( sample_adaptive_offset_enabled_flag ¦¦ adaptive_loop_filter_enabled_flag ) | 
if(adaptive_loop_filter_enabled_flag ) | 
adaptive_loop_filter_flag | u(1)
if(sample_adaptive_offset_enabled_flag ) | 
sample_adaptive_offset_flag | u(1)
if(sample_adaptive_offset_flag ¦¦ adaptive_loop_filter_flag) | 
aps_id | 
frame_num | u(v)
…….. | …
} | 
if( entropy_coding_mode_flag && slice_type != I) | 
cabac_init_idc | ue(v)
first_slice_in_pic_flag | u(1)
... | 
if( adaptive_loop_filter_enabled_flag && adaptive_loop_filter_flag) | 
alf_cu_control_flag | u(1)
if( adaptive_loop_filter_enabled_flag && adaptive_loop_filter_flag && alf_cu_control_flag) { | 
byte_align() | 
alf_cu_control_param( ) | ae(v)
byte_align() | 
} | 
} | 
alf_cu_control_flag is taken out of CABAC codeword and signalled before.

## Slide 16
Solution, continud
alf_cu_control_param() { | Descriptor
if( adaptive_loop_filter_flag ) { | 
alf_cu_control_flag | u(1)
if( alf_cu_control_flag ) { | 
alf_cu_control_max_depth | ue(v)
alf_length_cu_control_info | se(v)
for( i = 0; i < NumAlfCuFlag; i++ ) | 
alf_cu_flag[ i ] | u(1) ¦ ae(v)
} | 
} | 
} | 
By coding alf_cu_control_flag before the CABAC codeword, termination and padding bits can be saved.
CABAC engine is used less often.

## Slide 17: Simulation results for Part 1 and Part 2
HM4.0-dev-misc R1423.
1500Byte slices.

## Slide 18: Conclusion
Motivations:
Part 1: Introduction of adaptive_loop_filter_flag and sample_adaptive_offset_flag in slice header
Benefits:
Parsing robustness and slice level local adaptation for SAO and ALF
Part 2: Changing the coding method of alf_cu_control_flag
Benefits:
Coding gain via elimination of CABAC termination and byte alignment padding bits.
Proposed to be adopted for next version of HM.