## Slide 1: JCTVC-G568
Marko Viitanen, Jarno Vanne, Timo D. Hämäläinen
Tampere University of Technology
Jani Lainema, Kemal Ugur
Nokia
HM 4.0 entropy coding complexity considerations

## Slide 2: Introduction
Analyzed the HM 4.0 implementations of CABAC and CAVLC decoding
Cycle count as complexity measure
Identified some obsolete code and unnecessary division operation in CAVLC decoding – proposing to remove those
Processor | Intel Core 2 Duo E8400 (2 × 3.0 GHz)
Memory | 8 GB
L1 Cache | 2 × 32 KB (instruction) + 2 × 32 KB (data)
L2 Cache | 6 MB
Compiler | Microsoft Visual C++ 2010
OS | Microsoft Windows 7 Enterprise Service Pack 1
VTune | Amplifier XE 2011

## Slide 4: Summary of results
Removal of the obsolete code and division in CAVLC
Cycle count savings in CAVLC funtions with respect to HM 4.0 anchor:
QP | AI_LC | RA_LC | LB_LC | LP_LC
22 | -5.0 % | -7.7 % | -9.1 % | -8.2 %
27 | -5.4 % | -11.8 % | -14.9 % | -14.2 %
32 | -6.0 % | -14.4 % | -17.0 % | -17.3 %
37 | -6.5 % | -14.4 % | -18.6 % | -18.4 %
Avg. | -5.5 % | -10.3 % | -12.7 % | -12.0 %

## Slide 5: Summary of results
Cycle count increase of CABAC as compared to CAVLC cycle count (after removing obsolete code and unnecessary division operation in CAVLC)
QP | AI_LC | RA_LC | LB_LC | LP_LC
22 | 83.5% | 55.4% | 42.0% | 45.9%
27 | 61.2% | 33.1% | 14.4% | 16.9%
32 | 42.8% | 17.1% | -5.9% | -3.5%
37 | 24.7% | 4.9% | -18.5% | -17.8%
Avg. | 53.1% | 27.6% | 8.0% | 10.4%