## Slide 1: JCTVC-G569
Jani Lainema, Kemal Ugur, Antti Hallapuro
Nokia
Single entropy coder for HEVC with a high throughput binarization mode

## Slide 2: Background
Goal: Have a single entropy coding engine that supports both low complexity and high efficiency
CABAC gives good coding efficiency but its throughput remains a challenge (JCTVC-G659)
  CABAC: ~1 bin / cycle
  CAVLC: at least one codeword / cycle
The bottleneck appears to be most severe in coefficient coding at high bitrates
Proposal: Have CABAC as the single entropy coding engine with an option to code coefficients in high-throughput mode.

## Slide 3: Background
Example: Software decoder complexity distribution, Racehorses, QP 32 (as reported by Samsung in JCTVC-G988)
  At lower QP’s the Entropy Coding will dominate the complexity even more

## Slide 4: Example
Coded bins: HM 4.0 RA_LC with CABAC as entropy coder

## Slide 5: Proposal
Have CABAC as the single entropy coding engine
Have two binarization schemes for the coefficient data
  High efficiency binarization (HEB)
  High throughput binarization (HTB)
High efficiency binarization
  HM 4.0 CABAC binarization
High throughput binarization
  HM 4.0 CAVLC binarization
  Binarized data fed into CABAC bypass

## Slide 6: HM 4.0 design

## Slide 7: Proposal

## Slide 8: Compression efficiency results
 | All Intra HE |  |  | All Intra LC |  | 
 | Y | U | V | Y | U | V
Class A | 4.9 | 2.2 | 1.6 | -1.0 | 3.8 | 3.9
Class B | 4.6 | 1.3 | 1.0 | -1.4 | 2.3 | 2.9
Class C | 3.9 | 1.2 | 1.3 | -0.7 | 1.9 | 2.1
Class D | 3.7 | 0.6 | 0.5 | -0.3 | 1.8 | 1.8
Class E | 5.1 | 0.8 | 0.3 | -2.6 | 8.0 | 6.9
Overall | 4.4 | 1.2 | 1.0 | -1.1 | 3.3 | 3.3
Enc Time[%] | 104 % |  |  | 113 % |  | 
Dec Time[%] | 99 % |  |  | 103 % |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 6.8 | -1.3 | -0.2 | -2.1 | 5.6 | 6.1
Class B | 4.6 | 0.4 | 0.6 | -3.1 | 4.0 | 5.4
Class C | 3.9 | 0.7 | 1.1 | -1.7 | 2.7 | 3.7
Class D | 3.2 | -0.4 | -0.2 | -1.4 | 3.7 | 4.0
Class E |  |  |  |  |  | 
Overall | 4.6 | -0.1 | 0.3 | -2.1 | 4.0 | 4.8
Enc Time[%] | 101 % |  |  | 106 % |  | 
Dec Time[%] | 101 % |  |  | 102 % |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 4.5 | 0.8 | 0.4 | -2.9 | 6.8 | 10.7
Class C | 3.5 | 0.4 | 1.2 | -1.9 | 4.9 | 6.6
Class D | 3.1 | 0.3 | 0.8 | -1.6 | 8.8 | 9.2
Class E | 1.9 | 0.7 | 0.3 | -5.1 | 7.9 | 8.9
Overall | 3.4 | 0.5 | 0.7 | -2.7 | 7.0 | 9.0
Enc Time[%] | 100 % |  |  | 105 % |  | 
Dec Time[%] | 101 % |  |  | 102 % |  | 
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 4.0 | 0.2 | 0.3 | -3.5 | 7.5 | 11.4
Class C | 3.4 | 0.2 | 1.2 | -2.1 | 5.3 | 7.3
Class D | 3.1 | -0.3 | 0.3 | -1.7 | 8.3 | 9.1
Class E | 1.7 | 0.5 | -0.2 | -5.5 | 9.2 | 9.5
Overall | 3.2 | 0.1 | 0.4 | -3.1 | 7.5 | 9.4
Enc Time[%] | 100 % |  |  | 106 % |  | 
Dec Time[%] | 101 % |  |  | 102 % |  | 

## Slide 9: Summary of the throughput increase
Ratio of context adaptive coded bins in HTB vs HM 4.0 HE
QP | AI_HE | RA_HE | LB_HE | LP_HE | Aver. | Saving
2 | 4 % | 6 % | 6 % | 6 % | 6 % | 94 %
7 | 8 % | 10 % | 11 % | 10 % | 10 % | 90 %
12 | 11 % | 15 % | 14 % | 14 % | 13 % | 87 %
17 | 13 % | 19 % | 19 % | 19 % | 17 % | 83 %
22 | 17 % | 25 % | 28 % | 28 % | 25 % | 75 %
27 | 23 % | 35 % | 42 % | 42 % | 35 % | 65 %
32 | 30 % | 27 % | 54 % | 54 % | 41 % | 59 %
37 | 38 % | 56 % | 64 % | 64 % | 56 % | 44 %

## Slide 10: Example of throughput improvements

## Slide 11: Benefits of the proposed approach
Removes the HEVC throughput bottlenecks
  Reduced number of coded bins by 88% in low QP range, 61% in common conditions QP range
Compared to CAVLC, the coding efficiency is improved by
  -1.1% / -2.1% / -2.7% / -3.1 % for AI / RA / LB / LP (LC)
Very lightweight compared to full CAVLC:
  Uses ~30% of the CAVLC related syntax elements
  Uses ~15% of the CAVLC related tables (~700 bytes)
Additional benefits
  Reduces the actual coded bins and context modeling significantly
  Uses bypass for the simplified bins
  Allow multiple bins to be decoded at once
  Allows encoder to dynamically change the complexity/efficiency tradeoff