## Slide 1: Byte alignment overhead reduction
Semih Esenlik
Matthias Narroschke
Thomas Wedi
Panasonic Corporation
7th JCT-VC meeting, Geneva 21.-30. December 2011

## Slide 2: Outline
Background and problem about byte alignment
New coding tool: Byte aligned variable length coding
Simulation results

## Slide 3
Background: Byte alignment
Byte alignment is used to facilitate EPB insertion.
Used mainly before CABAC codewords.
Each byte alignment operation causes 3.5 bits expansion on average.

## Slide 4
Problem: Bitrate expansion due to byte alignment
aps_rbsp( ) { | Descriptor
aps_id | ue(v)
aps_sample_adaptive_offset_flag | u(1)
aps_adaptive_loop_filter_flag | u(1)
if( aps_sample_adaptive_offset_flag ¦¦ aps_adaptive_loop_filter_flag ) { | 
aps_cabac_use_flag | u(1)
if( aps_cabac_use_flag ) { | 
aps_cabac_init_idc | ue(v)
aps_cabac_init_qp_minus26 | se(v)
} | 
} | 
if(aps_sample_adaptive_offset_flag ) { | 
sao_data_byte_count | u(12)
byte_align() | 
sao_param() | ae(v)
if(aps_adaptive_loop_filter_flag) | 
byte_align() | 
} | 
if(aps_adaptive_loop_filter_flag) { | 
alf_data_byte_count | u(8)
byte_align () | 
alf_param() | ae(v)
} | 
rbsp_trailing_bits( ) | 
} | 

## Slide 5
Solution: Byte aligned variable length coding
A new variable length coding method: The codeword length increases in increments of 8 bits.
  Hence achieves byte alignment automatically.
  Need for explicit byte alignment is eliminated.
Indicated by
  ub(v) (for unsigned int)
  ib(v) (for signed int)
X
X
X
X
0
0
0
0
Example, Coding of unsigned integer: 5600
Termination bit = 0
1
0
1
0
0
0
0
1
Termination bit = 1
0
0
1
1
1
1
0
0
Termination bit = 0
Bits belonging to previous syntax element

## Slide 6
Usage of ub(v) in APS
aps_rbsp( ) { | Descriptor
aps_id | ue(v)
aps_sample_adaptive_offset_flag | u(1)
aps_adaptive_loop_filter_flag | u(1)
if( aps_sample_adaptive_offset_flag ¦¦ aps_adaptive_loop_filter_flag ) { | 
aps_cabac_use_flag | u(1)
if( aps_cabac_use_flag ) { | 
aps_cabac_init_idc | ue(v)
aps_cabac_init_qp_minus26 | se(v)
} | 
} | 
if(aps_sample_adaptive_offset_flag ) { | 
sao_data_byte_count | ub(v) u(12)
byte_align() | 
sao_param() | ae(v)
if(aps_adaptive_loop_filter_flag) | 
byte_align() | 
} | 
if(aps_adaptive_loop_filter_flag) { | 
alf_data_byte_count | ub(v) u(8)
byte_align () | 
alf_param() | ae(v)
} | 
rbsp_trailing_bits( ) | 
} | 
Byte alignment achieved automatically
Byte alignment achieved automatically
Byte alignment achieved automatically
Byte alignment achieved automatically

## Slide 7
Usage of ub(v) in APS
aps_rbsp( ) { | Descriptor
aps_id | ue(v)
aps_sample_adaptive_offset_flag | u(1)
aps_adaptive_loop_filter_flag | u(1)
if( aps_sample_adaptive_offset_flag ¦¦ aps_adaptive_loop_filter_flag ) { | 
aps_cabac_use_flag | u(1)
if( aps_cabac_use_flag ) { | 
aps_cabac_init_idc | ue(v)
aps_cabac_init_qp_minus26 | se(v)
} | 
} | 
if(aps_sample_adaptive_offset_flag ) { | 
sao_data_byte_count | ub(v)
byte_align() | 
sao_param() | ae(v)
if(aps_adaptive_loop_filter_flag) | 
byte_align() | 
} | 
if(aps_adaptive_loop_filter_flag) { | 
alf_data_byte_count | ub(v)
byte_align () | 
alf_param() | ae(v)
} | 
rbsp_trailing_bits( ) | 
} | 
Explicit byte alignment is not required anymore

## Slide 8: Usage of ib(v) in Slice Header
slice_header( ) { | Descriptor
lightweight_slice_flag | u(1)
… | 
… | 
if( entropy_coding_mode_flag && slice_type != I) | 
cabac_init_idc | ue(v)
first_slice_in_pic_flag | u(1)
if( first_slice_in_pic_flag == 0 ) | 
slice_address | u(v)
if( !lightweight_slice_flag ) { | 
slice_qp_delta | se(v)
if( deblocking_filter_control_present_flag ) { | 
disable_deblocking_filter_idc | 
if( disable_deblocking_filter_idc != 1 ) { | 
slice_alpha_c0_offset_div2 | 
slice_beta_offset_div2 | 
} | 
} | 
if( slice_type = = B ) | 
collocated_from_l0_flag | u(1)
} | 
if( !lightweight_slice_flag ) { | 
slice_qp_delta | ib(v)
} | 
byte_align() | 
if( adaptive_loop_filter_enabled_flag && aps_adaptive_loop_filter_flag ) { | 
alf_cu_control_param( ) | 
byte_align() | 
} | 
} | 
Byte aligned variable length codes for signed integer

## Slide 9: Simulation results
HM4.0-dev-misc R1423.
1500Byte slices.

## Slide 10: Simulation results for low-bitrate scenario
HM4.0-dev-misc R1423
1500Byte slices
Data points:
QP 31, 34, 37 and 40

## Slide 11: Conclusion
Motivation:
Reduction of byte alignment padding bits
Proposal
New coding method: Byte aligned variable length coding
Proposed to be adopted for next version of HM.

## Slide 12: Backup

## Slide 13: Bitrate comparison with exp-golomb code
Average code length | Bit string form |  | Range of codeNum
 | Largest codeword | Smallest codeword | 
5.5 | 0 x0 0 0 0 0 0 0 1 | x0 1 | 0..1
6.5 | x0 0 x1 0 0 0 0 0 0 1 | x0 x1 1 | 2..3
7.5 | x0 x1 0 x2 0 0 0 0 0 0 1 | x0 x1 x2 1 | 4..7
8.5 | x0 x1 x2 0 x3 0 0 0 0 0 0 1 | x0 x1 x2 x3 1 | 8..15
9.5 | x0 x1 x2 x3 0 x4 0 0 0 0 0 0 1 | x0 x1 x2 x3 x4 1 | 16..31
10.5 | … | … | 32..63
11.5 |  |  | 64..125
13.5 |  |  | 126..255
14.5 |  |  | 256..511
Code length + 3.5 average byte alignment bits | Bit string form | Range of codeNum
4.5 | 1 | 0
6.5 | 0 1 x0 | 1..2
8.5 | 0 0 1 x1 x0 | 3..6
10.5 | 0 0 0 1 x2 x1 x0 | 7..14
12.5 | 0 0 0 0 1 x3 x2 x1 x0 | 15..30
14.5 | 0 0 0 0 0 1 x4 x3 x2 x1 x0 | 31..62
16.5 | … | 63..126
18.5 | … | 127..254
20.5 | … | 255..510
Exp-Golomb code
Byte-aligned variable length code