## Slide 1: CE12 Subtest 5: Deblocking filter using adaptive weighting factors
Matthias Narroschke, Ann-Kathrin Seifert
Panasonic Corporation
7th JCT-VC meeting, Geneva 21.-30. November 2011

## Slide 2: Outline
Introduction
Deblocking filter using adaptive weighting factors
Estimation of weighting factors
Experiments and results
Conclusion

## Slide 3: Deblocking filter according to HM4.0
Deblocking of a reconstructed sample :
: Value by which a sample value is modified
Problem:
is generated by a fixed filter
=> No adaptation to varying signal statistics possible

## Slide 4: Deblocking filter using adaptive weighting factors
Adaptation to varying signal statistics by adaptive weighting factor :
Luminance: Individual weighting factors
  Strong and weak filtering
  Distance to block boundary
Chrominance: No weighting factors
Total: 5 weighting factors

## Slide 5: Estimation of weighting factors
Objective estimation: Minimization of mean squared error (MSE) for all samples:
Subjective estimation: Minimization of MSE for subjective important samples:
=> Considered as subjective important

## Slide 6: Coding of estimated weighting factors
Quantization with step size of 1/64
Coding of the 5 quantized weighting factors:
  Slice header
  No arithmetic coding

## Slide 7: Objective results for objective estimation
Configuration | BD-Bit rate [%] |  | Encoder run time ratio [%] |  | Decoder run time ratio [%] | 
 | Common QPs | High QPs | Common QPs | High QPs | Common QPs | High QPs
I HE | -0.4 | -0.3 | 100 | 99 | 101 | 100
I LC | -0.2 | -0.2 | 101 | 102 | 100 | 100
RA HE | -0.3 | -0.2 | 100 | 100 | 99 | 100
RA LC | -0.2 | -0.2 | 100 | 100 | 100 | 101
LDB HE | -0.5 | -0.2 | 100 | 101 | 102 | 100
LDB LC | -0.2 | -0.1 | 100 | 100 | 100 | 100
LDP HE | -0.3 | -0.1 | 100 | 98 | 101 | 100
LDP LC | -0.1 | -0.1 | 100 | 98 | 100 | 98

## Slide 8: Objective results for subjective estimation
Configuration | BD-Bit rate [%] |  | Encoder run time ratio [%] |  | Decoder run time ratio [%] | 
 | Common QPs | High QPs | Common QPs | High QPs | Common QPs | High QPs
I HE | -0.3 | -0.1 | 101 | 101 | 101 | 101
I LC | -0.2 | -0.0 | 102 | 102 | 101 | 101
RA HE | -0.1 | 0.3 | 99 | 100 | 100 | 100
RA LC | -0.1 | 0.3 | 100 | 100 | 100 | 100
LDB HE | -0.2 | 0.6 | 100 | 100 | 100 | 100
LDB LC | -0.0 | 0.5 | 100 | 100 | 100 | 100
LDP HE | -0.1 | 0.6 | 100 | 100 | 100 | 100
LDP LC | -0.0 | 0.5 | 101 | 100 | 100 | 100

## Slide 9: Subjective results for subjective estimation
HM4.0
JCTVC-G574
Cactus, LD HE, QP42, Frame 50

## Slide 10: Subjective results for subjective estimation
HM4.0
JCTVC-G574
RaceHorses, LD HE, QP42, Frame 195

## Slide 11: Conclusion
Introduction of adaptive weighting factors in the deblocking filter to adapt to varying signal statistics
Estimation of weighting factors by minimization of mean squared reconstruction error
Coding and transmission of estimated weighting factors
Results compared to HM4.0:
  Objective estimation: 0.3% bit rate reduction in average
  Subjective estimation: 0.1% bit rate reduction in average
  Increased subjective quality
  Approximately same run time
Proposal: Inclusion into next version of WD and HM