## Slide 1: JCTVC-G582 Multiview HEVC – experimental results
Chair of Multimedia Telecommunications and Microelectronics
Poznan University of Technology
Marek Domański Tomasz Grajek Damian Karwowski Krzysztof Klimaszewski
Jacek Konieczny Maciej Kurc Adam Łuczak Robert Ratajczak Jakub Siast
Olgierd Stankiewicz Jakub Stankowski Krzysztof Wegner
Notes: cmt

## Slide 2: Introduction
Multiview HEVC
Coding scheme similar to MVC
HM 3.0 based
Base view compliant with HEVC
Minimum interference in software structure
Easy portable to higher HM version
No additional complexity (merely additional reference frames)

## Slide 3: Coding scheme
Coding scheme similar to MVC
  inter-view prediction
  inter-view reference frames on reference list

## Slide 4: Test sequences
Sequences from Call for Proposals (CfP) on 3D Video Coding (3DVC)
Two classes:
  Class A
    2 natural and 2 synthetic (rendered)
    FullHD (1920x1088) resolution
    25 FPS
  Class C
    natural sequences
    XGA (1024x768) resolution
    30 FPS

## Slide 5: Coding scenarios
Call for Proposals (CfP) on 3D Video Coding (3DVC)
2-view case
  stereoscopic pair of views
  intended to display on stereoscopic monitor
3-view case
  intended to use in auto-stereoscopic displays
2-view case
3-view case

## Slide 6: Results
Performance of multiview HEVC compared to simulcast HEVC (HM 3.0) |  |  |  |  |  | 
 | RA-HE 2-view case |  |  | RA-HE 3-view case |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Class A | -26,8 | -27,0 | -26,9 | -35.5 | -35.4 | -35.1
Class C | -18.6 | -15.1 | -16.4 | -25.5 | -22.1 | -23.5
Overall | -22.7 | -21.1 | -21.7 | -30.5 | -28.8 | -29.3
 | -22.6 | -21.1 | -21.7 | -30.4 | -28.8 | -29.3
Enc Time | 113% |  |  | 126% |  | 
Dec Time | 96% |  |  | 97% |  | 

## Slide 7: Views and sequences details 3-view case
Performance of multiview HEVC compared to simulcast HEVC (HM 3.0) |  |  |  |  |  | 
 | RA-HE 1st dependent view |  |  | RA-HE 2nd dependent view |  | 
 | Y BD-rate | U BD-rate | V BD-rate | Y BD-rate | U BD-rate | V BD-rate
Poznan_Hall2 | -22.7 | -16.6 | -21.8 | -46.6 | -42.0 | -41.8
Poznan_Street | -36.6 | -37.3 | -31.9 | -64.2 | -64.7 | -63.5
Undo_Dancer | -50.2 | -52.9 | -51.9 | -73.2 | -75.6 | -74.6
GT_Fly | -52.9 | -54.1 | -54.3 | -78.3 | -79.1 | -79.2
Kendo | -21.8 | -14.3 | -19.3 | -51.8 | -46.1 | -48.0
Balloons | -30.4 | -25.6 | -27.3 | -51.5 | -47.8 | -50.7
Lovebird1 | -36.3 | -32.2 | -33.0 | -52.1 | -48.7 | -49.5
Newspaper | -16.0 | -13.8 | -15.3 | -50.3 | -45.7 | -46.9
Overall | -33.4 | -30.9 | -31.9 | -58.5 | -56.2 | -56.8