## Slide 1: CE12 Subtest 1: Results for modified decisions for deblocking
Matthias Narroschke, Thomas Wedi, Semih Esenlik
Panasonic Corporation
7th JCT-VC meeting, Geneva 21.-30. November 2011

## Slide 2: Outline
Introduction
Simplified decisions
Experiments and results
Conclusion

## Slide 3: Reference: HM4.0
One on/off decision for all 8 lines based on two lines
Individual strong/weak decision for each of the 8 lines

## Slide 4: Proposal: Simplified decisions
Separation of 8-line segment into two 4-line segments
One on/off decision for each 4 lines
One strong/weak decision for each 4 lines
  Strong filter for both lines => Strong filter for all 4 lines
  Else => Weak filter for all 4 lines

## Slide 5: Comparison to HM4.0
BD-bit rate and run time ratios
Average bit rate reduction of proposal: 0.1%

## Slide 6: Comparison to HM4.0
Number of decision operations
 | HM4.0 | Proposal
On-/Off | 20 | 40
Strong/Weak | 96 | 52
Sum | 116 | 92
20% less operations

## Slide 7: Comparison to HM4.0
4 Lines: Horizontal filter performed after vertical decision
1 Line required to decide horizontal filter
=> Decision line buffer required
HM4.0
4 Lines: Horizontal filter performed after vertical decision
=> No decision line buffer required
Proposal

## Slide 8: Enabled parallel deblocking of 8x8 blocks

## Slide 9: Conclusion
Proposal:
  Decisions for segments of 4 lines/columns
  Two lines/colums are evaluated for on/off and strong/weak decision
Results compared to HM4.0:
  Average bit rate reduction: 0.1%
  Slightly reduced run times
  20% less operations for decisions
  Elimination of decision line buffer
  Parallel deblocking of 8x8-blocks
Proposal: Inclusion into next version of the HM