## Slide 1: JCTVC-G593
Oguz Bici, Jani Lainema, Kemal Ugur
Nokia
Non-CE13: Simplification of merge mode

## Slide 2: Outline
Pruning processes in HM4.0 is complex and difficult to parallelize.
Two simplifications:
  Simplification of 1st pruning process (PART1)
    Parallelizable reduced set of comparisons
  Simplification of 2nd pruning process (PART2)
    Removes duplication check of all additional candidates
CABAC context reduction proposal
  To be discussed in CABAC session

## Slide 3: Summary Part 1
Disable the “2nd PU avoiding” except for trivial cases of A1 and B1
  No motion comparison required
Simplified 1st pruning:
  Reduced set of comparisons only within spatial candidates
  Worst-case # comparisons: 5
    Alternatively same idea can be implemented by reducing the number of full motion comparisons to 1
  Improved parallel comparison
Results: 0.1% loss on average, improved parallelism and reduced complexity
  Improved error resiliency since TMVP is not removed from the list based on comparing its motion information
B0
B1
B2
A1
A0
1st PU
2nd PU
B0
B1
B2
A1
A0
1st PU
2nd PU
B0
B1
B2
A1
A0

## Slide 4: Summary Part 2
Same List0 motion
= Cand 1
= Cand 0
= Comb Cand 0&2
During 1st pruning, the redundant combinations are known for majority of the cases
  If partial list motions are equal, guaranteed redundant combined candidates exist
Proposal:
Exploit this information and do not add the redundant combinations in the list
Do not perform any redundancy check for the additional candidates
  Reduce from 60 checks in HM4 to 0.
Results: No change in coding efficiency

## Slide 5: Part 1
HM4
  For every spatial candidate, check
  If current PU is a 2nd PU and candidate has same motion as 1st PU
    Avoid the candidate
Proposed
  Disable the “2nd PU avoiding” except for trivial cases of A1 and B1
    B1: Check if current PU is a 2nd PU of horizontal splitting (2Nxn)
    A1: Check if current PU is a 2nd PU of vertical splitting (nx2N)
  No motion comparison required
1st PU
2nd PU
B0
B1
B2
A1
A0
1st PU
2nd PU
B0
B1
B2
A1
A0
1st PU
2nd PU
B0
B1
B2
A1
A0
1st PU
2nd PU
B0
B1
B2
A1
A0

## Slide 6: Part 1
HM4
  Insert available spatial candidates and TMVP into the merge list
  Remove redundant candidates by comparing each pair
Proposed
  TMVP exempted from redundancy check (always in merge list)
  Decisions for spatial candidates
  Parallelizable, reduced set of comparisons within spatial candidates
  Simplified comparison operations
  Only one full comparison (A1 and B1 )
  NSameMotLeft(Above): Number of consecutive 4x4 blocks with same motion to Left(Above)
  2 x 5 bits variables defined for 4x4 blocks
B0
B1
B2
A1
A0
NSameMotLeft(B0) > 0
NSameMotLeft(B1) > WidthBlocks - 1
NSameMotAbove(A0) > 0
NSameMotAbove(A1) > HeightBlocks - 1
Direct motion comparison

## Slide 7: Part 1
After decoding motion information of each PU, update
  NSameMotLeft for the bottom-most blocks
  NSameMotAbove for the right-most blocks
During the update, continue the same motion information of the neighbor if
    NSameMotLeft: Merged left or Merged above and A1 has same motion as B1
    NSameMotAbove: Merged above or Merged left and A1 has same motion as B1
  Otherwise, update within PU
4
A1
5
0
6
1
7
2
8
3
NSameMotLeft available
Current PU
Merged A1
or merged B1 and A1==B1
B1
NSameMotLeft values to be updated
6
B1
7
0
8
1
9
2
10
3
NSameMotAbove values to be updated
NSameMotAbove available
Current PU
Merged B1
or merged A1 and A1==B1
A1

## Slide 8: Part 1
Compression efficiency results
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | -0.1% | 0.0% | 0.0% | 0.1% | 0.0%
Class B | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1%
Class C | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
Class D | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E |  |  |  |  |  | 
Overall | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 103% |  |  | 100% |  | 
Dec Time[%] | 95% |  |  | 99% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.1% | 0.0% | 0.1% | 0.1% | 0.2% | 0.3%
Class C | 0.1% | -0.1% | 0.1% | 0.1% | 0.1% | 0.0%
Class D | 0.1% | 0.2% | 0.3% | 0.1% | 0.2% | -0.3%
Class E | 0.2% | 0.7% | 1.0% | 0.2% | 0.7% | 0.3%
Overall | 0.1% | 0.1% | 0.3% | 0.1% | 0.3% | 0.1%
 | 0.1% | 0.1% | 0.3% | 0.1% | 0.2% | 0.0%
Enc Time[%] | 96% |  |  | 102% |  | 
Dec Time[%] | 96% |  |  | 95% |  | 

## Slide 9: Part 1
Limited effect on compression efficiency
Number of motion comparisons to obtain the initial MVP list reduced to 1 from 10 in the worst case.
  Some of the comparisons removed or replaced by simpler operations.
Suitable for parallel processing,
Memory bandwidth reduction since motion and reference index information of some candidates (A0, B0, B2) not required.
Possibility for a decoder to exit merge process as soon as the candidate corresponding to the decoded merge index is generated.
Improved error resiliency since TMVP is not removed from the list based on comparing its motion information.
  Uncertainity for the location of subsequent candidates avoided in case of frame losses

## Slide 10: Part 2
HM4
  If number of candidates after the 1st pruning < 5
  Create additional candidates
    Combined, non-scaled, zero
  Check redundancy of each additional candidate with previously inserted candidates
Proposed
  Derive redundancy of the combined candidates during 1st pruning
    If partial list motions are equal, guaranteed redundant combined candidates exist
  Remove duplication check of all additional candidates
Same List0 motion
= Cand 1
= Cand 0
= Comb Cand 0&2

## Slide 11: Part 2
 | Reference Picture list0 |  | Reference Picture list1 | 
CandIdx | MV | RefIdx | MV | RefIdx
0 | MV0List0 | RefIdx0List0 | MV0List1 | RefIdx0List1
1 | MV1List0 | RefIdx1List0 | MV1List1 | RefIdx1List1
2 | MV2List0 | RefIdx2List0 | MV2List1 | RefIdx2List1
3 | MV3List0 | RefIdx3List0 | MV3List1 | RefIdx3List1
Example initial MVP list
Initialized CombCandMap
CandIdx | 0 | 1 | 2 | 3
0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1
2 | 1 | 1 | 0 | 1
3 | 1 | 1 | 1 | 0
CandIdx | 0 | 1 | 2 | 3
0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0
2 | 1 | 1 | 0 | 1
3 | 1 | 1 | 1 | 0
If MV0List0 is equal to MV1List0 and RefIdx0List0 is equal to RefIdx1List0
CandIdx | 0 | 1 | 2 | 3
0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1
2 | 1 | 0 | 0 | 1
3 | 1 | 0 | 1 | 0
If MV0List1 is equal to MV1List1 and RefIdx0List1 is equal to RefIdx1List1
During the 1st pruning, generate an availability map (CombCandMap) for combined candidates
For redundancy check of the combined candidates, use the map rather than motion comparison

## Slide 12: Part 2
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.2% | -0.1% | 0.0% | 0.2% | 0.0%
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class E |  |  |  |  |  | 
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
Enc Time[%] | N/A |  |  | N/A |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | -0.2% | -0.1% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | -0.1% | -0.1% | 0.0% | 0.1% | -0.1%
Class D | 0.0% | 0.1% | 0.1% | 0.0% | 0.6% | 0.0%
Class E | 0.0% | 0.2% | 0.5% | 0.0% | 0.4% | -0.1%
Overall | 0.0% | 0.0% | 0.1% | 0.0% | 0.2% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | -0.1%
Enc Time[%] | N/A |  |  | N/A |  | 
Dec Time[%] | 101% |  |  | 100% |  | 
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | 0.0% | -0.1% | 0.0% | 0.0% | 0.1%
Class B | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1%
Class C | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0%
Class E |  |  |  |  |  | 
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1%
 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1%
Enc Time[%] | 100% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Class C | 0.0% | -0.1% | 0.0% | 0.1% | 0.2% | -0.1%
Class D | 0.0% | 0.3% | -0.1% | 0.0% | -0.1% | -0.1%
Class E | 0.1% | 0.0% | 0.8% | 0.1% | 0.4% | 0.4%
Overall | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0%
 | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 96% |  |  | 100% |  | 
Results of only modifying the combined candidates
Results of Part 2: also disabling redundancy check for the non-scaled and zero candidates

## Slide 13: Part 1 + Part 2 combined
 | Random Access HE |  |  | Random Access LC |  | 
 | Y | U | V | Y | U | V
Class A | 0.1% | -0.1% | -0.1% | 0.1% | 0.1% | 0.0%
Class B | 0.1% | 0.1% | 0.0% | 0.1% | 0.1% | 0.1%
Class C | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.1%
Class D | 0.1% | 0.1% | 0.0% | 0.1% | 0.0% | 0.0%
Class E |  |  |  |  |  | 
Overall | 0.1% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0%
 | 0.1% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.2% | 0.1% | 0.1% | 0.2% | 0.2% | 0.2%
Class C | 0.1% | 0.1% | 0.2% | 0.1% | 0.2% | 0.0%
Class D | 0.2% | 0.4% | 0.6% | 0.2% | 0.2% | 0.2%
Class E | 0.3% | 0.7% | 1.4% | 0.6% | 1.2% | 0.9%
Overall | 0.2% | 0.3% | 0.5% | 0.2% | 0.4% | 0.3%
 | 0.2% | 0.3% | 0.5% | 0.2% | 0.4% | 0.3%
Enc Time[%] | 101% |  |  | 101% |  | 
Dec Time[%] | 97% |  |  | 98% |  | 

## Slide 14: Part 3
Context reduction for merge index coding
HM4
  One context per bin ( total 4 contexts )
Proposed
  Two contexts for bin0, by-pass remaining three bins
  One context if skip flag==1, other context if skip flag==0

## Slide 15: Part 1 + Part 2 + Part 3
 | Random Access HE |  | 
 | Y | U | V
Class A | 0.1% | -0.1% | -0.2%
Class B | 0.1% | 0.1% | 0.1%
Class C | 0.1% | 0.0% | 0.2%
Class D | 0.1% | 0.2% | 0.0%
Class E |  |  | 
Overall | 0.1% | 0.1% | 0.0%
 | 0.1% | 0.1% | 0.1%
Enc Time[%] | 102% |  | 
Dec Time[%] | 99% |  | 
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.1% | 0.0% | 0.0%
Class C | 0.1% | 0.1% | 0.0%
Class D | 0.1% | 0.6% | -0.2%
Class E | 0.3% | 0.8% | 1.4%
Overall | 0.1% | 0.3% | 0.2%
 | 0.1% | 0.3% | 0.2%
Enc Time[%] | 101% |  | 
Dec Time[%] | 97% |  |