## Slide 1: JCTVC-G593
Oguz Bici, Jani Lainema, Kemal Ugur
Nokia
Non-CE13: Simplification of merge mode
Part 3 – Context modification for merge index coding

## Slide 2: Summary
Part 3 of JCTVC-G593: Modification of contexts for merge index coding with CABAC
bin0 bin1 bin2 bin3
Ctx0 Ctx1 Ctx2 Ctx3
HM4:
4 contexts
1 context per bin
bin0 bin1 bin2 bin3
Equal probability
Proposed:
2 contexts, both assigned for bin0
Rest: equal probability
Ctx0: skip flag==1
Ctx1: skip flag==0
Ctx0
Ctx1

## Slide 3: Results
 | Random Access HE |  | 
 | Y | U | V
Class A | 0.0% | -0.1% | -0.2%
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.0%
Class D | 0.0% | 0.1% | 0.0%
Class E |  |  | 
Overall | 0.0% | 0.0% | -0.1%
 | 0.0% | 0.0% | 0.0%
Enc Time[%] | N/A |  | 
Dec Time[%] | 99% |  | 
 | Low delay B HE |  | 
 | Y | U | V
Class A |  |  | 
Class B | 0.0% | 0.0% | 0.0%
Class C | -0.1% | 0.0% | -0.1%
Class D | 0.0% | 0.0% | 0.2%
Class E | -0.2% | -0.2% | 1.1%
Overall | -0.1% | 0.0% | 0.2%
 | -0.1% | 0.0% | 0.2%
Enc Time[%] | N/A |  | 
Dec Time[%] | 100% |  | 

## Slide 4: Conclusion
Number of contexts reduced to 2 from 4
Improvement in compression efficiency
3 out of 4 bins coded now with by-pass
Recommend for adoption