## Slide 1: Unified Deblocking and SAO JCTVC-G608 Andrew Segall and Jie Zhao
l
Notes: <number>

## Slide 2: Overview
We propose to modify SAO classification process
Our benefits and goals
  Unify SAO and deblocking
  Enable addition of SAO offset as soon as pixel is deblocked
  Combine SAO and parallel deblocking process.
Rest of the presentation
  Illustrate the problem first, then present our proposed method and result.

## Slide 3: Problem
In current HEVC design, SAO and deblocking are sequential operations at the decoder
  Deblocking filter in HM4.0 applies deblocking filter on 8x8 or larger block boundaries.
  Deblocking along horizontal boundaries can be done in parallel
  Deblocking along vertical boundaries can be done in parallel
  SAO then performed
The major reason for the serial processing
  Classification for EO types requires output from neighboring columns

## Slide 4: Proposed Method
Our proposal
  Use horizontal deblocked pixels in SAO classification in EO type
Benefit:
  Remove the dependency of SAO category classification on full deblocked pixels
  SAO offset calculated at the same time as vertical deblocking operation. Thus, SAO offset can be added during vertical deblocking operation.
  Merge SAO process and deblocking process. This includes maintaining parallel deblocking design.

## Slide 5: Proposed Method
Below shows the flowcharts of existing method in HM4.0 and proposed method.
Existing deblocking and SAO flowchart in HM4.0
Proposed deblocking and SAO flowchart in HM4.0
Note: Suitable for picture based processing, LCU based processing and combination with line buffer reduction techniques.

## Slide 6: Result
Use Horizontal Deblocked Pixels in EO type SAO classification
Common test Configurations
Average Impact on BD rate
  Intra (HE & LC): 0.1%, 0.1%
  Random access (HE&LC): 0.1%, 0.1
  Low delay B (HE&LC): 0.0%, 0.1%

## Slide 7: Conclusions
Conclusions
  We presented a technique to unify SAO and deblocking
  Enable adding SAO offset immediately after a pixel is deblocked
  Merge SAO into Parallel deblocking
  Impact on average BD rate
    Intra (both HE and LC): 0.1, 0.1%
    Random access (both HE and LC): 0.1, 0.1%
    Low delay B (both HE and LC): 0.0, 0.1%
  Method verified by Panasonic
  Propose to adopt this technique to HM.